## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Why is it not legal to transmit a 3 kHz bandwidth USB signal with a carrier frequency of 14.348 MHz?
A. USB is not used on 20-meter phone
B. The lower 1 kHz of the signal is outside the 20-meter band
C. 14.348 MHz is outside the 20-meter band
D. The upper 1 kHz of the signal is outside the 20-meter band
E1A01 [97.305, 97.307(b)]

## Slide 4: Why is it not legal to transmit a 3 kHz bandwidth USB signal with a carrier frequency of 14.348 MHz?
A. USB is not used on 20-meter phone
B. The lower 1 kHz of the signal is outside the 20-meter band
C. 14.348 MHz is outside the 20-meter band
D. The upper 1 kHz of the signal is outside the 20-meter band
E1A01 (D) [97.305, 97.307(b)]

## Slide 5: When using a transceiver that displays the carrier frequency of phone signals, which of the following displayed frequencies represents the lowest frequency at which a properly adjusted LSB emission will be totally within the band?
A. The exact lower band edge
B. 300 Hz above the lower band edge
C. 1 kHz above the lower band edge
D. 3 kHz above the lower band edge
FCC Rule: [97.301, 97.305] E1A02 ECLM Page (3 - 4)

## Slide 6: When using a transceiver that displays the carrier frequency of phone signals, which of the following displayed frequencies represents the lowest frequency at which a properly adjusted LSB emission will be totally within the band?
A. The exact lower band edge
B. 300 Hz above the lower band edge
C. 1 kHz above the lower band edge
D. 3 kHz above the lower band edge
(D) FCC Rule: [97.301, 97.305] E1A02 ECLM Page (3 - 4)

## Slide 7: What is the highest legal carrier frequency on the 20-meter band for transmitting a 2.8 kHz wide USB data signal?
A. 14.0708 MHz
B. 14.1002 MHz
C. 14.1472 MHz
D. 14.3490 MHz
E1A03 [97.305, 97.307(b)]

## Slide 8: What is the highest legal carrier frequency on the 20-meter band for transmitting a 2.8 kHz wide USB data signal?
A. 14.0708 MHz
B. 14.1002 MHz
C. 14.1472 MHz
D. 14.3490 MHz
E1A03 (C) [97.305, 97.307(b)]

## Slide 9: May an Extra class operator answer the CQ of a station on 3.601 MHz LSB phone?
A. Yes, the entire signal will be inside the SSB allocation for Extra class operators
B. Yes, the displayed frequency is within the 75-meter phone band segment
C. No, the sideband components will extend beyond the edge of the phone band segment
D. No, US stations are not permitted to use phone emissions below 3.610 MHz
E1A04 [97.301, 97.305]

## Slide 10: May an Extra class operator answer the CQ of a station on 3.601 MHz LSB phone?
A. Yes, the entire signal will be inside the SSB allocation for Extra class operators
B. Yes, the displayed frequency is within the 75-meter phone band segment
C. No, the sideband components will extend beyond the edge of the phone band segment
D. No, US stations are not permitted to use phone emissions below 3.610 MHz
E1A04 (C) [97.301, 97.305]

## Slide 11: Who must be in physical control of the station apparatus of an amateur station aboard any vessel or craft that is documented or registered in the United States?
A. Only a person with an FCC Marine Radio license grant
B. Only a person named in an amateur station license grant
C. Any person holding an FCC issued amateur license or who is authorized for alien reciprocal operation
D. Any person named in an amateur station license grant or a person holding an unrestricted Radiotelephone Operator Permit
E1A05 [97.5]

## Slide 12: Who must be in physical control of the station apparatus of an amateur station aboard any vessel or craft that is documented or registered in the United States?
A. Only a person with an FCC Marine Radio license grant
B. Only a person named in an amateur station license grant
C. Any person holding an FCC issued amateur license or who is authorized for alien reciprocal operation
D. Any person named in an amateur station license grant or a person holding an unrestricted Radiotelephone Operator Permit
E1A05 (C) [97.5]

## Slide 13: What is the required transmit frequency of a CW signal for channelized 60 meter operation? A. At the lowest frequency of the channel B. At the center frequency of the channel C. At the highest frequency of the channel D. On any frequency where the signal’s sidebands are within the channel E1A06 [97.303(h)(1)]

## Slide 14: What is the required transmit frequency of a CW signal for channelized 60 meter operation? A. At the lowest frequency of the channel B. At the center frequency of the channel C. At the highest frequency of the channel D. On any frequency where the signal’s sidebands are within the channel E1A06 (B) [97.303(h)(1)]

## Slide 15: What is the maximum power permitted on the 2200 meter band?
A. 50 watts PEP
B. 100 watts PEP
C. 1 watt EIRP (Equivalent isotropic radiated power)
D. 5 watts EIRP (Equivalent isotropic radiated power)
FCC Rule: [97.313(k)] E1A07 ECLM Page (3 - 5)

## Slide 16: What is the maximum power permitted on the 2200 meter band?
A. 50 watts PEP
B. 100 watts PEP
C. 1 watt EIRP (Equivalent isotropic radiated power)
D. 5 watts EIRP (Equivalent isotropic radiated power)
(C) FCC Rule: [97.313(k)] E1A07 ECLM Page (3 - 5)

## Slide 17: If a station in a message forwarding system inadvertently forwards a message that is in violation of FCC rules, who is primarily accountable for the rules violation?
A. The control operator of the packet bulletin board station
B. The control operator of the originating station
C. The control operators of all the stations in the system
D. The control operators of all the stations in the system not authenticating the source from which they accept communications
FCC Rule: [97.219] E1A08 ECLM Page (3 - 5)

## Slide 18: If a station in a message forwarding system inadvertently forwards a message that is in violation of FCC rules, who is primarily accountable for the rules violation?
A. The control operator of the packet bulletin board station
B. The control operator of the originating station
C. The control operators of all the stations in the system
D. The control operators of all the stations in the system not authenticating the source from which they accept communications
(B) FCC Rule: [97.219] E1A08 ECLM Page (3 - 5)

## Slide 19: Except in some parts of Alaska, what is the maximum power permitted on the 630-meter band?
A. 50 watts PEP (peak envelope power)
B. 100 watts PEP (peak envelope power)
C. 1 watt EIRP (equivalent isotropic radiated power)
D. 5 watts EIRP (equivalent isotropic radiated power)
E1A09 [97.313(l)]

## Slide 20: Except in some parts of Alaska, what is the maximum power permitted on the 630-meter band?
A. 50 watts PEP (peak envelope power)
B. 100 watts PEP (peak envelope power)
C. 1 watt EIRP (equivalent isotropic radiated power)
D. 5 watts EIRP (equivalent isotropic radiated power)
E1A09 (D) [97.313(l)]

## Slide 21: If an amateur station is installed aboard a ship or aircraft, what condition must be met before the station is operated?
A. Its operation must be approved by the master of the ship or the pilot in command of the aircraft
B. The amateur station operator must agree not to transmit when the main radio of the ship or aircraft is in use
C. The amateur station must have a power supply that is completely independent of the main ship or aircraft power supply
D. The amateur station must operate only in specific segments of the amateur service HF and VHF bands
E1A10 [97.11]

## Slide 22: If an amateur station is installed aboard a ship or aircraft, what condition must be met before the station is operated?
A. Its operation must be approved by the master of the ship or the pilot in command of the aircraft
B. The amateur station operator must agree not to transmit when the main radio of the ship or aircraft is in use
C. The amateur station must have a power supply that is completely independent of the main ship or aircraft power supply
D. The amateur station must operate only in specific segments of the amateur service HF and VHF bands
E1A10 (A) [97.11]

## Slide 23: What licensing is required when operating an amateur station aboard a US-registered vessel in international waters?
A. Any amateur license with an FCC Marine or Aircraft endorsement
B. Any FCC-issued amateur license
C. Only General class or higher amateur licenses
D. An unrestricted Radiotelephone Operator Permit
E1A11 [97.5]

## Slide 24: What licensing is required when operating an amateur station aboard a US-registered vessel in international waters?
A. Any amateur license with an FCC Marine or Aircraft endorsement
B. Any FCC-issued amateur license
C. Only General class or higher amateur licenses
D. An unrestricted Radiotelephone Operator Permit
E1A11 (B) [97.5]

## Slide 25: Which of the following constitutes a spurious emission?
A. An amateur station transmission made without the proper call sign identification
B. A signal transmitted to prevent its detection by any station other than the intended recipient
C. Any transmitted signal that unintentionally interferes with another licensed radio station
D. An emission outside the signal's necessary bandwidth that can be reduced or eliminated without affecting the information transmitted
FCC Rule: [97.3] E1B01 ECLM Page (3 - 7)

## Slide 26: Which of the following constitutes a spurious emission?
A. An amateur station transmission made without the proper call sign identification
B. A signal transmitted to prevent its detection by any station other than the intended recipient
C. Any transmitted signal that unintentionally interferes with another licensed radio station
D. An emission outside the signal's necessary bandwidth that can be reduced or eliminated without affecting the information transmitted
(D) FCC Rule: [97.3] E1B01 ECLM Page (3 - 7)

## Slide 27: Which of the following is an acceptable bandwidth for digital voice or slow-scan TV transmissions made on the HF amateur bands?
A. 3 kHz
B. 10 kHz
C. 15 kHz
D. 20 kHz
FCC Rule: [97.302(f)(2)] E1B02 ECLM Page (8 - 23)

## Slide 28: Which of the following is an acceptable bandwidth for digital voice or slow-scan TV transmissions made on the HF amateur bands?
A. 3 kHz
B. 10 kHz
C. 15 kHz
D. 20 kHz
(A) FCC Rule: [97.302(f)(2)] E1B02 ECLM Page (8 - 23)

## Slide 29: Within what distance must an amateur station protect an FCC monitoring facility from harmful interference?
A. 1 mile
B. 3 miles
C. 10 miles
D. 30 miles
FCC Rule: [97.13] E1B03 ECLM Page (3 - 8)

## Slide 30: Within what distance must an amateur station protect an FCC monitoring facility from harmful interference?
A. 1 mile
B. 3 miles
C. 10 miles
D. 30 miles
(A) FCC Rule: [97.13] E1B03 ECLM Page (3 - 8)

## Slide 31: What must be done before placing an amateur station within an officially designated wilderness area or wildlife preserve, or an area listed in the National Register of Historic Places?
A. A proposal must be submitted to the National Park Service
B. A letter of intent must be filed with the Environmental Protection Agency
C. An Environmental Assessment must be submitted to the FCC
D. A form FSD-15 must be submitted to the Department of the Interior
FCC Rule: [97.13, 1.1305-1.1319] E1B04 ECLM Page (3 - 8)

## Slide 32: What must be done before placing an amateur station within an officially designated wilderness area or wildlife preserve, or an area listed in the National Register of Historic Places?
A. A proposal must be submitted to the National Park Service
B. A letter of intent must be filed with the Environmental Protection Agency
C. An Environmental Assessment must be submitted to the FCC
D. A form FSD-15 must be submitted to the Department of the Interior
(C) FCC Rule: [97.13, 1.1305-1.1319] E1B04 ECLM Page (3 - 8)

## Slide 33: What is the National Radio Quiet Zone?
A. An area in Puerto Rico surrounding the Arecibo Radio Telescope
B. An area in New Mexico surrounding the White Sands Test Area
C. An area surrounding the National Radio Astronomy Observatory
D. An area in Florida surrounding Cape Canaveral
FCC Rule: [97.3] E1B05 ECLM Page (3 - 20)

## Slide 34: What is the National Radio Quiet Zone?
A. An area in Puerto Rico surrounding the Arecibo Radio Telescope
B. An area in New Mexico surrounding the White Sands Test Area
C. An area surrounding the National Radio Astronomy Observatory
D. An area in Florida surrounding Cape Canaveral
(C) FCC Rule: [97.3] E1B05 ECLM Page (3 - 20)

## Slide 35: Which of the following additional rules apply if you are installing an amateur station antenna at a site at or near a public use airport?
A. You may have to notify the Federal Aviation Administration and register it with the FCC as required by Part 17 of the FCC rules
B. You must submit engineering drawings to the FAA
C. You must file an Environmental Impact Statement with the EPA before construction begins
D. You must obtain a construction permit from the airport zoning authority
FCC Rule: [97.15] E1B06 ECLM Page (3 - 9)

## Slide 36: Which of the following additional rules apply if you are installing an amateur station antenna at a site at or near a public use airport?
A. You may have to notify the Federal Aviation Administration and register it with the FCC as required by Part 17 of the FCC rules
B. You must submit engineering drawings to the FAA
C. You must file an Environmental Impact Statement with the EPA before construction begins
D. You must obtain a construction permit from the airport zoning authority
(A) FCC Rule: [97.15] E1B06 ECLM Page (3 - 9)

## Slide 37: To what type of regulations does PRB-1 apply?
A. Homeowners associations
B. FAA tower height limits
C. State and local zoning
D. Use of wireless devices in vehicles
FCC Rule: [97.15] E1B07 ECLM Page (3 - 8)

## Slide 38: To what type of regulations does PRB-1 apply?
A. Homeowners associations
B. FAA tower height limits
C. State and local zoning
D. Use of wireless devices in vehicles
(C) FCC Rule: [97.15] E1B07 ECLM Page (3 - 8)

## Slide 39: What limitations may the FCC place on an amateur station if its signal causes interference to domestic broadcast reception, assuming that the receivers involved are of good engineering design?
A. The amateur station must cease operation
B. The amateur station must cease operation on all frequencies below 30 MHz
C. The amateur station must cease operation on all frequencies above 30 MHz
D. The amateur station must avoid transmitting during certain hours on frequencies that cause the interference
FCC Rule: [97.121] E1B08 ECLM Page (3 - 7)

## Slide 40: What limitations may the FCC place on an amateur station if its signal causes interference to domestic broadcast reception, assuming that the receivers involved are of good engineering design?
A. The amateur station must cease operation
B. The amateur station must cease operation on all frequencies below 30 MHz
C. The amateur station must cease operation on all frequencies above 30 MHz
D. The amateur station must avoid transmitting during certain hours on frequencies that cause the interference
(D) FCC Rule: [97.121] E1B08 ECLM Page (3 - 7)

## Slide 41: Which amateur stations may be operated under RACES rules?
A. Only those club stations licensed to Amateur Extra Class operators
B. Any FCC-licensed amateur station except a Technician Class
C. Any FCC-licensed amateur station certified by the responsible civil defense organization for the area served
D. Any FCC-licensed amateur station participating in the Military Auxiliary Radio System (MARS)
FCC Rule: [97.407] E1B09 ECLM Page (3 - 6)

## Slide 42: Which amateur stations may be operated under RACES rules?
A. Only those club stations licensed to Amateur Extra Class operators
B. Any FCC-licensed amateur station except a Technician Class
C. Any FCC-licensed amateur station certified by the responsible civil defense organization for the area served
D. Any FCC-licensed amateur station participating in the Military Auxiliary Radio System (MARS)
(C) FCC Rule: [97.407] E1B09 ECLM Page (3 - 6)

## Slide 43: What frequencies are authorized to an amateur station operating under RACES rules?
A. All amateur service frequencies authorized to the control operator
B. Specific segments in the amateur service MF, HF, VHF and UHF bands
C. Specific local government channels
D. Military Auxiliary Radio System (MARS) channels
FCC Rule: [97.407] E1B10 ECLM Page (3 - 6)

## Slide 44: What frequencies are authorized to an amateur station operating under RACES rules?
A. All amateur service frequencies authorized to the control operator
B. Specific segments in the amateur service MF, HF, VHF and UHF bands
C. Specific local government channels
D. Military Auxiliary Radio System (MARS) channels
(A) FCC Rule: [97.407] E1B10 ECLM Page (3 - 6)

## Slide 45: What does PRB-1 require of state and local regulations affecting amateur radio antenna size and structures?
A. No limitations may be placed on antenna size or placement
B. Reasonable accommodations of amateur radio must be made
C. Such structures must be permitted when use for emergency communications can be demonstrated
D. Such structures must be permitted if certified by a registered professional engineer
E1B11 [97.15]

## Slide 46: What does PRB-1 require of state and local regulations affecting amateur radio antenna size and structures?
A. No limitations may be placed on antenna size or placement
B. Reasonable accommodations of amateur radio must be made
C. Such structures must be permitted when use for emergency communications can be demonstrated
D. Such structures must be permitted if certified by a registered professional engineer
E1B11 (B) [97.15]

## Slide 47: What is the maximum bandwidth for a data emission on 60 meters?
A. 60 Hz
B. 170 Hz
C. 1.5 kHz
D. 2.8 kHz
FCC Rule: [97.303] E1C01 ECLM Page (3 - 4)

## Slide 48: What is the maximum bandwidth for a data emission on 60 meters?
A. 60 Hz
B. 170 Hz
C. 1.5 kHz
D. 2.8 kHz
(D) FCC Rule: [97.303] E1C01 ECLM Page (3 - 4)

## Slide 49: Which of the following apply to communications transmitted to amateur stations in foreign countries?
A. Third party traffic must be limited to that intended for the exclusive use of government and non-Government Organization (NGOs) involved in emergency relief activities
B. All transmissions must be in English
C. Communications must be limited to those incidental to the purpose of the amateur service and remarks of a personal nature
D. All these choices are correct
E1C02 [97.117]

## Slide 50: Which of the following apply to communications transmitted to amateur stations in foreign countries?
A. Third party traffic must be limited to that intended for the exclusive use of government and non-Government Organization (NGOs) involved in emergency relief activities
B. All transmissions must be in English
C. Communications must be limited to those incidental to the purpose of the amateur service and remarks of a personal nature
D. All these choices are correct
E1C02 (C) [97.117]

## Slide 51: How long must an operator wait after filing a notification with the Utilities Technology Council (UTC) before operating on the 2200-meter or 630-meter band?
A. Operators must not operate until approval is received
B. Operators may operate after 30 days, providing they have not been told that their station is within 1 kilometer of PLC systems using those frequencies
C. Operators may not operate until a test signal has been transmitted in coordination with the local power company
D. Operations may commence immediately, and may continue unless interference is reported by the UTC
E1C03 [97.303(g)]

## Slide 52: How long must an operator wait after filing a notification with the Utilities Technology Council (UTC) before operating on the 2200-meter or 630-meter band?
A. Operators must not operate until approval is received
B. Operators may operate after 30 days, providing they have not been told that their station is within 1 kilometer of PLC systems using those frequencies
C. Operators may not operate until a test signal has been transmitted in coordination with the local power company
D. Operations may commence immediately, and may continue unless interference is reported by the UTC
E1C03 (B) [97.303(g)]

## Slide 53: What is meant by IARP?
A. An international amateur radio permit that allows U.S. amateurs to operate in certain countries of the Americas
B. The internal amateur radio practices policy of the FCC
C. An indication of increased antenna reflected power.
D. A forecast of intermittent aurora radio propagation
E1C04 ECLM Page (3 - 21)

## Slide 54: What is meant by IARP?
A. An international amateur radio permit that allows U.S. amateurs to operate in certain countries of the Americas
B. The internal amateur radio practices policy of the FCC
C. An indication of increased antenna reflected power.
D. A forecast of intermittent aurora radio propagation
(A) E1C04 ECLM Page (3 - 21)

## Slide 55: Under what situation may a station transmit third party communications while being automatically controlled?
A. Never
B. Only when transmitting RTTY or data emissions
C. Only when transmitting SSB or CW
D. On any mode approved by the National Telecommunication and Information Administration
E1C05 [97.221(c)(1), 97.115()]

## Slide 56: Under what situation may a station transmit third party communications while being automatically controlled?
A. Never
B. Only when transmitting RTTY or data emissions
C. Only when transmitting SSB or CW
D. On any mode approved by the National Telecommunication and Information Administration
E1C05 (B) [97.221(c)(1), 97.115()]

## Slide 57: Which of the following is required in order to operate in accordance with CEPT rules in foreign countries where permitted?
A. You must identify in the official language of the country in which you are operating
B. The U.S. embassy must approve of your operation
C. You must bring a copy of FCC Public Notice DA 16-1048
D. You must append "/CEPT" to your call sign
E1C06 ECLM Page (3 - 21)

## Slide 58: Which of the following is required in order to operate in accordance with CEPT rules in foreign countries where permitted?
A. You must identify in the official language of the country in which you are operating
B. The U.S. embassy must approve of your operation
C. You must bring a copy of FCC Public Notice DA 16-1048
D. You must append "/CEPT" to your call sign
(C) E1C06 ECLM Page (3 - 21)

## Slide 59: What notifications must be given before transmitting on the 630- or 2200-meter bands?
A. A special endorsement must be requested from the FCC
B. An environmental impact statement must be filed with the Department of the Interior
C. Operators must inform the FAA of their intent to operate, giving their call sign and distance to the nearest runway
D. Operators must inform the Utilities Technology Council (UTC) of their call sign and coordinates of the station
E1C07 [97.303(g)]

## Slide 60: What notifications must be given before transmitting on the 630- or 2200-meter bands?
A. A special endorsement must be requested from the FCC
B. An environmental impact statement must be filed with the Department of the Interior
C. Operators must inform the FAA of their intent to operate, giving their call sign and distance to the nearest runway
D. Operators must inform the Utilities Technology Council (UTC) of their call sign and coordinates of the station
E1C07 (D) [97.303(g)]

## Slide 61: What is the maximum permissible duration of a remotely controlled station’s transmissions if its control link malfunctions?
A. 30 seconds
B. 3 minutes
C. 5 minutes
D. 10 minutes
FCC Rule: [97.213] E1C08 ECLM Page (3 - 10)

## Slide 62: What is the maximum permissible duration of a remotely controlled station’s transmissions if its control link malfunctions?
A. 30 seconds
B. 3 minutes
C. 5 minutes
D. 10 minutes
(B) FCC Rule: [97.213] E1C08 ECLM Page (3 - 10)

## Slide 63: What is the highest modulation index permitted at the highest modulation frequency for angle modulation below 29.0 MHz?
A. 0.5
B. 1.0
C. 2.0
D. 3.0
FCC Rule: [97.307] E1C09 ECLM Page (8 - 4)

## Slide 64: What is the highest modulation index permitted at the highest modulation frequency for angle modulation below 29.0 MHz?
A. 0.5
B. 1.0
C. 2.0
D. 3.0
(B) FCC Rule: [97.307] E1C09 ECLM Page (8 - 4)

## Slide 65: What is the maximum mean power level for a spurious emission below 30 MHz with respect to the fundamental emission?
A. - 43 dB
B. - 53 dB
C. - 63 dB
D. - 73 dB
E1C10 [97.307]

## Slide 66: What is the maximum mean power level for a spurious emission below 30 MHz with respect to the fundamental emission?
A. - 43 dB
B. - 53 dB
C. - 63 dB
D. - 73 dB
E1C10 (A) [97.307]

## Slide 67: Which of the following operating arrangements allows an FCC-licensed U.S. citizen to operate in many European countries, and alien amateurs from many European countries to operate in the U.S.?
A. CEPT agreement
B. IARP agreement
C. ITU reciprocal license
D. All these choices are correct
FCC Rule: [97.5] E1C11 ECLM Page (3 - 21)

## Slide 68: Which of the following operating arrangements allows an FCC-licensed U.S. citizen to operate in many European countries, and alien amateurs from many European countries to operate in the U.S.?
A. CEPT agreement
B. IARP agreement
C. ITU reciprocal license
D. All these choices are correct
(A) FCC Rule: [97.5] E1C11 ECLM Page (3 - 21)

## Slide 69: In what portion of the 630-meter band are phone emissions permitted?
A. None
B. Only the top 3 kHz
C. Only the bottom 3 kHz
D. The entire band
FCC Rule: [97.305(c)] E1C12 ECLM Page (3 - 5)

## Slide 70: In what portion of the 630-meter band are phone emissions permitted?
A. None
B. Only the top 3 kHz
C. Only the bottom 3 kHz
D. The entire band
(D) FCC Rule: [97.305(c)] E1C12 ECLM Page (3 - 5)