## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Which of the following digital modes is designed for meteor scatter communications?
A. WSPR
B. MSK144
C. Hellschreiber
D. APRS
E2D01 ECLM Page (10 - 16)

## Slide 4: Which of the following digital modes is designed for meteor scatter communications?
A. WSPR
B. MSK144
C. Hellschreiber
D. APRS
(B) E2D01 ECLM Page (10 - 16)

## Slide 5: What information replaces signal-to-noise ratio when using the FT8 or FT4 modes in a VHF contest?
A. RST report
B. State abbreviation
C. Serial number
D. Grid square
E2D02 ECLM Page (10 - 16)

## Slide 6: What information replaces signal-to-noise ratio when using the FT8 or FT4 modes in a VHF contest?
A. RST report
B. State abbreviation
C. Serial number
D. Grid square
(D) E2D02 ECLM Page (10 - 16)

## Slide 7: Which of the following digital modes is designed for EME communications?
A. MSK144
B. PACTOR III
C. WSPR
D. Q65
E2D03 ECLM Page (10 - 17)

## Slide 8: Which of the following digital modes is designed for EME communications?
A. MSK144
B. PACTOR III
C. WSPR
D. Q65
(D) E2D03 ECLM Page (10 - 17)

## Slide 9: What technology is used to track, in real time, balloons carrying amateur radio transmitters?
A. FT8
B. Bandwidth compressed LORAN
C. APRS
D. PACTOR III
E2D04 ECLM Page (8 - 12)

## Slide 10: What technology is used to track, in real time, balloons carrying amateur radio transmitters?
A. FT8
B. Bandwidth compressed LORAN
C. APRS
D. PACTOR III
(C) E2D04 ECLM Page (8 - 12)

## Slide 11: What is the characteristic of the JT65 mode?
A. Uses only a 65 Hz bandwidth
B. Decodes signals with a very low signal-to-noise ratio
C. Symbol rate is 65 baud
D. Permits fast-scan TV transmissions over narrow bandwidth
E2D05 ECLM Page (10 - 17)

## Slide 12: What is the characteristic of the JT65 mode?
A. Uses only a 65 Hz bandwidth
B. Decodes signals with a very low signal-to-noise ratio
C. Symbol rate is 65 baud
D. Permits fast-scan TV transmissions over narrow bandwidth
(B) E2D05 ECLM Page (10 - 17)

## Slide 13: Which of the following is a method for establishing EME contacts?
A. Time synchronous transmissions alternately from each station
B. Storing and forwarding digital messages
C. Judging optimum transmission times by monitoring beacons reflected from the moon
D. High speed CW identification to avoid fading
E2D06 ECLM Page (10 - 17)

## Slide 14: Which of the following is a method for establishing EME contacts?
A. Time synchronous transmissions alternately from each station
B. Storing and forwarding digital messages
C. Judging optimum transmission times by monitoring beacons reflected from the moon
D. High speed CW identification to avoid fading
(A) E2D06 ECLM Page (10 - 17)

## Slide 15: What digital protocol is used by APRS?
A. PACTOR
B. 802.11
C. AX.25
D. AMTOR
E2D07 ECLM Page (8 - 11)

## Slide 16: What digital protocol is used by APRS?
A. PACTOR
B. 802.11
C. AX.25
D. AMTOR
(C) E2D07 ECLM Page (8 - 11)

## Slide 17: What type of packet frame is used to transmit APRS beacon data?
A. Unnumbered Information
B. Disconnect
C. Acknowledgement
D. Connect
E2D08 ECLM Page (8 - 12)

## Slide 18: What type of packet frame is used to transmit APRS beacon data?
A. Unnumbered Information
B. Disconnect
C. Acknowledgement
D. Connect
(A) E2D08 ECLM Page (8 - 12)

## Slide 19: What type of modulation is used for JT65 contacts?
A. Multitone AFSK
B. PSK
C. RTTY
D. QAM
E2D09 ECLM Page (8 - 13)

## Slide 20: What type of modulation is used for JT65 contacts?
A. Multitone AFSK
B. PSK
C. RTTY
D. QAM
(A) E2D09 ECLM Page (8 - 13)

## Slide 21: What does the packet path WIDE3-1 designate?
A. Three stations are allowed on frequency, one transmitting at a time
B. Three subcarriers are permitted, subcarrier one is being used
C. Three digipeater hops are requested with one remaining
D. Three internet gateway stations may receive one transmission
E2D10 ECLM Page (8 - 12)

## Slide 22: What does the packet path WIDE3-1 designate?
A. Three stations are allowed on frequency, one transmitting at a time
B. Three subcarriers are permitted, subcarrier one is being used
C. Three digipeater hops are requested with one remaining
D. Three internet gateway stations may receive one transmission
(C) E2D10 ECLM Page (8 - 12)

## Slide 23: How do APRS stations relay data?
A. By packet ACK/NAK relay
B. By C4FM repeaters
C. By DMR repeaters
D. By packet digipeaters
E2D11 ECLM Page (8 - 12)

## Slide 24: How do APRS stations relay data?
A. By packet ACK/NAK relay
B. By C4FM repeaters
C. By DMR repeaters
D. By packet digipeaters
(D) E2D11 ECLM Page (8 - 12)

## Slide 25: Which of the following types of modulation is common for data emissions below 30 MHz?
A. DTMF tones modulating an FM signal
B. FSK
C. Pulse modulation
D. Spread spectrum
E2E01 ECLM Page (8 - 10)

## Slide 26: Which of the following types of modulation is common for data emissions below 30 MHz?
A. DTMF tones modulating an FM signal
B. FSK
C. Pulse modulation
D. Spread spectrum
(B) E2E01 ECLM Page (8 - 10)

## Slide 27: Which of the following synchronizes WSJT-X digital mode transmit/receive timing?
A. Alignment of frequency shifts
B. Synchronization of computer clocks
C. Sync-field transmission
D. Sync-pulse timing
E2E02 ECLM Page (8 - 17)

## Slide 28: Which of the following synchronizes WSJT-X digital mode transmit/receive timing?
A. Alignment of frequency shifts
B. Synchronization of computer clocks
C. Sync-field transmission
D. Sync-pulse timing
(B) E2E02 ECLM Page (8 - 17)

## Slide 29: To what does the "4" in FT4 refer?
A. Multiples of 4 bits of user information
B. Four-tone continuous-phase frequency shift keying
C. Four transmit/receive cycles per minute
D. All these choices are correct
E2E03 ECLM Page (8 - 13)

## Slide 30: To what does the "4" in FT4 refer?
A. Multiples of 4 bits of user information
B. Four-tone continuous-phase frequency shift keying
C. Four transmit/receive cycles per minute
D. All these choices are correct
(B) E2E03 ECLM Page (8 - 13)

## Slide 31: Which of the following is characteristic of the FST4 mode?
A. Four-tone Gaussian frequency shift keying
B. Variable transmit/receive periods
C. Seven different tone spacings
D. All these choices are correct
E2E04 ECLM Page (8 - 10)

## Slide 32: Which of the following is characteristic of the FST4 mode?
A. Four-tone Gaussian frequency shift keying
B. Variable transmit/receive periods
C. Seven different tone spacings
D. All these choices are correct
(D) E2E04 ECLM Page (8 - 10)

## Slide 33: Which of these digital modes does not support keyboard-to-keyboard operation?
A. WSPR
B. RTTY
C. PSK31
D. MFSK16
E2E05 ECLM Page (8 - 12)

## Slide 34: Which of these digital modes does not support keyboard-to-keyboard operation?
A. WSPR
B. RTTY
C. PSK31
D. MFSK16
(A) E2E05 ECLM Page (8 - 12)

## Slide 35: What is the length of an FT8 transmission cycle?
A. It varies with the amount of data
B. 8 seconds
C. 15 seconds
D. 30 seconds
E2E06 ECLM Page (8 - 12)

## Slide 36: What is the length of an FT8 transmission cycle?
A. It varies with the amount of data
B. 8 seconds
C. 15 seconds
D. 30 seconds
(C) E2E06 ECLM Page (8 - 12)

## Slide 37: How does Q65 differ from JT65?
A. Keyboard-to keyboard operation is supported
B. Quadrature modulation is used
C. Multiple receive cycles are averaged
D. All these choices are correct
E2E07

## Slide 38: How does Q65 differ from JT65?
A. Keyboard-to keyboard operation is supported
B. Quadrature modulation is used
C. Multiple receive cycles are averaged
D. All these choices are correct
(D) E2E07

## Slide 39: Which of the following HF digital modes can be used to transfer binary files?
PSK31
PACTOR
C. RTTY
D. AMTOR
E2E08 ECLM Page (8 - 12)

## Slide 40: Which of the following HF digital modes can be used to transfer binary files?
A. PSK31
B. PACTOR
C. RTTY
D. AMTOR
(B) E2E08 ECLM Page (8 - 12)

## Slide 41: Which of the following HF digital modes uses variable-length coding for bandwidth efficiency?
A. RTTY
B. PACTOR
C. MT63
D. PSK31
E2E09 ECLM Page (8 - 7)

## Slide 42: Which of the following HF digital modes uses variable-length coding for bandwidth efficiency?
A. RTTY
B. PACTOR
C. MT63
D. PSK31
(D) E2E09 ECLM Page (8 - 7)

## Slide 43: Which of these digital modes has the narrowest bandwidth?
A. MFSK16
B. 170-Hz shift, 45-baud RTTY
C. PSK31
D. 300-baud packet
E2E10 ECLM Page (8 - 11)

## Slide 44: Which of these digital modes has the narrowest bandwidth?
A. MFSK16
B. 170-Hz shift, 45-baud RTTY
C. PSK31
D. 300-baud packet
(C) E2E10 ECLM Page (8 - 11)

## Slide 45: What is the difference between direct FSK and audio FSK?
A. Direct FSK modulates the transmitter VFO
B. Direct FSK occupies less bandwidth
C. Direct FSK can transmit higher baud rates
D. All these choices are correct
E2E11 ECLM Page (8 - 10)

## Slide 46: What is the difference between direct FSK and audio FSK?
A. Direct FSK modulates the transmitter VFO
B. Direct FSK occupies less bandwidth
C. Direct FSK can transmit higher baud rates
D. All these choices are correct
(A ) E2E11 ECLM Page (8 - 10)

## Slide 47: How do ALE stations establish contact?
A. ALE constantly scans a list of frequencies, activating the radio when the designated call sign is received
B. ALE radios monitor an internet site for the frequency they are being paged on
C. ALE radios send a constant tone code to establish a frequency for future use
D. ALE radios activate when they hear their signal echoed by back scatter
E2E12 ECLM Page (8 - 6)

## Slide 48: How do ALE stations establish contact?
A. ALE constantly scans a list of frequencies, activating the radio when the designated call sign is received
B. ALE radios monitor an internet site for the frequency they are being paged on
C. ALE radios send a constant tone code to establish a frequency for future use
D. ALE radios activate when they hear their signal echoed by back scatter
(A) E2E12 ECLM Page (8 - 6)

## Slide 49: Which of these digital modes has the highest data throughput under clear communication conditions?
A. MFSK16
B. 170 Hz shift, 45 baud RTTY
C. FT8
D. PACTOR IV
E2E13 ECLM Page (8 - 12)

## Slide 50: Which of these digital modes has the highest data throughput under clear communication conditions?
A. MFSK16
B. 170 Hz shift, 45 baud RTTY
C. FT8
D. PACTOR IV
(D) E2E13 ECLM Page (8 - 12)