## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is the approximate maximum separation measured along the surface of the Earth between two stations communicating by EME?
A. 500 miles, if the moon is at perigee
B. 2000 miles, if the moon is at apogee
C. 5000 miles, if the moon is at perigee
D. 12,000 miles, if the moon is visible by both stations
E3A01 ECLM Page (10 - 17)

## Slide 4: What is the approximate maximum separation measured along the surface of the Earth between two stations communicating by EME?
A. 500 miles, if the moon is at perigee
B. 2000 miles, if the moon is at apogee
C. 5000 miles, if the moon is at perigee
D. 12,000 miles, if the moon is visible by both stations
(D) E3A01 ECLM Page (10 - 17)

## Slide 5: What characterizes libration fading of an EME signal?
A. A slow change in the pitch of the CW signal
B. A fluttery irregular fading
C. A gradual loss of signal as the sun rises
D. The returning echo is several hertz lower in frequency than the transmitted signal
E3A02 ECLM Page (10 - 17)

## Slide 6: What characterizes libration fading of an EME signal?
A. A slow change in the pitch of the CW signal
B. A fluttery irregular fading
C. A gradual loss of signal as the sun rises
D. The returning echo is several hertz lower in frequency than the transmitted signal
(B) E3A02 ECLM Page (10 - 17)

## Slide 7: When scheduling EME contacts, which of these conditions will generally result in the least path loss?
A. When the moon is at perigee
B. When the moon is full
C. When the moon is at apogee
D. When the MUF is above 30 MHz
E3A03 ECLM Page (10 - 17)

## Slide 8: When scheduling EME contacts, which of these conditions will generally result in the least path loss?
A. When the moon is at perigee
B. When the moon is full
C. When the moon is at apogee
D. When the MUF is above 30 MHz
(A) E3A03 ECLM Page (10 - 17)

## Slide 9: In what direction does an electromagnetic wave travel?
A. It depends on the phase angle of the magnetic field
B. It travels parallel to the electric and magnetic fields
C. It depends on the phase angle of the electric field
D. It travels at a right angle to the electric and magnetic fields
E3A04 ECLM Page (10 - 12)

## Slide 10: In what direction does an electromagnetic wave travel?
A. It depends on the phase angle of the magnetic field
B. It travels parallel to the electric and magnetic fields
C. It depends on the phase angle of the electric field
D. It travels at a right angle to the electric and magnetic fields
(D) E3A04 ECLM Page (10 - 12)

## Slide 11: How are the component fields of an electromagnetic wave oriented?
A. They are parallel
B. They are tangential
C. They are at right angles
D. They are 90 degrees out of phase
E3A05 ECLM Page (10 - 12)

## Slide 12: How are the component fields of an electromagnetic wave oriented?
A. They are parallel
B. They are tangential
C. They are at right angles
D. They are 90 degrees out of phase
(C) E3A05 ECLM Page (10 - 12)

## Slide 13: What should be done to continue a long-distance contact when the MUF for that path decreases due to darkness?
A. Switch to a higher frequency HF band
B. Switch to a lower frequency HF band
C. Change to an antenna with a higher takeoff angle
D. Change to an antenna with greater beam width
E3A06 ECLM Page (10 - 7)

## Slide 14: What should be done to continue a long-distance contact when the MUF for that path decreases due to darkness?
A. Switch to a higher frequency HF band
B. Switch to a lower frequency HF band
C. Change to an antenna with a higher takeoff angle
D. Change to an antenna with greater beam width
(B) E3A06 ECLM Page (10 - 7)

## Slide 15: Atmospheric ducts capable of propagating microwave signals often form over what geographic feature?
A. Mountain ranges
B. Stratocumulus clouds
C. Large bodies of water
D. Nimbus clouds
E3A07 ECLM Page (10 - 12)

## Slide 16: Atmospheric ducts capable of propagating microwave signals often form over what geographic feature?
A. Mountain ranges
B. Stratocumulus clouds
C. Large bodies of water
D. Nimbus clouds
(C) E3A07 ECLM Page (10 - 12)

## Slide 17: When a meteor strikes the Earth’s atmosphere, a linear ionized region is formed at what region of the ionosphere?
A. The E layer
B. The F1 layer
C. The F2 layer
D. The D layer
E3A08 ECLM Page (10 - 16)

## Slide 18: When a meteor strikes the Earth’s atmosphere, a linear ionized region is formed at what region of the ionosphere?
A. The E layer
B. The F1 layer
C. The F2 layer
D. The D layer
(A) E3A08 ECLM Page (10 - 16)

## Slide 19: Which of the following frequency ranges is most suited for meteor-scatter communications?
A. 1.8 MHz - 1.9 MHz
B. 10 MHz - 14 MHz
C. 28 MHz - 148 MHz
D. 220 MHz - 450 MHz
E3A09 ECLM Page (10 - 16)

## Slide 20: Which of the following frequency ranges is most suited for meteor-scatter communications?
A. 1.8 MHz - 1.9 MHz
B. 10 MHz - 14 MHz
C. 28 MHz - 148 MHz
D. 220 MHz - 450 MHz
(C) E3A09 ECLM Page (10 - 16)

## Slide 21: What determines the speed of electromagnetic waves through a medium?
A. Resistance and reactance
B. Evanescence
C. Birefringence
D. The index of refraction
E3A10 ECLM Page (10 - 12)

## Slide 22: What determines the speed of electromagnetic waves through a medium?
A. Resistance and reactance
B. Evanescence
C. Birefringence
D. The index of refraction
(D) E3A10 ECLM Page (10 - 12)

## Slide 23: What is a typical range for tropospheric propagation of microwave signals?
A. 10 miles to 50 miles
B. 100 miles to 300 miles
C. 1200 miles
D. 2500 miles
E3A11 ECLM Page (10 - 12)

## Slide 24: What is a typical range for tropospheric propagation of microwave signals?
A. 10 miles to 50 miles
B. 100 miles to 300 miles
C. 1200 miles
D. 2500 miles
(B) E3A11 ECLM Page (10 - 12)

## Slide 25: What is most likely to result in auroral propagation?
A. Meteor showers
B. Quiet geomagnetic conditions
C. Severe geomagnetic storms
D. Extreme low-pressure areas in polar regions
E3A12 ECLM Page (10 - 14)

## Slide 26: What is most likely to result in auroral propagation?
A. Meteor showers
B. Quiet geomagnetic conditions
C. Severe geomagnetic storms
D. Extreme low-pressure areas in polar regions
(C) E3A12 ECLM Page (10 - 14)

## Slide 27: Which of these emission modes is best for auroral propagation?
A. CW
B. SSB
C. FM
D. RTTY
E3A13 ECLM Page (10 - 14)

## Slide 28: Which of these emission modes is best for auroral propagation?
A. CW
B. SSB
C. FM
D. RTTY
(A) E3A13 ECLM Page (10 - 14)

## Slide 29: What are circularly polarized electromagnetic waves?
A. Waves with an electric field bent into a circular shape
B. Waves with rotating electric and magnetic fields
C. Waves that circle Earth
D. Waves produced by a loop antenna
E3A14 ECLM Page (10 - 3)

## Slide 30: What are circularly polarized electromagnetic waves?
A. Waves with an electric field bent into a circular shape
B. Waves with rotating electric and magnetic fields
C. Waves that circle Earth
D. Waves produced by a loop antenna
(B) E3A14 ECLM Page (10 - 3)

## Slide 31: Where is transequatorial propagation (TEP) most likely to occur?
A. Between points separated by 2,000 miles to 3,000 miles over a path perpendicular to the geomagnetic equator
B. Between points located 1,500 miles to 2,000 miles apart on the geomagnetic equator
C. Between points located at each other’s antipode
D. Through the region where the terminator crosses the geographic equator
E3B01 ECLM Page (10 - 13)

## Slide 32: Where is transequatorial propagation (TEP) most likely to occur?
A. Between points separated by 2,000 miles to 3,000 miles over a path perpendicular to the geomagnetic equator
B. Between points located 1,500 miles to 2,000 miles apart on the geomagnetic equator
C. Between points located at each other’s antipode
D. Through the region where the terminator crosses the geographic equator
(A) E3B01 ECLM Page (10 - 13)

## Slide 33: What is the approximate maximum range for signals using transequatorial propagation?
A. 1000 miles
B. 2500 miles
C. 5000 miles
D. 7500 miles
E3B02 ECLM Page (10 - 14)

## Slide 34: What is the approximate maximum range for signals using transequatorial propagation?
A. 1000 miles
B. 2500 miles
C. 5000 miles
D. 7500 miles
(C) E3B02 ECLM Page (10 - 14)

## Slide 35: At what time of day is transequatorial propagation most likely to occur?
A. Morning
B. Noon
C. Afternoon or early evening
D. Late at night
E3B03 ECLM Page (10 - 14)

## Slide 36: At what time of day is transequatorial propagation most likely to occur?
A. Morning
B. Noon
C. Afternoon or early evening
D. Late at night
(C) E3B03 ECLM Page (10 - 14)

## Slide 37: What is meant by the terms "extraordinary" and "ordinary" waves?
A. Extraordinary waves exhibit rare long-skip propagation, compared to ordinary waves, which travel shorter distances
B. Independently propagating, elliptically polarized waves created in the ionosphere
C. Long-path and short-path waves
D. Refracted rays and reflected waves
E3B04 ECLM Page (10 - 7)

## Slide 38: What is meant by the terms "extraordinary" and "ordinary" waves?
A. Extraordinary waves exhibit rare long-skip propagation, compared to ordinary waves, which travel shorter distances
B. Independently propagating, elliptically polarized waves created in the ionosphere
C. Long-path and short-path waves
D. Refracted rays and reflected waves
(B) E3B04 ECLM Page (10 - 7)

## Slide 39: Which of the following paths is most likely to support long-distance propagation on 160 meters?
A. A path entirely in sunlight
B. Paths at high latitudes
C. A direct north-south path
D. A path entirely in darkness
E3B05 ECLM Page (10 - 9)

## Slide 40: Which of the following paths is most likely to support long-distance propagation on 160 meters?
A. A path entirely in sunlight
B. Paths at high latitudes
C. A direct north-south path
D. A path entirely in darkness
(D) E3B05 ECLM Page (10 - 9)

## Slide 41: On which of the following amateur bands is long-path propagation most frequent?
A. 160 meters and 80 meters
B. 40 meters and 20 meters
C. 10 meters and 6 meters
D. 6 meters and 2 meters
E3B06 ECLM Page (10 - 9)

## Slide 42: On which of the following amateur bands is long-path propagation most frequent?
A. 160 meters and 80 meters
B. 40 meters and 20 meters
C. 10 meters and 6 meters
D. 6 meters and 2 meters
(B) E3B06 ECLM Page (10 - 9)

## Slide 43: What effect does lowering a signal’s transmitted elevation angle have on ionospheric HF skip propagation?
A. Faraday rotation becomes stronger
B. The MUF decreases
C. The distance covered by each hop increases
D. The critical frequency increases
E3B07 ECLM Page (10 - 7)

## Slide 44: What effect does lowering a signal’s transmitted elevation angle have on ionospheric HF skip propagation?
A. Faraday rotation becomes stronger
B. The MUF decreases
C. The distance covered by each hop increases
D. The critical frequency increases
(C) E3B07 ECLM Page (10 - 7)

## Slide 45: How does the maximum range of ground-wave propagation change when the signal frequency is increased?
A. It stays the same
B. It increases
C. It decreases
D. It peaks at roughly 8 MHz
E3B08

## Slide 46: How does the maximum range of ground-wave propagation change when the signal frequency is increased?
A. It stays the same
B. It increases
C. It decreases
D. It peaks at roughly 8 MHz
(C) E3B08

## Slide 47: At what time of year is sporadic E propagation most likely to occur?
A. Around the solstices, especially the summer solstice
B. Around the solstices, especially the winter solstice
C. Around the equinoxes, especially the spring equinox
D. Around the equinoxes, especially the fall equinox
E3B09 ECLM Page (10 - 13)

## Slide 48: At what time of year is sporadic E propagation most likely to occur?
A. Around the solstices, especially the summer solstice
B. Around the solstices, especially the winter solstice
C. Around the equinoxes, especially the spring equinox
D. Around the equinoxes, especially the fall equinox
(A) E3B09 ECLM Page (10 - 13)

## Slide 49: What is the effect of chordal-hop propagation?
A. The signal experiences less loss compared to multi-hop using Earth as a reflector
B. The MUF for chordal hop propagation is much lower than for normal skip propagation
C. Atmospheric noise is lower in the direction of chordal hop propagation
D. Signals travel faster along ionospheric chords
E3B10 ECLM Page (10 - 6)

## Slide 50: What is the effect of chordal-hop propagation?
A. The signal experiences less loss compared to multi-hop using Earth as a reflector
B. The MUF for chordal hop propagation is much lower than for normal skip propagation
C. Atmospheric noise is lower in the direction of chordal hop propagation
D. Signals travel faster along ionospheric chords
(A) E3B10 ECLM Page (10 - 6)

## Slide 51: At what time of day is sporadic-E propagation most likely to occur?
A. Between midnight and sunrise
B. Between sunset and midnight
C. Between sunset and sunrise
D. Between sunrise and sunset
E3B11 ECLM Page (10 - 13)

## Slide 52: At what time of day can sporadic E propagation occur?
A. Between midnight and sunrise
B. Between sunset and midnight
C. Between sunset and sunrise
D. Between sunrise and sunset
(D) E3B11 ECLM Page (10 - 13)

## Slide 53: What is chordal-hop propagation?
A. Propagation away from the great circle bearing between stations
B. Successive ionospheric refractions without an intermediate reflection from the ground
C. Propagation across the geomagnetic equator
D. Signals reflected back toward the transmitting station
E3B12 ECLM Page (10 - 6)

## Slide 54: What is chordal-hop propagation?
A. Propagation away from the great circle bearing between stations
B. Successive ionospheric refractions without an intermediate reflection from the ground
C. Propagation across the geomagnetic equator
D. Signals reflected back toward the transmitting station
(B) E3B12 ECLM Page (10 - 6)

## Slide 55: What type of polarization is supported by ground-wave propagation?
A. Vertical
B. Horizontal
C. Circular
D. Elliptical
E3B13

## Slide 56: What type of polarization is supported by ground-wave propagation?
A. Vertical
B. Horizontal
C. Circular
D. Elliptical
(A) E3B13

## Slide 57: What is the cause of short-term radio blackouts?
A. Coronal mass ejections
B. Sunspots on the solar equator
C. North-oriented interplanetary magnetic field
D. Solar flares
E3C01 ECLM Page (10 - 8)

## Slide 58: What is the cause of short-term radio blackouts?
A. Coronal mass ejections
B. Sunspots on the solar equator
C. North-oriented interplanetary magnetic field
D. Solar flares
(D) E3C01 ECLM Page (10 - 8)

## Slide 59: What is indicated by a rising A or K index?
A. Increasing disturbance of the geomagnetic field
B. Decreasing disturbance of the geomagnetic field
C. Higher levels of solar UV radiation
D. An increase in the critical frequency
E3C02 ECLM Page (10 - 5)

## Slide 60: What is indicated by a rising A or K index?
A. Increasing disturbance of the geomagnetic field
B. Decreasing disturbance of the geomagnetic field
C. Higher levels of solar UV radiation
D. An increase in the critical frequency
(A) E3C02 ECLM Page (10 - 5)

## Slide 61: Which of the following signal paths is most likely to experience high levels of absorption when the A index or K index is elevated?
A. Transequatorial
B. Polar
C. Sporadic E
D. NVIS
E3C03 ECLM Page (10 - 8)

## Slide 62: Which of the following signal paths is most likely to experience high levels of absorption when the A index or K index is elevated?
A. Transequatorial
B. Polar
C. Sporadic E
D. NVIS
(B) E3C03 ECLM Page (10 - 8)

## Slide 63: What does the value of Bz (B sub Z) represent?
A. Geomagnetic field stability
B. Critical frequency for vertical transmissions
C. Direction and strength of the interplanetary magnetic field
D. Duration of long-delayed echoes
E3C04 ECLM Page (10 - 5)

## Slide 64: What does the value of Bz (B sub Z) represent?
A. Geomagnetic field stability
B. Critical frequency for vertical transmissions
C. Direction and strength of the interplanetary magnetic field
D. Duration of long-delayed echoes
(C) E3C04 ECLM Page (10 - 5)

## Slide 65: What orientation of Bz (B sub z) increases the likelihood that incoming particles from the sun will cause disturbed conditions?
A. Southward
B. Northward
C. Eastward
D. Westward
E3C05 ECLM Page (10 - 5)

## Slide 66: What orientation of Bz (B sub z) increases the likelihood that incoming particles from the sun will cause disturbed conditions?
A. Southward
B. Northward
C. Eastward
D. Westward
(A) E3C05 ECLM Page (10 - 5)

## Slide 67: How does the VHF/UHF radio horizon compare to the geographic horizon?
A. It is approximately 15 percent farther
B. It is approximately 20 percent nearer
C. It is approximately 50 percent farther
D. They are approximately the same
E3C06 ECLM Page (10 - 10)

## Slide 68: How does the VHF/UHF radio horizon compare to the geographic horizon?
A. It is approximately 15 percent farther
B. It is approximately 20 percent nearer
C. It is approximately 50 percent farther
D. They are approximately the same
(A) E3C06 ECLM Page (10 - 10)

## Slide 69: Which of the following indicates the greatest solar flare intensity?
A. Class A
B. Class Z
C. Class M
D. Class X
E3C07

## Slide 70: Which of the following indicates the greatest solar flare intensity?
A. Class A
B. Class Z
C. Class M
D. Class X
(D) E3C07

## Slide 71: Which of the following is the space-weather term for an extreme geomagnetic storm?
A. B9
B. X5
C. M9
D. G5
E3C08 ECLM Page (10 - 5)

## Slide 72: Which of the following is the space-weather term for an extreme geomagnetic storm?
A. B9
B. X5
C. M9
D. G5
(D) E3C08 ECLM Page (10 - 5)

## Slide 73: What type of data is reported by amateur radio propagation reporting networks?
A. Solar flux
B. Electric field intensity
C. Magnetic declination
D. Digital-mode and CW signals
E3C09 ECLM Page (10 - 4)

## Slide 74: What type of data is reported by amateur radio propagation reporting networks?
A. Solar flux
B. Electric field intensity
C. Magnetic declination
D. Digital-mode and CW signals
(D) E3C09 ECLM Page (10 - 4)

## Slide 75: What does the 304A solar parameter measure?
A. The ratio of X-ray flux to radio flux, correlated to sunspot number
B. UV emissions at 304 angstroms, correlated to the solar flux index
C. The solar wind velocity at an angle of 304 degrees from the solar equator, correlated to geomagnetic storms
D. The solar emission at 304 GHz, correlated to X-ray flare levels
E3C10 ECLM Page (10 - 4)

## Slide 76: What does the 304A solar parameter measure?
A. The ratio of X-ray flux to radio flux, correlated to sunspot number
B. UV emissions at 304 angstroms, correlated to the solar flux index
C. The solar wind velocity at an angle of 304 degrees from the solar equator, correlated to geomagnetic storms
D. The solar emission at 304 GHz, correlated to X-ray flare levels
(B) E3C10 ECLM Page (10 - 4)

## Slide 77: What does VOACAP software model?
A. AC voltage and impedance
B. VHF radio propagation
C. HF propagation
D. AC current and impedance
E3C11 ECLM Page (10 - 8)

## Slide 78: What does VOACAP software model?
A. AC voltage and impedance
B. VHF radio propagation
C. HF propagation
D. AC current and impedance
(C) E3C11 ECLM Page (10 - 8)

## Slide 79: Which of the following is indicated by a sudden rise in radio background noise across a large portion of the HF spectrum?
A. A temperature inversion has occurred
B. A coronal mass ejection impact or a solar flare has occurred
C. Transequatorial propagation on 6 meters is likely
D. Long-path propagation on the higher HF bands is likely
E3C12 ECLM Page (10 - 6)

## Slide 80: Which of the following is indicated by a sudden rise in radio background noise across a large portion of the HF spectrum?
A. A temperature inversion has occurred
B. A coronal mass ejection impact or a solar flare has occurred
C. Transequatorial propagation on 6 meters is likely
D. Long-path propagation on the higher HF bands is likely
(B) E3C12 ECLM Page (10 - 6)