## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Which of the following limits the highest frequency signal that can be accurately displayed on a digital oscilloscope?
A. Sampling rate of the analog-to-digital converter
B. Analog-to-digital converter reference frequencyC. Q of the circuit
D. All these choices are correct
E4A01 ECLM Page (7 - 7)

## Slide 4: Which of the following limits the highest frequency signal that can be accurately displayed on a digital oscilloscope?
A. Sampling rate of the analog-to-digital converter
B. Analog-to-digital converter reference frequencyC. Q of the circuit
D. All these choices are correct
(A) E4A01 ECLM Page (7 - 7)

## Slide 5: Which of the following parameters does a spectrum analyzer display on the vertical and horizontal axes?
A. RF amplitude and time
B. RF amplitude and frequency
C. SWR and frequency
D. SWR and time
E4A02 ECLM Page (7 - 10)

## Slide 6: Which of the following parameters does a spectrum analyzer display on the vertical and horizontal axes?
A. RF amplitude and time
B. RF amplitude and frequency
C. SWR and frequency
D. SWR and time
(B) E4A02 ECLM Page (7 - 10)

## Slide 7: Which of the following test instruments is used to display spurious signals and/or intermodulation distortion products generated by an SSB transmitter?
A. Differential resolver
B. Spectrum analyzer
C. Logic analyzer
D. Network analyzer
E4A03 ECLM Page (7 - 10)

## Slide 8: Which of the following test instruments is used to display spurious signals and/or intermodulation distortion products generated by an SSB transmitter?
A. Differential resolver
B. Spectrum analyzer
C. Logic analyzer
D. Network analyzer
(B) E4A03 ECLM Page (7 - 10)

## Slide 9: How is compensation of an oscilloscope probe performed?
A. A square wave is displayed, and the probe is adjusted until the horizontal portions of the displayed wave are as nearly flat as possible
B. A high frequency sine wave is displayed, and the probe is adjusted for maximum amplitude
C. A frequency standard is displayed, and the probe is adjusted until the deflection time is accurate
D. A DC voltage standard is displayed, and the probe is adjusted until the displayed voltage is accurate
E4A04 ECLM Page (7 - 7)

## Slide 10: How is compensation of an oscilloscope probe performed?
A. A square wave is displayed, and the probe is adjusted until the horizontal portions of the displayed wave are as nearly flat as possible
B. A high frequency sine wave is displayed, and the probe is adjusted for maximum amplitude
C. A frequency standard is displayed, and the probe is adjusted until the deflection time is accurate
D. A DC voltage standard is displayed, and the probe is adjusted until the displayed voltage is accurate
(A) E4A04 ECLM Page (7 - 7)

## Slide 11: What is the purpose of the prescaler function on a frequency counter?
A. Amplify low-level signals for more accurate counting
B. Multiply a higher frequency signal so a low-frequency counter can display the operating frequency
C. Prevent oscillation in a low-frequency counter circuit
D. Reduce the signal frequency to within the counter's operating range
E4A05 ECLM Page (7 - 4)

## Slide 12: What is the purpose of the prescaler function on a frequency counter?
A. Amplify low-level signals for more accurate counting
B. Multiply a higher frequency signal so a low-frequency counter can display the operating frequency
C. Prevent oscillation in a low-frequency counter circuit
D. Reduce the signal frequency to within the counter's operating range
(D) E4A05 ECLM Page (7 - 4)

## Slide 13: What is the effect of aliasing on a digital oscilloscope when displaying a waveform?
A. A false, jittery low-frequency version of the waveform is displayed
B. The waveform DC offset will be inaccurate
C. Calibration of the vertical scale is no longer valid
D. Excessive blanking occurs, which prevents display of the waveform
E4A06 ECLM Page (7 - 7)

## Slide 14: What is the effect of aliasing on a digital oscilloscope when displaying a waveform?
A. A false, jittery low-frequency version of the waveform is displayed
B. The waveform DC offset will be inaccurate
C. Calibration of the vertical scale is no longer valid
D. Excessive blanking occurs, which prevents display of the waveform
(A) E4A06 ECLM Page (7 - 7)

## Slide 15: Which of the following is an advantage of using an antenna analyzer compared to an SWR bridge?
A. Antenna analyzers automatically tune your antenna for resonance
B. Antenna analyzers compute SWR and impedance automatically
C. Antenna analyzers display a time-varying representation of the modulation envelope
D. All these choices are correct
E4A07 ECLM Page (9 - 40)

## Slide 16: Which of the following is an advantage of using an antenna analyzer compared to an SWR bridge?
A. Antenna analyzers automatically tune your antenna for resonance
B. Antenna analyzers compute SWR and impedance automatically
C. Antenna analyzers display a time-varying representation of the modulation envelope
D. All these choices are correct
(B) E4A07 ECLM Page (9 - 40)

## Slide 17: Which of the following measures SWR?
A. A spectrum analyzer
B. A Q meter
C. An ohmmeter
D. An antenna analyzer
E4A08 ECLM Page (9 - 39)

## Slide 18: Which of the following measures SWR?
A. A spectrum analyzer
B. A Q meter
C. An ohmmeter
D. An antenna analyzer
(D) E4A08 ECLM Page (9 - 39)

## Slide 19: Which of the following is good practice when using an oscilloscope probe?
A. Keep the signal ground connection of the probe as short as possible
B. Never use a high impedance probe to measure a low impedance circuit
C. Never use a DC-coupled probe to measure an AC circuit
D. All these choices are correct
E4A09 ECLM Page (7 - 6)

## Slide 20: Which of the following is good practice when using an oscilloscope probe?
A. Keep the signal ground connection of the probe as short as possible
B. Never use a high impedance probe to measure a low impedance circuit
C. Never use a DC-coupled probe to measure an AC circuit
D. All these choices are correct
(A) E4A09 ECLM Page (7 - 6)

## Slide 21: Which trigger mode is most effective when using an oscilloscope to measure a linear power supply’s output ripple?
A. Single-shot
B. Edge
C. Level
D. Line
E4A10 ECLM Page (7 - 7)

## Slide 22: Which trigger mode is most effective when using an oscilloscope to measure a linear power supply’s output ripple?
A. Single-shot
B. Edge
C. Level
D. Line
(A) E4A10 ECLM Page (7 - 7)

## Slide 23: Which of the following can be measured with an antenna analyzer?
A. Velocity factor
B. Cable length
C. Resonant frequency of a tuned circuit
D. All these choices are correct
E4A11 ECLM Page (9 - 39)

## Slide 24: Which of the following can be measured with an antenna analyzer?
A. Velocity factor
B. Cable length
C. Resonant frequency of a tuned circuit
D. All these choices are correct
(D) E4A11 ECLM Page (9 - 39)

## Slide 25: Which of the following factors most affects the accuracy of a frequency counter?
A. Input attenuator accuracy
B. Time base accuracy
C. Decade divider accuracy
D. Temperature coefficient of the logic
E4B01 ECLM Page (7 - 4)

## Slide 26: Which of the following factors most affects the accuracy of a frequency counter?
A. Input attenuator accuracy
B. Time base accuracy
C. Decade divider accuracy
D. Temperature coefficient of the logic
(B) E4B01 ECLM Page (7 - 4)

## Slide 27: What is the significance of voltmeter sensitivity expressed in ohms per volt?
A. The full scale reading of the voltmeter multiplied by its ohms per volt rating will indicate the input impedance of the voltmeter
B. When used as a galvanometer, the reading in volts multiplied by the ohms per volt rating will determine the power drawn by the device under test
C. When used as an ohmmeter, the reading in ohms divided by the ohms per volt rating will determine the voltage applied to the circuit
D. When used as an ammeter, the full scale reading in amps divided by ohms per volt rating will determine the size of shunt needed
E4B02 ECLM Page (7 - 2)

## Slide 28: What is the significance of voltmeter sensitivity expressed in ohms per volt?
A. The full scale reading of the voltmeter multiplied by its ohms per volt rating will indicate the input impedance of the voltmeter
B. When used as a galvanometer, the reading in volts multiplied by the ohms per volt rating will determine the power drawn by the device under test
C. When used as an ohmmeter, the reading in ohms divided by the ohms per volt rating will determine the voltage applied to the circuit
D. When used as an ammeter, the full scale reading in amps divided by ohms per volt rating will determine the size of shunt needed
(A) E4B02 ECLM Page (7 - 2)

## Slide 29: Which S parameter is equivalent to forward gain?
A. S11
B. S12
C. S21
D. S22
E4B03 ECLM Page (9 - 39)

## Slide 30: Which S parameter is equivalent to forward gain?
A. S11
B. S12
C. S21
D. S22
(C) E4B03 ECLM Page (9 - 39)

## Slide 31: Which S parameter represents input port return loss or reflection coefficient (equivalent to VSWR)?
A. S11
B. S12
C. S21
D. S22
E4B04 ECLM Page (9 - 38)

## Slide 32: Which S parameter represents input port return loss or reflection coefficient (equivalent to VSWR)?
A. S11
B. S12
C. S21
D. S22
(A) E4B04 ECLM Page (9 - 38)

## Slide 33: What three test loads are used to calibrate an RF vector network analyzer?
A. 50 ohms, 75 ohms, and 90 ohms
B. Short circuit, open circuit, and 50 ohms
C. Short circuit, open circuit, and resonant circuit
D. 50 ohms through 1/8 wavelength, 1/4 wavelength, and 1/2 wavelength of coaxial cable
E4B05 ECLM Page (9 - 40)

## Slide 34: What three test loads are used to calibrate an RF vector network analyzer?
A. 50 ohms, 75 ohms, and 90 ohms
B. Short circuit, open circuit, and 50 ohms
C. Short circuit, open circuit, and resonant circuit
D. 50 ohms through 1/8 wavelength, 1/4 wavelength, and 1/2 wavelength of coaxial cable
(B) E4B05 ECLM Page (9 - 40)

## Slide 35: How much power is being absorbed by the load when a directional power meter connected between a transmitter and a terminating load reads 100 watts forward power and 25 watts reflected power?
A. 100 watts
B. 125 watts
C. 25 watts
D. 75 watts
E4B06 ECLM Page (9 - 32)

## Slide 36: How much power is being absorbed by the load when a directional power meter connected between a transmitter and a terminating load reads 100 watts forward power and 25 watts reflected power?
A. 100 watts
B. 125 watts
C. 25 watts
D. 75 watts
(D) E4B06 ECLM Page (9 - 32)

## Slide 37: What do the subscripts of S parameters represent?
A. The port or ports at which measurements are made
B. The relative time between measurements
C. Relative quality of the data
D. Frequency order of the measurements
E4B07 ECLM Page (9 - 38)

## Slide 38: What do the subscripts of S parameters represent?
A. The port or ports at which measurements are made
B. The relative time between measurements
C. Relative quality of the data
D. Frequency order of the measurements
(A) E4B07 ECLM Page (9 - 38)

## Slide 39: Which of the following can be used to measure the Q of a series-tuned circuit?
A. The inductance to capacitance ratio
B. The frequency shift
C. The bandwidth of the circuit's frequency response
D. The resonant frequency of the circuit
E4B08 ECLM Page (4 - 32)

## Slide 40: Which of the following can be used to measure the Q of a series-tuned circuit?
A. The inductance to capacitance ratio
B. The frequency shift
C. The bandwidth of the circuit's frequency response
D. The resonant frequency of the circuit
(C) E4B08 ECLM Page (4 - 32)

## Slide 41: Which of the following can be measured by a two-port vector network analyzer?
A. Phase noise
B. Filter frequency response
C. Pulse rise time
D. Forward power
E4B09 ECLM Page (9 - 32)

## Slide 42: Which of the following can be measured by a two-port vector network analyzer?
A. Phase noise
B. Filter frequency response
C. Pulse rise time
D. Forward power
(B) E4B09 ECLM Page (9 - 32)

## Slide 43: Which of the following methods measures intermodulation distortion in an SSB transmitter?
A. Modulate the transmitter using two RF signals having non-harmonically related frequencies and observe the RF output with a spectrum analyzer
B. Modulate the transmitter using two AF signals having non-harmonically related frequencies and observe the RF output with a spectrum analyzer
C. Modulate the transmitter using two AF signals having harmonically related frequencies and observe the RF output with a peak reading wattmeter
D. Modulate the transmitter using two RF signals having harmonically related frequencies and observe the RF output with a logic analyzer
E4B10 ECLM Page (7 - 11)

## Slide 44: Which of the following methods measures intermodulation distortion in an SSB transmitter?
A. Modulate the transmitter using two RF signals having non-harmonically related frequencies and observe the RF output with a spectrum analyzer
B. Modulate the transmitter using two AF signals having non-harmonically related frequencies and observe the RF output with a spectrum analyzer
C. Modulate the transmitter using two AF signals having harmonically related frequencies and observe the RF output with a peak reading wattmeter
D. Modulate the transmitter using two RF signals having harmonically related frequencies and observe the RF output with a logic analyzer
(B) E4B10 ECLM Page (7 - 11)

## Slide 45: Which of the following can be measured with a vector network analyzer?
A. Input impedance
B. Output impedance
C. Reflection coefficient
D. All these choices are correct
E4B11 ECLM Page (9 - 40)

## Slide 46: Which of the following can be measured with a vector network analyzer?
A. Input impedance
B. Output impedance
C. Reflection coefficient
D. All these choices are correct
(D) E4B11 ECLM Page (9 - 40)

## Slide 47: What is an effect of excessive phase noise in an SDR receiver’s master clock oscillator?
A. It limits the receiver’s ability to receive strong signals
B. It can affect the receiver’s frequency calibration
C. It decreases receiver third-order intercept point
D. It can combine with strong signals on nearby frequencies to generate interference
E4C01 ECLM Page (7 - 20)

## Slide 48: What is an effect of excessive phase noise in an SDR receiver’s master clock oscillator?
A. It limits the receiver’s ability to receive strong signals
B. It can affect the receiver’s frequency calibration
C. It decreases receiver third-order intercept point
D. It can combine with strong signals on nearby frequencies to generate interference
(D) E4C01 ECLM Page (7 - 20)

## Slide 49: Which of the following receiver circuits can be effective in eliminating interference from strong out-of-band signals?
A. A front-end filter or pre-selector
B. A narrow IF filter
C. A notch filter
D. A properly adjusted product detector
E4C02 ECLM Page (7 - 14)

## Slide 50: Which of the following receiver circuits can be effective in eliminating interference from strong out-of-band signals?
A. A front-end filter or pre-selector
B. A narrow IF filter
C. A notch filter
D. A properly adjusted product detector
(A) E4C02 ECLM Page (7 - 14)

## Slide 51: What is the term for the suppression in an FM receiver of one signal by another stronger signal on the same frequency?
A. Desensitization
B. Cross-modulation interference
C. Capture effect
D. Frequency discrimination
E4C03 ECLM Page (7 - 21)

## Slide 52: What is the term for the suppression in an FM receiver of one signal by another stronger signal on the same frequency?
A. Desensitization
B. Cross-modulation interference
C. Capture effect
D. Frequency discrimination
(C) E4C03 ECLM Page (7 - 21)

## Slide 53: What is the noise figure of a receiver?
A. The ratio of atmospheric noise to phase noise
B. The ratio of the noise bandwidth in hertz to the theoretical bandwidth of a resistive network
C. The ratio of thermal noise to atmospheric noise
D. The ratio in dB of the noise generated by the receiver to the theoretical minimum noise
E4C04 ECLM Page (7 - 13)

## Slide 54: What is the noise figure of a receiver?
A. The ratio of atmospheric noise to phase noise
B. The ratio of the noise bandwidth in hertz to the theoretical bandwidth of a resistive network
C. The ratio of thermal noise to atmospheric noise
D. The ratio in dB of the noise generated by the receiver to the theoretical minimum noise
(D) E4C04 ECLM Page (7 - 13)

## Slide 55: What does a receiver noise floor of -174 dBm represent?
A. The minimum detectable signal as a function of receive frequency
B. The theoretical noise in a 1 Hz bandwidth at the input of a perfect receiver at room temperature
C. The noise figure of a 1 Hz bandwidth receiver
D. The galactic noise contribution to minimum detectable signal
E4C05 ECLM Page (7 - 12)

## Slide 56: What does a receiver noise floor of -174 dBm represent?
A. The minimum detectable signal as a function of receive frequency
B. The theoretical noise in a 1 Hz bandwidth at the input of a perfect receiver at room temperature
C. The noise figure of a 1 Hz bandwidth receiver
D. The galactic noise contribution to minimum detectable signal
(B) E4C05 ECLM Page (7 - 12)

## Slide 57: How much does increasing a receiver’s bandwidth from 50 Hz to 1,000 Hz increase the receiver’s noise floor?
A. 3 dB
B. 5 dB
C. 10 dB
D. 13 dB
E4C06 ECLM Page (7 - 13)

## Slide 58: How much does increasing a receiver’s bandwidth from 50 Hz to 1,000 Hz increase the receiver’s noise floor?
A. 3 dB
B. 5 dB
C. 10 dB
D. 13 dB
(D) E4C06 ECLM Page (7 - 13)

## Slide 59: What does the MDS of a receiver represent?
A. The meter display sensitivity
B. The minimum discernible signal
C. The multiplex distortion stability
D. The maximum detectable spectrum
E4C07 ECLM Page (7 - 12)

## Slide 60: What does the MDS of a receiver represent?
A. The meter display sensitivity
B. The minimum discernible signal
C. The multiplex distortion stability
D. The maximum detectable spectrum
(B) E4C07 ECLM Page (7 - 12)

## Slide 61: An SDR receiver is overloaded when input signals exceed what level?
A. One-half the maximum sample rate
B. One-half the maximum sampling buffer size
C. The maximum count value of the analog-to-digital converter
D. The reference voltage of the analog-to-digital converter
E4C08 ECLM Page (7 - 16)

## Slide 62: An SDR receiver is overloaded when input signals exceed what level?
A. One-half the maximum sample rate
B. One-half the maximum sampling buffer size
C. The maximum count value of the analog-to-digital converter
D. The reference voltage of the analog-to-digital converter
(C) E4C08 ECLM Page (7 - 16)

## Slide 63: Which of the following choices is a good reason for selecting a high frequency for the design of the IF in a superheterodyne HF or VHF communications receiver?
A. Fewer components in the receiver
B. Reduced drift
C. Easier for front-end circuitry to eliminate image responses
D. Improved receiver noise figure
E4C09 ECLM Page (7 - 14)

## Slide 64: Which of the following choices is a good reason for selecting a high frequency for the design of the IF in a superheterodyne HF or VHF communications receiver?
A. Fewer components in the receiver
B. Reduced drift
C. Easier for front-end circuitry to eliminate image responses
D. Improved receiver noise figure
(C) E4C09 ECLM Page (7 - 14)

## Slide 65: What is an advantage of having a variety of receiver bandwidths from which to select?
A. The noise figure of the RF amplifier can be adjusted to match the modulation type, thus increasing receiver sensitivity
B. Receiver power consumption can be reduced when wider bandwidth is not required
C. Receive bandwidth can be set to match the modulation bandwidth, maximizing signal-to-noise ratio and minimizing interference
D. Multiple frequencies can be received simultaneously if desired
E4C10 ECLM Page (7 - 15)

## Slide 66: What is an advantage of having a variety of receiver bandwidths from which to select?
A. The noise figure of the RF amplifier can be adjusted to match the modulation type, thus increasing receiver sensitivity
B. Receiver power consumption can be reduced when wider bandwidth is not required
C. Receive bandwidth can be set to match the modulation bandwidth, maximizing signal-to-noise ratio and minimizing interference
D. Multiple frequencies can be received simultaneously if desired
(C) E4C10 ECLM Page (7 - 15)

## Slide 67: Why does input attenuation reduce receiver overload on the lower frequency HF bands with little or no impact on signal-to-noise ratio?
A. The attenuator has a low-pass filter to increase the strength of lower frequency signals
B. The attenuator has a noise filter to suppress interference
C. Signals are attenuated separately from the noise
D. Atmospheric noise is generally greater than internally generated noise even after attenuation
E4C11 ECLM Page (7 - 12)

## Slide 68: Why does input attenuation reduce receiver overload on the lower frequency HF bands with little or no impact on signal-to-noise ratio?
A. The attenuator has a low-pass filter to increase the strength of lower frequency signals
B. The attenuator has a noise filter to suppress interference
C. Signals are attenuated separately from the noise
D. Atmospheric noise is generally greater than internally generated noise even after attenuation
(D) E4C11 ECLM Page (7 - 12)

## Slide 69: How does a narrow-band roofing filter affect receiver performance?
A. It improves sensitivity by reducing front-end noise
B. It improves intelligibility by using low Q circuitry to reduce ringing
C. It improves blocking dynamic range by attenuating strong signals near the receive frequency
D. All these choices are correct
E4C12 ECLM Page (7 - 16)

## Slide 70: How does a narrow-band roofing filter affect receiver performance?
A. It improves sensitivity by reducing front-end noise
B. It improves intelligibility by using low Q circuitry to reduce ringing
C. It improves blocking dynamic range by attenuating strong signals near the receive frequency
D. All these choices are correct
(C) E4C12 ECLM Page (7 - 16)

## Slide 71: What is reciprocal mixing?
A. Two out-of-band signals mixing to generate an in-band spurious signal
B. In-phase signals cancelling in a mixer resulting in loss of receiver sensitivity
C. Two digital signals combining from alternate time slots
D. Local oscillator phase noise mixing with adjacent strong signals to create interference to desired signals
E4C13 ECLM Page (7 - 15)

## Slide 72: What is reciprocal mixing?
A. Two out-of-band signals mixing to generate an in-band spurious signal
B. In-phase signals cancelling in a mixer resulting in loss of receiver sensitivity
C. Two digital signals combining from alternate time slots
D. Local oscillator phase noise mixing with adjacent strong signals to create interference to desired signals
(D) E4C13 ECLM Page (7 - 15)

## Slide 73: What is the purpose of the receiver IF Shift control?
A. To permit listening on a different frequency from the transmitting frequency
B. To change frequency rapidly
C. To reduce interference from stations transmitting on adjacent frequencies
D. To tune in stations slightly off frequency without changing the transmit frequency
E4C14 ECLM Page (7 - 15)

## Slide 74: What is the purpose of the receiver IF Shift control?
A. To permit listening on a different frequency from the transmitting frequency
B. To change frequency rapidly
C. To reduce interference from stations transmitting on adjacent frequencies
D. To tune in stations slightly off frequency without changing the transmit frequency
(C) E4C14 ECLM Page (7 - 15)