## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is meant by the blocking dynamic range of a receiver?
A. The difference in dB between the noise floor and the level of an incoming signal that will cause 1 dB of gain compression
B. The minimum difference in dB between the levels of two FM signals that will cause one signal to block the other
C. The difference in dB between the noise floor and the third order intercept point
D. The minimum difference in dB between two signals which produce third order intermodulation products greater than the noise floor
E4D01 ECLM Page (7 - 20)

## Slide 4: What is meant by the blocking dynamic range of a receiver?
A. The difference in dB between the noise floor and the level of an incoming signal that will cause 1 dB of gain compression
B. The minimum difference in dB between the levels of two FM signals that will cause one signal to block the other
C. The difference in dB between the noise floor and the third order intercept point
D. The minimum difference in dB between two signals which produce third order intermodulation products greater than the noise floor
(A) E4D01 ECLM Page (7 - 20)

## Slide 5: Which of the following describes problems caused by poor dynamic range in a receiver?
A. Spurious signals caused by cross-modulation and desensitization from strong adjacent signals
B. Oscillator instability requiring frequent retuning and loss of ability to recover the opposite sideband
C. Cross-modulation of the desired signal and insufficient audio power to operate the speaker
D. Oscillator instability and severe audio distortion of all but the strongest received signals
E4D02 ECLM Page (7 - 22)

## Slide 6: Which of the following describes problems caused by poor dynamic range in a receiver?
A. Spurious signals caused by cross-modulation and desensitization from strong adjacent signals
B. Oscillator instability requiring frequent retuning and loss of ability to recover the opposite sideband
C. Cross-modulation of the desired signal and insufficient audio power to operate the speaker
D. Oscillator instability and severe audio distortion of all but the strongest received signals
(A) E4D02 ECLM Page (7 - 22)

## Slide 7: What creates intermodulation interference between two repeaters in close proximity?
A. The output signals cause feedback in the final amplifier of one or both transmitters
B. The output signals mix in the final amplifier of one or both transmitters
C. The input frequencies are harmonically related
D. The output frequencies are harmonically related
E4D03 ECLM Page (7 - 22)

## Slide 8: What creates intermodulation interference between two repeaters in close proximity?
A. The output signals cause feedback in the final amplifier of one or both transmitters
B. The output signals mix in the final amplifier of one or both transmitters
C. The input frequencies are harmonically related
D. The output frequencies are harmonically related
(B) E4D03 ECLM Page (7 - 22)

## Slide 9: Which of the following is used to reduce or eliminate intermodulation interference in a repeater caused by a nearby transmitter?
A. A band-pass filter in the feed line between the transmitter and receiver
B. A properly terminated circulator at the output of the repeater's transmitter
C. Utilizing a Class C final amplifier
D. Utilizing a Class D final amplifier
E4D04 ECLM Page (7 - 22)

## Slide 10: Which of the following is used to reduce or eliminate intermodulation interference in a repeater caused by a nearby transmitter?
A. A band-pass filter in the feed line between the transmitter and receiver
B. A properly terminated circulator at the output of the repeater's transmitter
C. Utilizing a Class C final amplifier
D. Utilizing a Class D final amplifier
(B) E4D04 ECLM Page (7 - 22)

## Slide 11: What transmitter frequencies would create an intermodulation-product signal in a receiver tuned to 146.70 MHz when a nearby station transmits on 146.52 MHz?
A. 146.34 MHz and 146.61 MHz
B. 146.88 MHz and 146.34 MHz
C. 146.10 MHz and 147.30 MHz
D. 146.30 MHz and 146.90 MHz
E4D05 ECLM Page (7 - 18)

## Slide 12: What transmitter frequencies would create an intermodulation-product signal in a receiver tuned to 146.70 MHz when a nearby station transmits on 146.52 MHz?
A. 146.34 MHz and 146.61 MHz
B. 146.88 MHz and 146.34 MHz
C. 146.10 MHz and 147.30 MHz
D. 146.30 MHz and 146.90 MHz
(A) E4D05 ECLM Page (7 - 18)

## Slide 13: What is the term for the reduction in receiver sensitivity caused by a strong signal near the received frequency?
A. Reciprocal mixing
B. Quieting
C. Desensitization
D. Cross modulation interference
E4D06 ECLM Page (7 - 22)

## Slide 14: What is the term for the reduction in receiver sensitivity caused by a strong signal near the received frequency?
A. Reciprocal mixing
B. Quieting
C. Desensitization
D. Cross modulation interference
(C) E4D06 ECLM Page (7 - 22)

## Slide 15: Which of the following reduces the likelihood of receiver desensitization?
A. Insert attenuation before the first RF stage
B. Raise the receiver’s IF frequency
C. Increase the receiver’s front-end gain
D. Switch from fast AGC to slow AGC
E4D07 ECLM Page (7 - 17)

## Slide 16: Which of the following reduces the likelihood of receiver desensitization?
A. Insert attenuation before the first RF stage
B. Raise the receiver’s IF frequency
C. Increase the receiver’s front-end gain
D. Switch from fast AGC to slow AGC
(A) E4D07 ECLM Page (7 - 17)

## Slide 17: What causes intermodulation in an electronic circuit?
A. Negative feedback
B. Lack of neutralization
C. Nonlinear circuits or devices
D. Positive feedback
E4D08 ECLM Page (7 - 22)

## Slide 18: What causes intermodulation in an electronic circuit?
A. Negative feedback
B. Lack of neutralization
C. Nonlinear circuits or devices
D. Positive feedback
(C) E4D08 ECLM Page (7 - 22)

## Slide 19: What is the purpose of the preselector in a communications receiver?
A. To store often-used frequencies
B. To provide a range of AGC time constants
C. To increase rejection of signals outside the desired band
D. To allow selection of the optimum RF amplifier device
E4D09 ECLM Page (7 - 14)

## Slide 20: What is the purpose of the preselector in a communications receiver?
A. To store often-used frequencies
B. To provide a range of AGC time constants
C. To increase rejection of signals outside the desired band
D. To allow selection of the optimum RF amplifier device
(C) E4D09 ECLM Page (7 - 14)

## Slide 21: What does a third-order intercept level of 40 dBm mean with respect to receiver performance?
A. Signals less than 40 dBm will not generate audible third-order intermodulation products
B. The receiver can tolerate signals up to 40 dB above the noise floor without producing third-order intermodulation products
C. A pair of 40 dBm input signals will theoretically generate a third-order intermodulation product that has the same output amplitude as either of the input signals
D. A pair of 1 mW input signals will produce a third-order intermodulation product that is 40 dB stronger than the input signal
E4D10 ECLM Page (7 - 19)

## Slide 22: What does a third-order intercept level of 40 dBm mean with respect to receiver performance?
A. Signals less than 40 dBm will not generate audible third-order intermodulation products
B. The receiver can tolerate signals up to 40 dB above the noise floor without producing third-order intermodulation products
C. A pair of 40 dBm input signals will theoretically generate a third-order intermodulation product that has the same output amplitude as either of the input signals
D. A pair of 1 mW input signals will produce a third-order intermodulation product that is 40 dB stronger than the input signal
(C) E4D10 ECLM Page (7 - 19)

## Slide 23: Why are odd-order intermodulation products, created within a receiver, of particular interest compared to other products?
A. Odd-order products of two signals in the band of interest are also likely to be within the band
B. Odd-order products overload the IF filters
C. Odd-order products are an indication of poor image rejection
D. Odd-order intermodulation produces three products for every input signal within the band of interest
E4D11 ECLM Page (7 - 18)

## Slide 24: Why are odd-order intermodulation products, created within a receiver, of particular interest compared to other products?
A. Odd-order products of two signals in the band of interest are also likely to be within the band
B. Odd-order products overload the IF filters
C. Odd-order products are an indication of poor image rejection
D. Odd-order intermodulation produces three products for every input signal within the band of interest
(A) E4D11 ECLM Page (7 - 18)

## Slide 25: What is the link margin in a system with a transmit power level of 10 W (+40 dBm), a system antenna gain of 10 dBi, a cable loss of 3 dB, a path loss of 136 dB, a receiver minimum discernable signal of -103 dBm, and a required signal-to-noise ratio of 6 dB?
A. -8dB
B. -14dB
C. +8dB
D. +14dB
E4D12 ECLM Page (7 - 16)

## Slide 26: What is the link margin in a system with a transmit power level of 10 W (+40 dBm), a system antenna gain of 10 dBi, a cable loss of 3 dB, a path loss of 136 dB, a receiver minimum discernable signal of -103 dBm, and a required signal-to-noise ratio of 6 dB?
A. -8dB
B. -14dB
C. +8dB
D. +14dB
(C) E4D12 ECLM Page (7 - 16)

## Slide 27: What is the received signal level with a transmit power of 10 W (+40 dBm), a transmit antenna gain of 6 dBi, a receive antenna gain of 3 dBi, and a path loss of 100 dB?
A. -51 dBm
B. -54 dBm
C. -57 dBm
D. -60 dBm
E4D13 ECLM Page (7 - 16)

## Slide 28: What is the received signal level with a transmit power of 10 W (+40 dBm), a transmit antenna gain of 6 dBi, a receive antenna gain of 3 dBi, and a path loss of 100 dB?
A. -51 dBm
B. -54 dBm
C. -57 dBm
D. -60 dBm
(A) E4D13 ECLM Page (7 - 16)

## Slide 29: What power level does a receiver minimum discernible signal of -100 dBm represent?
A. 100 microwatts
B. 0.1 microwatt
C. 0.001 microwatts
D. 0.1 picowatts
E4D14 ECLM

## Slide 30: What power level does a receiver minimum discernible signal of -100 dBm represent?
A. 100 microwatts
B. 0.1 microwatt
C. 0.001 microwatts
D. 0.1 picowatts
(D) E4D14 ECLM

## Slide 31: What problem can occur when using an automatic notch filter (ANF) to remove interfering carriers while receiving CW signals?
A. Removal of the CW signal as well as the interfering carrier
B. Any nearby signal passing through the DSP system will overwhelm the desired signal
C. Received CW signals will appear to be modulated at the DSP clock frequency
D. Ringing in the DSP filter will completely remove the spaces between the CW characters
E4E01 ECLM Page (7 - 27)

## Slide 32: What problem can occur when using an automatic notch filter (ANF) to remove interfering carriers while receiving CW signals?
A. Removal of the CW signal as well as the interfering carrier
B. Any nearby signal passing through the DSP system will overwhelm the desired signal
C. Received CW signals will appear to be modulated at the DSP clock frequency
D. Ringing in the DSP filter will completely remove the spaces between the CW characters
(A) E4E01 ECLM Page (7 - 27)

## Slide 33: Which of the following types of noise can often be reduced by a digital noise reduction?
A. Broadband white noise
B. Ignition noise
C. Power line noise
D. All these choices are correct
E4E02 ECLM Page (7 - 27)

## Slide 34: Which of the following types of noise can often be reduced by a digital noise reduction?
A. Broadband white noise
B. Ignition noise
C. Power line noise
D. All these choices are correct
(D) E4E02 ECLM Page (7 - 27)

## Slide 35: Which of the following types of noise are removed by a noise blanker?
A. Broadband white noise
B. Impulse noise
C. Hum and buzz
D. All these choices are correct
E4E03 ECLM Page (7 - 26)

## Slide 36: Which of the following types of noise are removed by a noise blanker?
A. Broadband white noise
B. Impulse noise
C. Hum and buzz
D. All these choices are correct
(B) E4E03 ECLM Page (7 - 26)

## Slide 37: How can conducted noise from an automobile battery charging system be suppressed?
A. By installing filter capacitors in series with the alternator leads
B. By installing a noise suppression resistor and a blocking capacitor at the battery
C. By installing a high-pass filter in series with the radio’s power lead and a low-pass filter in parallel with the antenna feed line
D. By installing ferrite chokes on the charging system leads
E4E04 ECLM Page (7 - 26)

## Slide 38: How can conducted noise from an automobile battery charging system be suppressed?
A. By installing filter capacitors in series with the alternator leads
B. By installing a noise suppression resistor and a blocking capacitor at the battery
C. By installing a high-pass filter in series with the radio’s power lead and a low-pass filter in parallel with the antenna feed line
D. By installing ferrite chokes on the charging system leads
(D) E4E04 ECLM Page (7 - 26)

## Slide 39: What is used to suppress radio frequency interference from a line-driven AC motor?
A. A high-pass filter in series with the motor’s power leads
B. A brute-force AC-line filter in series with the motor’s power leads
C. A bypass capacitor in series with the motor’s field winding
D. A bypass choke in parallel with the motor’s field winding
E4E05 ECLM Page (7 - 25)

## Slide 40: What is used to suppress radio frequency interference from a line-driven AC motor?
A. A high-pass filter in series with the motor’s power leads
B. A brute-force AC-line filter in series with the motor’s power leads
C. A bypass capacitor in series with the motor’s field winding
D. A bypass choke in parallel with the motor’s field winding
(B) E4E05 ECLM Page (7 - 25)

## Slide 41: What type of electrical interference can be caused by computer network equipment?
A. A loud AC hum in the audio output of your station receiver
B. A clicking noise at intervals of a few seconds
C. The appearance of unstable modulated or unmodulated signals at specific frequencies
D. A whining-type noise that continually pulses off and on
E4E06 ECLM Page (7 - 25)

## Slide 42: What type of electrical interference can be caused by computer network equipment?
A. A loud AC hum in the audio output of your station receiver
B. A clicking noise at intervals of a few seconds
C. The appearance of unstable modulated or unmodulated signals at specific frequencies
D. A whining-type noise that continually pulses off and on
(C) E4E06 ECLM Page (7 - 25)

## Slide 43: Which of the following can cause shielded cables to radiate or receive interference?
A. Low inductance ground connections at both ends of the shield
B. Common mode currents on the shield and conductors
C. Use of braided shielding material
D. Tying all ground connections to a common point resulting in differential mode currents in the shield
E4E07 ECLM Page (7 - 25)

## Slide 44: Which of the following can cause shielded cables to radiate or receive interference?
A. Low inductance ground connections at both ends of the shield
B. Common mode currents on the shield and conductors
C. Use of braided shielding material
D. Tying all ground connections to a common point resulting in differential mode currents in the shield
(B) E4E07 ECLM Page (7 - 25)

## Slide 45: What current flows equally on all conductors of an unshielded multiconductor cable?
A. Differential-mode current
B. Common-mode current
C. Reactive current only
D. Magnetically-coupled current only
E4E08 ECLM Page (7 - 25)

## Slide 46: What current flows equally on all conductors of an unshielded multiconductor cable?
A. Differential-mode current
B. Common-mode current
C. Reactive current only
D. Magnetically-coupled current only
(B) E4E08 ECLM Page (7 - 25)

## Slide 47: What undesirable effect can occur when using an IF noise blanker?
A. Received audio in the speech range might have an echo effect
B. The audio frequency bandwidth of the received signal might be compressed
C. Nearby signals may appear to be excessively wide even if they meet emission standards
D. FM signals can no longer be demodulated
E4E09 ECLM Page (7 - 26)

## Slide 48: What undesirable effect can occur when using an IF noise blanker?
A. Received audio in the speech range might have an echo effect
B. The audio frequency bandwidth of the received signal might be compressed
C. Nearby signals may appear to be excessively wide even if they meet emission standards
D. FM signals can no longer be demodulated
(C) E4E09 ECLM Page (7 - 26)

## Slide 49: Which of the following can create intermittent loud roaring or buzzing AC line interference?
A. Arcing contacts in a thermostatically controlled device
B. A defective doorbell or doorbell transformer inside a nearby residence
C. A malfunctioning illuminated advertising display
D. All these choices are correct
E4E10 ECLM Page (7 - 25)

## Slide 50: Which of the following can create intermittent loud roaring or buzzing AC line interference?
A. Arcing contacts in a thermostatically controlled device
B. A defective doorbell or doorbell transformer inside a nearby residence
C. A malfunctioning illuminated advertising display
D. All these choices are correct
(D) E4E10 ECLM Page (7 - 25)

## Slide 51: What could cause local AM broadcast band signals to combine to generate spurious signals in the MF or HF bands?
A. One or more of the broadcast stations is transmitting an over-modulated signal
B. Nearby corroded metal joints are mixing and re-radiating the broadcast signals
C. You are receiving skywave signals from a distant station
D. Your station receiver IF amplifier stage is defective
E4E11 ECLM Page (7 - 23)

## Slide 52: What could cause local AM broadcast band signals to combine to generate spurious signals in the MF or HF bands?
A. One or more of the broadcast stations is transmitting an over-modulated signal
B. Nearby corroded metal joints are mixing and re-radiating the broadcast signals
C. You are receiving skywave signals from a distant station
D. Your station receiver IF amplifier stage is defective
(B) E4E11 ECLM Page (7 - 23)

## Slide 53: What causes interference received as a series of carriers at regular intervals across a wide frequency range?
A. Switch-mode power supplies
B. Radar transmitters
C. Wireless security camera transmitters
D. Electric fences
E4E12 ECLM Page (7 - 23)

## Slide 54: What causes interference received as a series of carriers at regular intervals across a wide frequency range?
A. Switch-mode power supplies
B. Radar transmitters
C. Wireless security camera transmitters
D. Electric fences
(A) E4E12 ECLM Page (7 - 23)

## Slide 55: Where should a station AC surge protector be installed?
A. At the AC service panel
B. At an AC outlet
C. On the single point ground panel
D. On a ground rod outside the station
E4E13 ECLM Page (7 - 23)

## Slide 56: Where should a station AC surge protector be installed?
A. At the AC service panel
B. At an AC outlet
C. On the single point ground panel
D. On a ground rod outside the station
(C) E4E13 ECLM Page (7 - 23)

## Slide 57: What is the purpose of a single point ground panel?
A. Remove AC power in case of a short-circuit
B. Prevent common-mode transients in multi-wire systems
C. Eliminate air gaps between protected and non-protected circuits
D. Ensure all lightning protectors activate at the same time
E4E14 ECLM Page (7 - 23)

## Slide 58: What is the purpose of a single point ground panel?
A. Remove AC power in case of a short-circuit
B. Prevent common-mode transients in multi-wire systems
C. Eliminate air gaps between protected and non-protected circuits
D. Ensure all lightning protectors activate at the same time
(D) E4E14 ECLM Page (7 - 23)