## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What can cause the voltage across reactances in a series RLC circuit to be higher than the voltage applied to the entire circuit?
A. Resonance
B. Capacitance
C. Conductance
D. Resistance
E5A01 ECLM Page (4 - 30)

## Slide 4: What can cause the voltage across reactances in a series RLC circuit to be higher than the voltage applied to the entire circuit?
A. Resonance
B. Capacitance
C. Conductance
D. Resistance
(A) E5A01 ECLM Page (4 - 30)

## Slide 5: What is the resonant frequency of an RLC circuit if R is 22 ohms, L is 50 microhenries, and C is 40 picofarads?
A. 44.72 MHz
B. 22.36 MHz
C. 3.56 MHz
D. 1.78 MHz
E5A02 ECLM Page (4 - 27)

## Slide 6: What is the resonant frequency of an RLC circuit if R is 22 ohms, L is 50 microhenries, and C is 40 picofarads?
A. 44.72 MHz
B. 22.36 MHz
C. 3.56 MHz
D. 1.78 MHz
(C) E5A02 ECLM Page (4 - 27)

## Slide 7: What is the magnitude of the impedance of a series RLC circuit at resonance?
A. High, as compared to the circuit resistance
B. Approximately equal to capacitive reactance
C. Approximately equal to inductive reactance
D. Approximately equal to circuit resistance
E5A03 ECLM Page (4 - 30)

## Slide 8: What is the magnitude of the impedance of a series RLC circuit at resonance?
A. High, as compared to the circuit resistance
B. Approximately equal to capacitive reactance
C. Approximately equal to inductive reactance
D. Approximately equal to circuit resistance
(D) E5A03 ECLM Page (4 - 30)

## Slide 9: What is the magnitude of the impedance of a parallel RLC circuit at resonance?
A. Approximately equal to circuit resistance
B. Approximately equal to inductive reactance
C. Low compared to the circuit resistance
D. High compared to the circuit resistance
E5A04 ECLM Page (4 - 30)

## Slide 10: What is the magnitude of the impedance of a parallel RLC circuit at resonance?
A. Approximately equal to circuit resistance
B. Approximately equal to inductive reactance
C. Low compared to the circuit resistance
D. High compared to the circuit resistance
(A) E5A04 ECLM Page (4 - 30)

## Slide 11: What is the result of increasing the Q of an impedance-matching circuit?
A. Matching bandwidth is decreased
B. Matching bandwidth is increased
C. Matching range is increased
D. It has no effect on impedance matching
E5A05 ECLM Page (4 - 33)

## Slide 12: What is the result of increasing the Q of an impedance-matching circuit?
A. Matching bandwidth is decreased
B. Matching bandwidth is increased
C. Matching range is increased
D. It has no effect on impedance matching
(A) E5A05 ECLM Page (4 - 33)

## Slide 13: What is the magnitude of the circulating current within the components of a parallel LC circuit at resonance?
A. It is at a minimum
B. It is at a maximum
C. It equals 1 divided by the quantity 2 times pi, multiplied by the square root of inductance L multiplied by capacitance C
D. It equals 2 multiplied by pi, multiplied by frequency "F", multiplied by inductance "L"
E5A06 ECLM Page (4 - 30)

## Slide 14: What is the magnitude of the circulating current within the components of a parallel LC circuit at resonance?
A. It is at a minimum
B. It is at a maximum
C. It equals 1 divided by the quantity 2 times pi, multiplied by the square root of inductance L multiplied by capacitance C
D. It equals 2 multiplied by pi, multiplied by frequency "F", multiplied by inductance "L"
(B) E5A06 ECLM Page (4 - 30)

## Slide 15: What is the magnitude of the current at the input of a parallel RLC circuit at resonance?
A. Minimum
B. Maximum
C. R/L
D. L/R
E5A07 ECLM Page (4 - 30)

## Slide 16: What is the magnitude of the current at the input of a parallel RLC circuit at resonance?
A. Minimum
B. Maximum
C. R/L
D. L/R
(A) E5A07 ECLM Page (4 - 30)

## Slide 17: What is the phase relationship between the current through and the voltage across a series resonant circuit at resonance?
A. The voltage leads the current by 90 degrees
B. The current leads the voltage by 90 degrees
C. The voltage and current are in phase
D. The voltage and current are 180 degrees out of phase
E5A08 ECLM Page (4 - 31)

## Slide 18: What is the phase relationship between the current through and the voltage across a series resonant circuit at resonance?
A. The voltage leads the current by 90 degrees
B. The current leads the voltage by 90 degrees
C. The voltage and current are in phase
D. The voltage and current are 180 degrees out of phase
(C) E5A08 ECLM Page (4 - 31)

## Slide 19: How is the Q of an RLC parallel resonant circuit calculated?
A. Reactance of either the inductance or capacitance divided by the resistance
B. Reactance of either the inductance or capacitance multiplied by the resistance
C. Resistance divided by the reactance of either the inductance or capacitance
D. Reactance of the inductance multiplied by the reactance of the capacitance
E5A09 ECLM Page (4 - 32)

## Slide 20: How is the Q of an RLC parallel resonant circuit calculated?
A. Reactance of either the inductance or capacitance divided by the resistance
B. Reactance of either the inductance or capacitance multiplied by the resistance
C. Resistance divided by the reactance of either the inductance or capacitance
D. Reactance of the inductance multiplied by the reactance of the capacitance
(C) E5A09 ECLM Page (4 - 32)

## Slide 21: What is the resonant frequency of an RLC circuit if R is 33 ohms, L is 50 microhenries, and C is 10 picofarads?
A. 7.12 MHz
B. 23.5 kHz
C. 7.12 kHz
D. 23.5 MHz
E5A10 ECLM Page (4 - 32)

## Slide 22: How is the Q of an RLC series resonant circuit calculated?
A. Reactance of either the inductance or capacitance divided by the resistance
B. Reactance of either the inductance or capacitance multiplied by the resistance
C. Resistance divided by the reactance of either the inductance or capacitance
D. Reactance of the inductance multiplied by the reactance of the capacitance
(A) E5A10 ECLM Page (4 - 32)

## Slide 23: What is the half-power bandwidth of a resonant circuit that has a resonant frequency of 7.1 MHz and a Q of 150?
A. 157.8 Hz
B. 315.6 Hz
C. 47.3 kHz
D. 23.67 kHz
E5A11 ECLM Page (4 - 33)

## Slide 24: What is the half-power bandwidth of a resonant circuit that has a resonant frequency of 7.1 MHz and a Q of 150?
A. 157.8 Hz
B. 315.6 Hz
C. 47.3 kHz
D. 23.67 kHz
(C) E5A11 ECLM Page (4 - 33)

## Slide 25: What is the half-power bandwidth of a resonant circuit that has a resonant frequency of 3.7 MHz and a Q of 118?
A. 436.6 kHz
B. 218.3 kHz
C. 31.4 kHz
D. 15.7 kHz
E5A12 ECLM Page (4 - 33)

## Slide 26: What is the half-power bandwidth of a resonant circuit that has a resonant frequency of 3.7 MHz and a Q of 118?
A. 436.6 kHz
B. 218.3 kHz
C. 31.4 kHz
D. 15.7 kHz
(C) E5A12 ECLM Page (4 - 33)

## Slide 27: What is an effect of increasing Q in a series resonant circuit?
A. Fewer components are needed for the same performance
B. Parasitic effects are minimized
C. Internal voltages increase
D. Phase shift can become uncontrolled
E5A13 ECLM Page (4 - 32)

## Slide 28: What is an effect of increasing Q in a series resonant circuit?
A. Fewer components are needed for the same performance
B. Parasitic effects are minimized
C. Internal voltages increase
D. Phase shift can become uncontrolled
(C) E5A13 ECLM Page (4 - 32)

## Slide 29: What is the term for the time required for the capacitor in an RC circuit to be charged to 63.2% of the applied voltage or to discharge to 36.8% of its initial voltage?
A. An exponential rate of one
B. One time constant
C. One exponential period
D. A time factor of one
E5B01 ECLM Page (4 - 9)

## Slide 30: What is the term for the time required for the capacitor in an RC circuit to be charged to 63.2% of the applied voltage or to discharge to 36.8% of its initial voltage?
A. An exponential rate of one
B. One time constant
C. One exponential period
D. A time factor of one
(B) E5B01 ECLM Page (4 - 9)

## Slide 31: What letter is commonly used to represent susceptance?
A. G
B. X
C. Y
D. B
E5B02 ECLM Page (4 - 19)

## Slide 32: What letter is commonly used to represent susceptance?
A. G
B. X
C. Y
D. B
(D) E5B02 ECLM Page (4 - 19)

## Slide 33: How is impedance in polar form converted to an equivalent admittance?
A. Take the reciprocal of the angle and change the sign of the magnitude
B. Take the reciprocal of the magnitude and change the sign of the angle
C. Take the square root of the magnitude and add 180 degrees to the angle
D. Square the magnitude and subtract 90 degrees from the angle
E5B03 ECLM Page (4 - 20)

## Slide 34: How is impedance in polar form converted to an equivalent admittance?
A. Take the reciprocal of the angle and change the sign of the magnitude
B. Take the reciprocal of the magnitude and change the sign of the angle
C. Take the square root of the magnitude and add 180 degrees to the angle
D. Square the magnitude and subtract 90 degrees from the angle
(B) E5B03 ECLM Page (4 - 20)

## Slide 35: What is the time constant of a circuit having two 220-microfarad capacitors and two 1-megohm resistors, all in parallel?
A. 55 seconds
B. 110 seconds
C. 440 seconds
D. 220 seconds
E5B04 ECLM Page (4 - 11)

## Slide 36: What is the time constant of a circuit having two 220-microfarad capacitors and two 1-megohm resistors, all in parallel?
A. 55 seconds
B. 110 seconds
C. 440 seconds
D. 220 seconds
(D) E5B04 ECLM Page (4 - 11)

## Slide 37: What is the effect on the magnitude of pure reactance when it is converted to susceptance?
A. It is unchanged
B. The sign is reversed
C. It is shifted by 90 degrees
D. It becomes the reciprocal
E5B05 ECLM Page (4 - 19)

## Slide 38: What is the effect on the magnitude of pure reactance when it is converted to susceptance?
A. It is unchanged
B. The sign is reversed
C. It is shifted by 90 degrees
D. It becomes the reciprocal
(D) E5B05 ECLM Page (4 - 19)

## Slide 39: What is susceptance?
A. The magnetic impedance of a circuit
B. The ratio of magnetic field to electric field
C. The imaginary part of admittance
D. A measure of the efficiency of a transformer
E5B06 ECLM Page (4 - 19)

## Slide 40: What is susceptance?
A. The magnetic impedance of a circuit
B. The ratio of magnetic field to electric field
C. The imaginary part of admittance
D. A measure of the efficiency of a transformer
(C) E5B06 ECLM Page (4 - 19)

## Slide 41: What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 500 ohms, R is 1 kilohm, and XL is 250 ohms?
A. 68.2 degrees with the voltage leading the current
B. 14.0 degrees with the voltage leading the current
C. 14.0 degrees with the voltage lagging the current
D. 68.2 degrees with the voltage lagging the current
E5B07 ECLM Page (4 - 22)

## Slide 42: What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 500 ohms, R is 1 kilohm, and XL is 250 ohms?
A. 68.2 degrees with the voltage leading the current
B. 14.0 degrees with the voltage leading the current
C. 14.0 degrees with the voltage lagging the current
D. 68.2 degrees with the voltage lagging the current
(C) E5B07 ECLM Page (4 - 22)

## Slide 43: What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 300 ohms, R is 100 ohms, and XL is 100 ohms?
A. 63 degrees with the voltage lagging the current
B. 63 degrees with the voltage leading the current
C. 27 degrees with the voltage leading the current
D. 27 degrees with the voltage lagging the current
E5B08 ECLM Page (4 - 22)

## Slide 44: What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 300 ohms, R is 100 ohms, and XL is 100 ohms?
A. 63 degrees with the voltage lagging the current
B. 63 degrees with the voltage leading the current
C. 27 degrees with the voltage leading the current
D. 27 degrees with the voltage lagging the current
(A) E5B08 ECLM Page (4 - 22)

## Slide 45: What is the relationship between the AC current through a capacitor and the voltage across a capacitor?
A. Voltage and current are in phase
B. Voltage and current are 180 degrees out of phase
C. Voltage leads current by 90 degrees
D. Current leads voltage by 90 degrees
E5B09 ECLM Page (4 - 14)

## Slide 46: What is the relationship between the AC current through a capacitor and the voltage across a capacitor?
A. Voltage and current are in phase
B. Voltage and current are 180 degrees out of phase
C. Voltage leads current by 90 degrees
D. Current leads voltage by 90 degrees
(D) E5B09 ECLM Page (4 - 14)

## Slide 47: What is the relationship between the AC current through an inductor and the voltage across an inductor?
A. Voltage leads current by 90 degrees
B. Current leads voltage by 90 degrees
C. Voltage and current are 180 degrees out of phase
D. Voltage and current are in phase
E5B10 ECLM Page (4 - 15)

## Slide 48: What is the relationship between the AC current through an inductor and the voltage across an inductor?
A. Voltage leads current by 90 degrees
B. Current leads voltage by 90 degrees
C. Voltage and current are 180 degrees out of phase
D. Voltage and current are in phase
(A) E5B10 ECLM Page (4 - 15)

## Slide 49: What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 25 ohms, R is 100 ohms, and XL is 75 ohms?
A. 27 degrees with the voltage lagging the current
B. 27 degrees with the voltage leading the current
C. 63 degrees with the voltage lagging the current
D. 63 degrees with the voltage leading the current
E5B11 ECLM Page (4 - 23)

## Slide 50: What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 25 ohms, R is 100 ohms, and XL is 75 ohms?
A. 27 degrees with the voltage lagging the current
B. 27 degrees with the voltage leading the current
C. 63 degrees with the voltage lagging the current
D. 63 degrees with the voltage leading the current
(B) E5B11 ECLM Page (4 - 23)

## Slide 51: What is admittance?
A. The inverse of impedance
B. The term for the gain of a field effect transistor
C. The turns ratio of a transformer
D. The inverse of Q factor
E5B12 ECLM Page (4 - 19)

## Slide 52: What is admittance?
A. The inverse of impedance
B. The term for the gain of a field effect transistor
C. The turns ratio of a transformer
D. The inverse of Q factor
(A) E5B12 ECLM Page (4 - 19)

## Slide 53: Which of the following represents a capacitive reactance in rectangular notation?
A. 0 - j100
B. 0 + j100
C. 100 - j0
D. 100 + j0
E5C01 ECLM Page (4 - 16)

## Slide 54: Which of the following represents a capacitive reactance in rectangular notation?
A. 0 - j100
B. 0 + j100
C. 100 - j0
D. 100 + j0
(A) E5C01 ECLM Page (4 - 16)

## Slide 55: How are impedances described in polar coordinates?
A. By X and R values
B. By real and imaginary parts
C. By phase angle and magnitude
D. By Y and G values
E5C02 ECLM Page (4 - 16)

## Slide 56: How are impedances described in polar coordinates?
A. By X and R values
B. By real and imaginary parts
C. By phase angle and magnitude
D. By Y and G values
(C) E5C02 ECLM Page (4 - 16)

## Slide 57: Which of the following represents a pure inductive reactance in polar coordinates?
A. A positive 45 degree phase angle
B. A negative 45 degree phase angle
C. A positive 90 degree phase angle
D. A negative 90 degree phase angle
E5C03 ECLM Page (4 - 16)

## Slide 58: Which of the following represents a pure inductive reactance in polar coordinates?
A. A positive 45 degree phase angle
B. A negative 45 degree phase angle
C. A positive 90 degree phase angle
D. A negative 90 degree phase angle
(C) E5C03 ECLM Page (4 - 16)

## Slide 59: What type of Y-axis scale is most often used for graphs of circuit frequency response?
A. Linear
B. Scatter
C. Random
D. Logarithmic
E5C04 ECLM Page (4 - 16)

## Slide 60: What type of Y-axis scale is most often used for graphs of circuit frequency response?
A. Linear
B. Scatter
C. Random
D. Logarithmic
(D) E5C04 ECLM Page (4 - 16)

## Slide 61: What kind of diagram is used to show the phase relationship between impedances at a given frequency?
A. Venn diagram
B. Near field diagram
C. Phasor diagram
D. Far field diagram
E5C05 ECLM Page (4 - 16)

## Slide 62: What kind of diagram is used to show the phase relationship between impedances at a given frequency?
A. Venn diagram
B. Near field diagram
C. Phasor diagram
D. Far field diagram
(C) E5C05 ECLM Page (4 - 16)

## Slide 63: What does the impedance 50 – j25 represent?
A. 50 ohms resistance in series with 25 ohms inductive reactance
B. 50 ohms resistance in series with 25 ohms capacitive reactance
C. 25 ohms resistance in series with 50 ohms inductive reactance
D. 25 ohms resistance in series with 50 ohms capacitive reactance
E5C06 ECLM Page (4 - 16)

## Slide 64: What does the impedance 50 – j25 represent?
A. 50 ohms resistance in series with 25 ohms inductive reactance
B. 50 ohms resistance in series with 25 ohms capacitive reactance
C. 25 ohms resistance in series with 50 ohms inductive reactance
D. 25 ohms resistance in series with 50 ohms capacitive reactance
(B) E5C06 ECLM Page (4 - 16)

## Slide 65: Where is the impedance of a pure resistance plotted on rectangular coordinates?
A. On the vertical axis
B. On a line through the origin, slanted at 45 degrees
C. On a horizontal line, offset vertically above the horizontal axis
D. On the horizontal axis
E5C07 ECLM Page (4 - 16)

## Slide 66: Where is the impedance of a pure resistance plotted on rectangular coordinates?
A. On the vertical axis
B. On a line through the origin, slanted at 45 degrees
C. On a horizontal line, offset vertically above the horizontal axis
D. On the horizontal axis
(D) E5C07 ECLM Page (4 - 16)

## Slide 67: What coordinate system is often used to display the phase angle of a circuit containing resistance, inductive and/or capacitive reactance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Polar coordinates
E5C08 ECLM Page (4 - 16)

## Slide 68: What coordinate system is often used to display the phase angle of a circuit containing resistance, inductive and/or capacitive reactance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Polar coordinates
(D) E5C08 ECLM Page (4 - 16)

## Slide 69: When using rectangular coordinates to graph the impedance of a circuit, what do the axes represent?
A. The X axis represents the resistive component and the Y axis represents the reactive component
B. The X axis represents the reactive component and the Y axis represents the resistive component
C. The X axis represents the phase angle and the Y axis represents the magnitude
D. The X axis represents the magnitude and the Y axis represents the phase angle
E5C09 ECLM Page (4 - 16)

## Slide 70: When using rectangular coordinates to graph the impedance of a circuit, what do the axes represent?
A. The X axis represents the resistive component and the Y axis represents the reactive component
B. The X axis represents the reactive component and the Y axis represents the resistive component
C. The X axis represents the phase angle and the Y axis represents the magnitude
D. The X axis represents the magnitude and the Y axis represents the phase angle
(A) E5C09 ECLM Page (4 - 16)

## Slide 71: Which point on Figure E5-1 best represents the impedance of a series circuit consisting of a 400-ohm resistor and a 38-picofarad capacitor at 14 MHz?
A. Point 2
B. Point 4
C. Point 5
D. Point 6
E5C10 ECLM Page (4 - 21)

## Slide 72: Which point on Figure E5-1 best represents the impedance of a series circuit consisting of a 400-ohm resistor and a 38-picofarad capacitor at 14 MHz?
A. Point 2
B. Point 4
C. Point 5
D. Point 6
(B) E5C10 ECLM Page (4 - 21)

## Slide 73: Which point in Figure E5-1 best represents the impedance of a series circuit consisting of a 300-ohm resistor and an 18-microhenry inductor at 3.505 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8
E5C11 ECLM Page (4 - 20)

## Slide 74: Which point in Figure E5-1 best represents the impedance of a series circuit consisting of a 300-ohm resistor and an 18-microhenry inductor at 3.505 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8
(B) E5C11 ECLM Page (4 - 20)

## Slide 75: Which point on Figure E5-1 best represents the impedance of a series circuit consisting of a 300-ohm resistor and a 19-picofarad capacitor at 21.200 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8
E5C12 ECLM Page (4 - 22)

## Slide 76: Which point on Figure E5-1 best represents the impedance of a series circuit consisting of a 300-ohm resistor and a 19-picofarad capacitor at 21.200 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8
(A) E5C12 ECLM Page (4 - 22)