## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is the result of skin effect?
A. As frequency increases, RF current flows in a thinner layer of the conductor, closer to the surface
B. As frequency decreases, RF current flows in a thinner layer of the conductor, closer to the surface
C. Thermal effects on the surface of the conductor increase the impedance
D. Thermal effects on the surface of the conductor decrease the impedance
E5D01 ECLM Page (4 - 33)

## Slide 4: What is the result of skin effect?
A. As frequency increases, RF current flows in a thinner layer of the conductor, closer to the surface
B. As frequency decreases, RF current flows in a thinner layer of the conductor, closer to the surface
C. Thermal effects on the surface of the conductor increase the impedance
D. Thermal effects on the surface of the conductor decrease the impedance
(A) E5D01 ECLM Page (4 - 33)

## Slide 5: Why is it important to keep lead lengths short for components used in circuits for VHF and above?
A. To increase the thermal time constant
B. To avoid unwanted inductive reactance
C. To maintain component lifetime
D. All these choices are correct
E5D02 ECLM Page (4 - 35)

## Slide 6: Why is it important to keep lead lengths short for components used in circuits for VHF and above?
A. To increase the thermal time constant
B. To avoid unwanted inductive reactance
C. To maintain component lifetime
D. All these choices are correct
(B) E5D02 ECLM Page (4 - 35)

## Slide 7: What is the phase relationship between current and voltage for reactive power?
A. They are out of phase
B. They are in phase
C. They are 90 degrees out of phase
D. They are 45 degrees out of phase
E5D03 ECLM Page (5 - 13)

## Slide 8: What is the phase relationship between current and voltage for reactive power?
A. They are out of phase
B. They are in phase
C. They are 90 degrees out of phase
D. They are 45 degrees out of phase
(C) E5D03 ECLM Page (5 - 13)

## Slide 9: Why are short connections used at microwave frequencies?
A. To increase neutralizing resistance
B. To reduce phase shift along the connection
C. To increase compensating capacitance
D. To reduce noise figure
E5D04 ECLM Page (4 - 35)

## Slide 10: Why are short connections used at microwave frequencies?
A. To increase neutralizing resistance
B. To reduce phase shift along the connection
C. To increase compensating capacitance
D. To reduce noise figure
(B) E5D04 ECLM Page (4 - 35)

## Slide 11: What parasitic characteristic causes electrolytic capacitors to be unsuitable for use at RF?
A. Skin effect
B. Shunt capacitance
C. Inductance
D. Dielectric leakage
E5D05 ECLM Page (4 - 26)

## Slide 12: What parasitic characteristic causes electrolytic capacitors to be unsuitable for use at RF?
A. Skin effect
B. Shunt capacitance
C. Inductance
D. Dielectric leakage
(C) E5D05 ECLM Page (4 - 26)

## Slide 13: What parasitic characteristic creates an inductor’s self-resonance?
A. Skin effect
B. Dielectric loss
C. Coupling
D. Inter-turn capacitance
E5D06 ECLM Page (4 - 7)

## Slide 14: What parasitic characteristic creates an inductor’s self-resonance?
A. Skin effect
B. Dielectric loss
C. Coupling
D. Inter-turn capacitance
(D) E5D06 ECLM Page (4 - 7)

## Slide 15: What combines to create the self-resonance of a component?
A. The component’s resistance and reactance
B. The component’s nominal and parasitic reactance
C. The component’s inductance and capacitance
D. The component’s electrical length and impedance
E5D07 ECLM Page (4 - 26)

## Slide 16: What combines to create the self-resonance of a component?
A. The component’s resistance and reactance
B. The component’s nominal and parasitic reactance
C. The component’s inductance and capacitance
D. The component’s electrical length and impedance
(B) E5D07 ECLM Page (4 - 26)

## Slide 17: What is the primary cause of loss in film capacitors at RF?
A. Inductance
B. Dielectric loss
C. Self-discharge
D. Skin effect
E5D08 ECLM Page (4 - 26)

## Slide 18: What is the primary cause of loss in film capacitors at RF?
A. Inductance
B. Dielectric loss
C. Self-discharge
D. Skin effect
(D) E5D08 ECLM Page (4 - 26)

## Slide 19: What happens to reactive power in ideal inductors and capacitors?
A. It is dissipated as heat in the circuit
B. Energy is stored in magnetic or electric fields, but power is not dissipated
C. It is canceled by Coulomb forces in the capacitor and inductor
D. It is dissipated in the formation of inductive and capacitive fields
E5D09 ECLM Page (4 - 24)

## Slide 20: What happens to reactive power in ideal inductors and capacitors?
A. It is dissipated as heat in the circuit
B. Energy is stored in magnetic or electric fields, but power is not dissipated
C. It is canceled by Coulomb forces in the capacitor and inductor
D. It is dissipated in the formation of inductive and capacitive fields
(B) E5D09 ECLM Page (4 - 24)

## Slide 21: As a conductor’s diameter increases, what is the effect on its electrical length?
A. Thickness has no effect on electrical length
B. It varies randomly
C. It decreases
D. It increases
E5D10 ECLM Page (4 - 25)

## Slide 22: As a conductor’s diameter increases, what is the effect on its electrical length?
A. Thickness has no effect on electrical length
B. It varies randomly
C. It decreases
D. It increases
(D) E5D10 ECLM Page (4 - 25)

## Slide 23: How much real power is consumed in a circuit consisting of a 100-ohm resistor in series with a 100-ohm inductive reactance drawing 1 ampere?
A. 70.7 watts
B. 100 watts
C. 141.4 watts
D. 200 watts
E5D11 ECLM Page (4 - 26)

## Slide 24: How much real power is consumed in a circuit consisting of a 100-ohm resistor in series with a 100-ohm inductive reactance drawing 1 ampere?
A. 70.7 watts
B. 100 watts
C. 141.4 watts
D. 200 watts
(B) E5D11 ECLM Page (4 - 26)

## Slide 25: What is reactive power?
A. Power consumed in circuit Q
B. Power consumed by an inductor’s wire resistance
C. The power consumed in inductors and capacitors
D. Wattless, nonproductive power
E5D12 ECLM Page (4 - 26)

## Slide 26: What is reactive power?
A. Power consumed in circuit Q
B. Power consumed by an inductor’s wire resistance
C. The power consumed in inductors and capacitors
D. Wattless, nonproductive power
(D) E5D12 ECLM Page (4 - 26)