## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: How much does the gain of an ideal parabolic dish antenna change when the operating frequency is doubled?
A. 2 dB
B. 3 dB
C. 4 dB
D. 6 dB
E9D01 ECLM Page (9 - 19)

## Slide 4: How much does the gain of an ideal parabolic dish antenna change when the operating frequency is doubled?
A. 2 dB
B. 3 dB
C. 4 dB
D. 6 dB
(D) E9D01 ECLM Page (9 - 19)

## Slide 5: How can two linearly polarized Yagi antennas be used to produce circular polarization?
A. Stack two Yagis to form an array with the respective elements in parallel planes fed 90 degrees out of phase
B. Stack two Yagis to form an array with the respective elements in parallel planes fed in phase
C. Arrange two Yagis on the same axis and perpendicular to each other with the driven elements at the same point on the boom and fed 90 degrees out of phase
D. Arrange two Yagis collinear to each other with the driven elements fed 180 degrees out of phase
E9D02 ECLM Page (9 - 19)

## Slide 6: How can two linearly polarized Yagi antennas be used to produce circular polarization?
A. Stack two Yagis to form an array with the respective elements in parallel planes fed 90 degrees out of phase
B. Stack two Yagis to form an array with the respective elements in parallel planes fed in phase
C. Arrange two Yagis on the same axis and perpendicular to each other with the driven elements at the same point on the boom and fed 90 degrees out of phase
D. Arrange two Yagis collinear to each other with the driven elements fed 180 degrees out of phase
(C) E9D02 ECLM Page (9 - 19)

## Slide 7: What is the most efficient location for a loading coil on an electrically short whip?
A. Near the center of the vertical radiator
B. As low as possible on the vertical radiator
C. At a voltage maximum
D. At a voltage null
E9D03 ECLM Page (9 - 13)

## Slide 8: What is the most efficient location for a loading coil on an electrically short whip?
A. Near the center of the vertical radiator
B. As low as possible on the vertical radiator
C. At a voltage maximum
D. At a voltage null
(A) E9D03 ECLM Page (9 - 13)

## Slide 9: Why should antenna loading coils have a high ratio of reactance to resistance?
A. To swamp out harmonics
B. To lower the radiation angle
C. To minimize losses
D. To minimize the Q
E9D04 ECLM Page (9 - 13)

## Slide 10: Why should antenna loading coils have a high ratio of reactance to resistance?
A. To swamp out harmonics
B. To lower the radiation angle
C. To minimize losses
D. To minimize the Q
(C) E9D04 ECLM Page (9 - 13)

## Slide 11: Approximately how long is a Yagi’s driven element?
A. 234 divided by frequency in MHz
B. 1005 divided by frequency in MHz
C. 1/4 wavelength
D. 1/2 wavelength
E9D05 ECLM Page (9 - 42)

## Slide 12: Approximately how long is a Yagi’s driven element?
A. 234 divided by frequency in MHz
B. 1005 divided by frequency in MHz
C. 1/4 wavelength
D. 1/2 wavelength
(D) E9D05 ECLM Page (9 - 42)

## Slide 13: What happens to the SWR bandwidth when one or more loading coils are used to resonate an electrically short antenna?
A. It is increased
B. It is decreased
C. It is unchanged if the loading coil is located at the feed point
D. It is unchanged if the loading coil is located at a voltage maximum point
E9D06 ECLM Page (9 - 13)

## Slide 14: What happens to the SWR bandwidth when one or more loading coils are used to resonate an electrically short antenna?
A. It is increased
B. It is decreased
C. It is unchanged if the loading coil is located at the feed point
D. It is unchanged if the loading coil is located at a voltage maximum point
(B) E9D06 ECLM Page (9 - 13)

## Slide 15: What is an advantage of using top loading in a shortened HF vertical antenna?
A. Lower Q
B. Greater structural strength
C. Higher losses
D. Improved radiation efficiency
E9D07 ECLM Page (9 - 13)

## Slide 16: What is an advantage of using top loading in a shortened HF vertical antenna?
A. Lower Q
B. Greater structural strength
C. Higher losses
D. Improved radiation efficiency
(D) E9D07 ECLM Page (9 - 13)

## Slide 17: What happens as the Q of an antenna increases?
A. SWR bandwidth increases
B. SWR bandwidth decreases
C. Gain is reduced
D. More common-mode current is present on the feed line
E9D08 ECLM Page (9 - 8)

## Slide 18: What happens as the Q of an antenna increases?
A. SWR bandwidth increases
B. SWR bandwidth decreases
C. Gain is reduced
D. More common-mode current is present on the feed line
(B) E9D08 ECLM Page (9 - 8)

## Slide 19: What is the function of a loading coil in an electrically short antenna?
A. To increase the SWR bandwidth by increasing net reactance
B. To lower the losses
C. To lower the Q
D. To resonate the antenna by cancelling the capacitive reactance
E9D09 ECLM Page (9 - 12)

## Slide 20: What is the function of a loading coil in an electrically short antenna?
A. To increase the SWR bandwidth by increasing net reactance
B. To lower the losses
C. To lower the Q
D. To resonate the antenna by cancelling the capacitive reactance
(D) E9D09 ECLM Page (9 - 12)

## Slide 21: How does radiation resistance of a base-fed whip antenna change below its resonant frequency?
A. Radiation resistance increases
B. Radiation resistance decreases
C. Radiation resistance becomes imaginary
D. Radiation resistance does not depend on frequency
E9D10 ECLM Page (9 - 12)

## Slide 22: How does radiation resistance of a base-fed whip antenna change below its resonant frequency?
A. Radiation resistance increases
B. Radiation resistance decreases
C. Radiation resistance becomes imaginary
D. Radiation resistance does not depend on frequency
(B) E9D10 ECLM Page (9 - 12)

## Slide 23: Why do most two-element Yagis with normal spacing have a reflector instead of a director?
A. Lower SWR
B. Higher receiving directivity factor
C. Greater front-to-side
D. Higher gain
E9D11 ECLM Page (9 - 9)

## Slide 24: Why do most two-element Yagis with normal spacing have a reflector instead of a director?
A. Lower SWR
B. Higher receiving directivity factor
C. Greater front-to-side
D. Higher gain
(D) E9D11 ECLM Page (9 - 9)

## Slide 25: What is the purpose of making a Yagi’s parasitic elements either longer or shorter than resonance?
A. Wind torque cancellation
B. Mechanical balance
C. Control of phase shift
D. Minimize losses
E9D12 ECLM Page (9 - 9)

## Slide 26: What is the purpose of making a Yagi’s parasitic elements either longer or shorter than resonance?
A. Wind torque cancellation
B. Mechanical balance
C. Control of phase shift
D. Minimize losses
(C) E9D12 ECLM Page (9 - 9)

## Slide 27: Which matching system for Yagi antennas requires the driven element to be insulated from the boom?
A. Gamma
B. Beta or hairpin
C. Shunt-fed
D. T-match
E9E01 ECLM Page (9 - 25)

## Slide 28: Which matching system for Yagi antennas requires the driven element to be insulated from the boom?
A. Gamma
B. Beta or hairpin
C. Shunt-fed
D. T-match
(B) E9E01 ECLM Page (9 - 25)

## Slide 29: What antenna matching system matches coaxial cable to an antenna by connecting the shield to the center of the antenna and the conductor a fraction of a wavelength to one side?
A. Gamma match
B. Delta match
C. T-match
D. Stub match
E9E02 ECLM Page (9 - 25)

## Slide 30: What antenna matching system matches coaxial cable to an antenna by connecting the shield to the center of the antenna and the conductor a fraction of a wavelength to one side?
A. Gamma match
B. Delta match
C. T-match
D. Stub match
(A) E9E02 ECLM Page (9 - 25)

## Slide 31: What matching system uses a short length of transmission line connected in parallel with the feed line at or near the feed point?
A. Gamma match
B. Delta match
C. T-match
D. Stub match
E9E03 ECLM Page (9 - 26)

## Slide 32: What matching system uses a short length of transmission line connected in parallel with the feed line at or near the feed point?
A. Gamma match
B. Delta match
C. T-match
D. Stub match
(D) E9E03 ECLM Page (9 - 26)

## Slide 33: What is the purpose of the series capacitor in a gamma match?
A. To provide DC isolation between the feed line and the antenna
B. To cancel unwanted inductive reactance
C. To provide a rejection notch that prevents the radiation of harmonics
D. To transform the antenna impedance to a higher value
E9E04 ECLM Page (9 - 26)

## Slide 34: What is the purpose of the series capacitor in a gamma match?
A. To provide DC isolation between the feed line and the antenna
B. To cancel unwanted inductive reactance
C. To provide a rejection notch that prevents the radiation of harmonics
D. To transform the antenna impedance to a higher value
(B) E9E04 ECLM Page (9 - 26)

## Slide 35: What Yagi driven element feed point impedance is required to use a beta or hairpin matching system?
A. Capacitive (driven element electrically shorter than 1/2 wavelength)
B. Inductive (driven element electrically longer than 1/2 wavelength)
C. Purely resistive
D. Purely reactive
E9E05 ECLM Page (9 - 38)

## Slide 36: What Yagi driven element feed point impedance is required to use a beta or hairpin matching system?
A. Capacitive (driven element electrically shorter than 1/2 wavelength)
B. Inductive (driven element electrically longer than 1/2 wavelength)
C. Purely resistive
D. Purely reactive
(A) E9E05 ECLM Page (9 - 38)

## Slide 37: Which of these transmission line impedances would be suitable for constructing a quarter-wave Q-section for matching a 100-ohm feed point impedance to a 50-ohm transmission line?
A. 50 ohms
B. 62 ohms
C. 75 ohms
D. 90 ohms
E9E06 ECLM Page (9 - 38)

## Slide 38: Which of these transmission line impedances would be suitable for constructing a quarter-wave Q-section for matching a 100-ohm feed point impedance to a 50-ohm transmission line?
A. 50 ohms
B. 62 ohms
C. 75 ohms
D. 90 ohms
(C) E9E06 ECLM Page (9 - 38)

## Slide 39: What parameter describes the interactions at the load end of a mismatched transmission line?
A. Characteristic impedance
B. Reflection coefficient
C. Velocity factor
D. Dielectric constant
E9E07 ECLM Page (9 - 31)

## Slide 40: What parameter describes the interactions at the load end of a mismatched transmission line?
A. Characteristic impedance
B. Reflection coefficient
C. Velocity factor
D. Dielectric constant
(B) E9E07 ECLM Page (9 - 31)

## Slide 41: What is a use for a Wilkinson divider?
A. It divides the operating frequency of a transmitter signal so it can be used on a lower frequency band
B. It is used to feed high-impedance antennas from a low-impedance source
C. It is used to divide power equally between two 50-ohm loads while maintaining 50-ohm input impedance
D. It is used to feed low-impedance loads from a high-impedance source
E9E08 ECLM Page (9 - 18)

## Slide 42: What is a use for a Wilkinson divider?
A. It divides the operating frequency of a transmitter signal so it can be used on a lower frequency band
B. It is used to feed high-impedance antennas from a low-impedance source
C. It is used to divide power equally between two 50-ohm loads while maintaining 50-ohm input impedance
D. It is used to feed low-impedance loads from a high-impedance source
(C) E9E08 ECLM Page (9 - 18)

## Slide 43: Which of the following is used to shunt-feed a grounded tower at its base?
A. Double-bazooka match
B. Hairpin match
C. Gamma match
D. All these choices are correct
E9E09 ECLM Page (9 - 9)

## Slide 44: Which of the following is used to shunt-feed a grounded tower at its base?
A. Double-bazooka match
B. Hairpin match
C. Gamma match
D. All these choices are correct
(C) E9E09 ECLM Page (9 - 9)

## Slide 45: E9E10 Question Deleted (section not renumbered)

## Slide 46: What is the purpose of using multiple driven elements connected through phasing lines?
A. To control the antenna’s radiation pattern
B. To prevent harmonic radiation from the transmitter
C. To allow single-band antennas to operate on other bands
D. To create a low-angle radiation pattern
E9E11 ECLM Page (9 - 18)

## Slide 47: What is the purpose of using multiple driven elements connected through phasing lines?
A. To control the antenna’s radiation pattern
B. To prevent harmonic radiation from the transmitter
C. To allow single-band antennas to operate on other bands
D. To create a low-angle radiation pattern
(A) E9E11 ECLM Page (9 - 18)

## Slide 48: What is the velocity factor of a transmission line?
A. The ratio of the characteristic impedance of the line to the terminating impedance
B. The index of shielding for coaxial cable
C. The velocity of the wave in the transmission line multiplied by the velocity of light in a vacuum
D. The velocity of the wave in the transmission line divided by the velocity of light in a vacuum
E9F01 ECLM Page (9 - 28)

## Slide 49: What is the velocity factor of a transmission line?
A. The ratio of the characteristic impedance of the line to the terminating impedance
B. The index of shielding for coaxial cable
C. The velocity of the wave in the transmission line multiplied by the velocity of light in a vacuum
D. The velocity of the wave in the transmission line divided by the velocity of light in a vacuum
(D) E9F01 ECLM Page (9 - 28)

## Slide 50: Which of the following has the biggest effect on the velocity factor of a transmission line?
A. The termination impedance
B. The line length
C. Dielectric materials used in the line
D. The center conductor resistivity
E9F02 ECLM Page (9 - 28)

## Slide 51: Which of the following has the biggest effect on the velocity factor of a transmission line?
A. The termination impedance
B. The line length
C. Dielectric materials used in the line
D. The center conductor resistivity
(C) E9F02 ECLM Page (9 - 28)

## Slide 52: Why is the electrical length of a coaxial cable longer than its physical length?
A. Skin effect is less pronounced in the coaxial cable
B. Skin effect is more pronounced in the coaxial cable
C. Electromagnetic waves move faster in coaxial cable than in air
D. Electromagnetic waves move more slowly in a coaxial cable than in air
E9F03 ECLM Page (9 - 29)

## Slide 53: Why is the electrical length of a coaxial cable longer than its physical length?
A. Skin effect is less pronounced in the coaxial cable
B. Skin effect is more pronounced in the coaxial cable
C. Electromagnetic waves move faster in coaxial cable than in air
D. Electromagnetic waves move more slowly in a coaxial cable than in air
(D) E9F03 ECLM Page (9 - 29)

## Slide 54: What impedance does a 1/2-wavelength transmission line present to an RF generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the line
D. The same as the output impedance of the generator
E9F04 ECLM Page (9 - 36)

## Slide 55: What impedance does a 1/2-wavelength transmission line present to an RF generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the line
D. The same as the output impedance of the generator
(B) E9F04 ECLM Page (9 - 36)

## Slide 56: What is microstrip?
A. Special shielding material designed for microwave frequencies
B. Miniature coax used for low power applications
C. Short lengths of coax mounted on printed circuit boards to minimize time delay between microwave circuits
D. Precision printed circuit conductors above a ground plane that provide constant impedance interconnects at microwave frequencies
E9F05 ECLM Page (9 - 29)

## Slide 57: What is microstrip?
A. Special shielding material designed for microwave frequencies
B. Miniature coax used for low power applications
C. Short lengths of coax mounted on printed circuit boards to minimize time delay between microwave circuits
D. Precision printed circuit conductors above a ground plane that provide constant impedance interconnects at microwave frequencies
(D) E9F05 ECLM Page (9 - 29)

## Slide 58: What is the approximate physical length of an air-insulated, parallel conductor transmission line that is electrically 1/2 wavelength long at 14.10 MHz?
A. 7.0 meters
B. 8.5 meters
C. 10.6 meters
D. 13.3 meters
E9F06 ECLM Page (9 - 30)

## Slide 59: What is the approximate physical length of an air-insulated, parallel conductor transmission line that is electrically 1/2 wavelength long at 14.10 MHz?
A. 7.0 meters
B. 8.5 meters
C. 10.6 meters
D. 13.3 meters
(C) E9F06 ECLM Page (9 - 30)

## Slide 60: How does parallel conductor transmission line compare to coaxial cable with a plastic dielectric?
A. Lower loss
B. Higher SWR
C. Smaller reflection coefficient
D. Lower velocity factor
E9F07 ECLM Page (9 - 30)

## Slide 61: How does parallel conductor transmission line compare to coaxial cable with a plastic dielectric?
A. Lower loss
B. Higher SWR
C. Smaller reflection coefficient
D. Lower velocity factor
(A) E9F07 ECLM Page (9 - 30)

## Slide 62: Which of the following is a significant difference between foam dielectric coaxial cable and solid dielectric cable, assuming all other parameters are the same?
A. Foam dielectric has lower safe operating voltage limits
B. Foam dielectric has lower loss per unit of length
C. Foam dielectric has higher velocity factor
D. All these choices are correct
E9F08 ECLM Page (9 - 31)

## Slide 63: Which of the following is a significant difference between foam dielectric coaxial cable and solid dielectric cable, assuming all other parameters are the same?
A. Foam dielectric has lower safe operating voltage limits
B. Foam dielectric has lower loss per unit of length
C. Foam dielectric has higher velocity factor
D. All these choices are correct
(D) E9F08 ECLM Page (9 - 31)

## Slide 64: What impedance does a 1/4-wavelength transmission line present to an RF generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the transmission line
D. The same as the generator output impedance
E9F09 ECLM Page (9 - 29)

## Slide 65: What impedance does a 1/4-wavelength transmission line present to an RF generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the transmission line
D. The same as the generator output impedance
(A) E9F09 ECLM Page (9 - 29)

## Slide 66: What impedance does a 1/8-wavelength transmission line present to an RF generator when the line is shorted at the far end?
A. A capacitive reactance
B. The same as the characteristic impedance of the line
C. An inductive reactance
D. Zero
E9F10 ECLM Page (9 - 37)

## Slide 67: What impedance does a 1/8-wavelength transmission line present to an RF generator when the line is shorted at the far end?
A. A capacitive reactance
B. The same as the characteristic impedance of the line
C. An inductive reactance
D. Zero
(C) E9F10 ECLM Page (9 - 37)

## Slide 68: What impedance does a 1/8-wavelength transmission line present to an RF generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. An inductive reactance
C. A capacitive reactance
D. Infinite
E9F11 ECLM Page (9 - 36)

## Slide 69: What impedance does a 1/8-wavelength transmission line present to a generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. An inductive reactance
C. A capacitive reactance
D. Infinite
(C) E9F11 ECLM Page (9 - 36)

## Slide 70: What impedance does a 1/4-wavelength transmission line present to an RF generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. The same as the input impedance to the generator
C. Very high impedance
D. Very low impedance
E9F12 ECLM Page (9 - 36)

## Slide 71: What impedance does a 1/4-wavelength transmission line present to an RF generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. The same as the input impedance to the generator
C. Very high impedance
D. Very low impedance
(D) E9F12 ECLM Page (9 - 36)