## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Which of the following can be calculated using a Smith chart?
A. Impedance along transmission lines
B. Radiation resistance
C. Antenna radiation pattern
D. Radio propagation
E9G01 ECLM Page (9 - 33)

## Slide 4: Which of the following can be calculated using a Smith chart?
A. Impedance along transmission lines
B. Radiation resistance
C. Antenna radiation pattern
D. Radio propagation
(A) E9G01 ECLM Page (9 - 33)

## Slide 5: What type of coordinate system is used in a Smith chart?
A. Voltage circles and current arcs
B. Resistance circles and reactance arcs
C. Voltage lines and current chords
D. Resistance lines and reactance chords
E9G02 ECLM Page (9 - 35)

## Slide 6: What type of coordinate system is used in a Smith chart?
A. Voltage circles and current arcs
B. Resistance circles and reactance arcs
C. Voltage lines and current chords
D. Resistance lines and reactance chords
(B) E9G02 ECLM Page (9 - 35)

## Slide 7: Which of the following is often determined using a Smith chart?
A. Beam headings and radiation patterns
B. Satellite azimuth and elevation bearings
C. Impedance and SWR values in transmission lines
D. Trigonometric functions
E9G03 ECLM Page (9 - 33)

## Slide 8: Which of the following is often determined using a Smith chart?
A. Beam headings and radiation patterns
B. Satellite azimuth and elevation bearings
C. Impedance and SWR values in transmission lines
D. Trigonometric functions
(C) E9G03 ECLM Page (9 - 33)

## Slide 9: What are the two families of circles and arcs that make up a Smith chart?
A. Resistance and voltage
B. Reactance and voltage
C. Resistance and reactance
D. Voltage and impedance
E9G04 ECLM Page (9 - 35)

## Slide 10: What are the two families of circles and arcs that make up a Smith chart?
A. Resistance and voltage
B. Reactance and voltage
C. Resistance and reactance
D. Voltage and impedance
(C) E9G04 ECLM Page (9 - 35)

## Slide 11: Which of the following is a common use for a Smith chart?
A. Determine the length and position of an impedance matching stub
B. Determine the impedance of a transmission line, given the physical dimensions
C. Determine the gain of an antenna given the physical and electrical parameters
D. Determine the loss/100 feet of a transmission line, given the velocity factor and conductor materials
E9G05 ECLM Page (9 - 27)

## Slide 12: Which of the following is a common use for a Smith chart?
A. Determine the length and position of an impedance matching stub
B. Determine the impedance of a transmission line, given the physical dimensions
C. Determine the gain of an antenna given the physical and electrical parameters
D. Determine the loss/100 feet of a transmission line, given the velocity factor and conductor materials
(A) E9G05 ECLM Page (9 - 27)

## Slide 13: On the Smith chart shown in Figure E9-3, what is the name for the large outer circle on which the reactance arcs terminate?
A. Prime axis
B. Reactance axis
C. Impedance axis
D. Polar axis
E9G06 ECLM Page (9 - 35)

## Slide 14: On the Smith chart shown in Figure E9-3, what is the name for the large outer circle on which the reactance arcs terminate?
A. Prime axis
B. Reactance axis
C. Impedance axis
D. Polar axis
(B) E9G06 ECLM Page (9 - 35)

## Slide 15: On the Smith chart shown in Figure E9-3, what is the only straight line shown?
A. The reactance axis
B. The current axis
C. The voltage axis
D. The resistance axis
E9G07 ECLM Page (9 - 33)

## Slide 16: On the Smith chart shown in Figure E9-3, what is the only straight line shown?
A. The reactance axis
B. The current axis
C. The voltage axis
D. The resistance axis
(D) E9G07 ECLM Page (9 - 33)

## Slide 17: How is a Smith chart normalized?
A. Reassign the reactance axis with resistance values
B. Reassign the resistance axis with reactance values
C. Reassign the prime center’s impedance value
D. Reassign the prime center to the reactance axis
E9G08 ECLM Page (9 - 35)

## Slide 18: How is a Smith chart normalized?
A. Reassign the reactance axis with resistance values
B. Reassign the resistance axis with reactance values
C. Reassign the prime center’s impedance value
D. Reassign the prime center to the reactance axis
(C) E9G08 ECLM Page (9 - 35)

## Slide 19: What third family of circles is often added to a Smith chart during the process of solving problems?
A. Standing-wave ratio circles
B. Antenna-length circles
C. Coaxial-length circles
D. Radiation-pattern circles
E9G09 ECLM Page (9 - 35)

## Slide 20: What third family of circles is often added to a Smith chart during the process of solving problems?
A. Standing-wave ratio circles
B. Antenna-length circles
C. Coaxial-length circles
D. Radiation-pattern circles
(A) E9G09 ECLM Page (9 - 35)

## Slide 21: What do the arcs on a Smith chart represent?
A. Frequency
B. SWR
C. Points with constant resistance
D. Points with constant reactance
E9G10 ECLM Page (9 - 35)

## Slide 22: What do the arcs on a Smith chart represent?
A. Frequency
B. SWR
C. Points with constant resistance
D. Points with constant reactance
(D) E9G10 ECLM Page (9 - 35)

## Slide 23: In what units are the wavelength scales on a Smith chart calibrated?
A. In fractions of transmission line electrical frequency
B. In fractions of transmission line electrical wavelength
C. In fractions of antenna electrical wavelength
D. In fractions of antenna electrical frequency
E9G11 ECLM Page (9 - 35)

## Slide 24: In what units are the wavelength scales on a Smith chart calibrated?
A. In fractions of transmission line electrical frequency
B. In fractions of transmission line electrical wavelength
C. In fractions of antenna electrical wavelength
D. In fractions of antenna electrical frequency
(B) E9G11 ECLM Page (9 - 35)

## Slide 25: When constructing a Beverage antenna, which of the following factors should be included in the design to achieve good performance at the desired frequency?
A. Its overall length must not exceed 1/4 wavelength
B. It must be mounted more than 1 wavelength above ground
C. It should be configured as a four-sided loop
D. It should be one or more wavelengths long
E9H01 ECLM Page (9 - 15)

## Slide 26: When constructing a Beverage antenna, which of the following factors should be included in the design to achieve good performance at the desired frequency?
A. Its overall length must not exceed 1/4 wavelength
B. It must be mounted more than 1 wavelength above ground
C. It should be configured as a four-sided loop
D. It should be one or more wavelengths long
(D) E9H01 ECLM Page (9 - 15)

## Slide 27: Which is generally true for 160- and 80-meter receiving antennas?
A. Atmospheric noise is so high that directivity is much more important than losses
B. They must be erected at least 1/2 wavelength above the ground to attain good directivity
C. Low loss coax transmission line is essential for good performance
D. All these choices are correct
E9H02 ECLM Page (9 - 15)

## Slide 28: Which is generally true for 160- and 80-meter receiving antennas?
A. Atmospheric noise is so high that directivity is much more important than losses
B. They must be erected at least 1/2 wavelength above the ground to attain good directivity
C. Low loss coax transmission line is essential for good performance
D. All these choices are correct
(A) E9H02 ECLM Page (9 - 15)

## Slide 29: What is Receiving Directivity Factor (RDF)?
A. Forward gain compared to the gain in the reverse direction
B. Relative directivity compared to isotropic
C. Relative directivity compared to a dipole
D. Peak antenna gain compared to average gain over the hemisphere around and above the antenna
E9H03 ECLM Page (9 - 21)

## Slide 30: What is Receiving Directivity Factor (RDF)?
A. Forward gain compared to the gain in the reverse direction
B. Relative directivity compared to isotropic
C. Relative directivity compared to a dipole
D. Peak antenna gain compared to average gain over the hemisphere around and above the antenna
(D) E9H03 ECLM Page (9 - 21)

## Slide 31: What is the purpose of placing an electrostatic shield around a small-loop direction-finding antenna?
A. It adds capacitive loading, increasing the bandwidth of the antenna
B. It eliminates unbalanced capacitive coupling to the antenna’s surroundings, improving the depth of its nulls
C. It eliminates tracking errors caused by strong out-of-band signals
D. It increases signal strength by providing a better match to the feed line
E9H04 ECLM Page (9 - 20)

## Slide 32: What is the purpose of placing an electrostatic shield around a small-loop direction-finding antenna?
A. It adds capacitive loading, increasing the bandwidth of the antenna
B. It eliminates unbalanced capacitive coupling to the antenna’s surroundings, improving the depth of its nulls
C. It eliminates tracking errors caused by strong out-of-band signals
D. It increases signal strength by providing a better match to the feed line
(B) E9H04 ECLM Page (9 - 20)

## Slide 33: What challenge is presented by a small wire-loop antenna for direction finding?
A. It has a bidirectional null pattern
B. It does not have a clearly defined null
C. It is practical for use only on VHF and higher bands
D. All these choices are correct
E9H05 ECLM Page (9 - 20)

## Slide 34: What challenge is presented by a small wire-loop antenna for direction finding?
A. It has a bidirectional null pattern
B. It does not have a clearly defined null
C. It is practical for use only on VHF and higher bands
D. All these choices are correct
(A) E9H05 ECLM Page (9 - 20)

## Slide 35: What indicates the correct value of terminating resistance for a Beverage antenna?
A. Maximum feed point DC resistance at the center of the desired frequency range
B. Minimum low-angle front-to-back ratio at the design frequency
C. Maximum DC current in the terminating resistor
D. Minimum variation in SWR over the desired frequency range
E9H06 ECLM Page (9 - 22)

## Slide 36: What indicates the correct value of terminating resistance for a Beverage antenna?
A. Maximum feed point DC resistance at the center of the desired frequency range
B. Minimum low-angle front-to-back ratio at the design frequency
C. Maximum DC current in the terminating resistor
D. Minimum variation in SWR over the desired frequency range
(D) E9H06 ECLM Page (9 - 22)

## Slide 37: What is the function of a Beverage antenna’s termination resistor?
A. Increase the front-to-side ratio
B. Absorb signals from the reverse direction
C. Decrease SWR bandwidth
D. Eliminate harmonic reception
E9H07 ECLM Page (9 - 21)

## Slide 38: What is the function of a Beverage antenna’s termination resistor?
A. Increase the front-to-side ratio
B. Absorb signals from the reverse direction
C. Decrease SWR bandwidth
D. Eliminate harmonic reception
(B) E9H07 ECLM Page (9 - 21)

## Slide 39: What is the function of a sense antenna?
A. It modifies the pattern of a DF antenna array to provide a null in one direction
B. It increases the sensitivity of a DF antenna array
C. It allows DF antennas to receive signals at different vertical angles
D. It provides diversity reception that cancels multipath signals
E9H08 ECLM Page (9 - 20)

## Slide 40: What is the function of a sense antenna?
A. It modifies the pattern of a DF antenna array to provide a null in one direction
B. It increases the sensitivity of a DF antenna array
C. It allows DF antennas to receive signals at different vertical angles
D. It provides diversity reception that cancels multipath signals
(A) E9H08 ECLM Page (9 - 20)

## Slide 41: What type of radiation pattern is created by a single-turn, terminated loop such as a pennant antenna?
A. Cardioid
B. Bidirectional
C. Omnidirectional
D. Hyperbolic
E9H09 ECLM Page (9 - 21)

## Slide 42: What type of radiation pattern is created by a single-turn, terminated loop such as a pennant antenna?
A. Cardioid
B. Bidirectional
C. Omnidirectional
D. Hyperbolic
(A) E9H09 ECLM Page (9 - 21)

## Slide 43: How can the output voltage of a multiple-turn receiving loop antenna be increased?
A. By reducing the permeability of the loop shield
B. By utilizing high impedance wire for the coupling loop
C. By increasing the number of turns and/or the area enclosed by the loop
D. All these choices are correct
E9H10 ECLM Page (9 - 21)

## Slide 44: How can the output voltage of a multiple-turn receiving loop antenna be increased?
A. By reducing the permeability of the loop shield
B. By utilizing high impedance wire for the coupling loop
C. By increasing the number of turns and/or the area enclosed by the loop
D. All these choices are correct
(C) E9H10 ECLM Page (9 - 21)

## Slide 45: What feature of a cardioid pattern antenna makes it useful for direction finding?
A. A very sharp peak
B. A very sharp single null
C. Broad band response
D. High-radiation angle
E9H11 ECLM Page (9 - 20)

## Slide 46: What feature of a cardioid pattern antenna makes it useful for direction finding?
A. A very sharp peak
B. A very sharp single null
C. Broad band response
D. High-radiation angle
(B) E9H11 ECLM Page (9 - 20)