## Slide 1: Amateur Extra License Course
Instructors:
Rick-WØPC, John-NØHMZ, Jay-WØPS, Jim-N5MU, Ken-WØKAH, Gordon-AH6DA
Bob-ADØGF

## Slide 2: The College
Non Smoking Campus
Restroom – Down the hall to the right
Cell Phones – Take call outside classroom
Emergency Phones – End of hall & Classroom
Blue Light in Parking lot – Emergency Phone
Department of Public Safety – Will Escort
Trash – Cleanup after yourself (trash & recycle containers)

## Slide 3: Instructor Team
Rick Crockett – WØPC
John Lehnhoff – NØHMZ
Jim Richardson – N5MU
Ken Humbertson – WØKAH
Jay Underdown – WØPS
Gordon Deno – AH6DA
Bob Perrey - ADØGF

## Slide 4: Student Introduction
Introduce yourself
  Name & Call Sign?
  How did you hear of this class?
  How long have you been a ham?

## Slide 5: Credits
PowerPoint Side Material taken from an outline of “The Extra Class License Manual, 10th Edition
Graphics also are from the same textbook as well as the ARRL’s web site for Instructor material

## Slide 6: Class Format
Textbook: “The ARRL Extra Class License Manual, 10th Edition”
11 Chapters are divided into 9 groups
Reading assignments are the responsibility of the student! (If you miss a class keep reading up to schedule)
  The Extra Class means putting an EXTRA amount of study time
  Classroom discussion will not replace doing the assigned reading and homework

## Slide 7: Class Schedule
March 26 - Chapters 1 & 2 “Introduction” & “Operating Practice”
April 2 - Chapter 3 “Rules and Regulations”
April 9 - Chapter 4 “Electrical Principles”
April 16 - Chapter 5 “Components and Building Blocks”
April 23 - Chapter 6 “Electronic Circuits”
April 30 - Chapter 7 “Radio Signals and Measurements”
May 7 - Chapter 8 “Radio Modes and Measurements”
May 14 - Chapter 9 “Antennas and Feed Lines”
May 21 - Chapter 10 & 11 “Topics in Radio Propagation” & “Safety”
May 28 - VE Test Session (open to walk-ins)

## Slide 8: How to Use the Book
Read the Chapters as Assigned
Do the Practice Questions as called out in the reading
  Test Question by Chapter: http://www.arrl.org/files/file/Extra%20Class%20License%20Manual/ECLM%2010th%20edition/Studyguide%20%20FINAL.pdf
  Supplemental Information by Chapter: http://www.arrl.org/extra-class-license-manual

## Slide 9: How to Use The Book
Updates and Correction to the License Manual
  http://www.arrl.org/files/file/Extra%20Class%20License%20Manual/ECLM%2010th%20edition/Extra%20Class%20License%20Manual%2010th%20Edition%20-%20Supplement%20and%20Errata%20-%2030%20Nov%202013.pdf
Practice Exam Software CD Included
  Do practice exams by chapter (Demo)

## Slide 10: The Extra Class License
Greatest achievement in amateur licensing
All amateur frequencies are now available
  The best DX windows are available
You can have a special Extra Class Call Sign
Volunteer Examiner (VE) for all levels
Extra’s don’t have to be a Technical Guru
  Other may think you are so…

## Slide 11: Frequency Chart

## Slide 12: Operating Practices
DX Windows and Watering Holes (Table 2-1)
  The definition of DX depends on the bands on which you are operating
    VHF/UHF may be 50 to 100 miles away, beyond the radio horizon or Moon Bounce
    HF usually means working foreign countries
    HF is usually on the bottom of the bands
  “DX Windows” narrow range of frequencies reserved for weak signal or foreign stations calling only. US listens for DX (1.830 – 1.835 MHz)

## Slide 13: Operating Practices
Pileup Productivity
  You have to be able to hear the DX station before you start calling - Stay in Sync
    Timing is critical (many techniques)
    Say your full call sign twice using standard Phonetics
    Use short transmission (Language limitations)
  Operating Split (listen to instructions)
    Backing up to a band edge forces pile one direction
    Spreads out the pile of callers (working up 5)
  Listen for QSL information (QSL Manager)

## Slide 14: Operating Practices
Dxing Propagation
  You can’t work them if you can’t hear them
  Understanding propagation is crucial to Dxing success
  Sun Spot Cycle
  Day/Night Conditions
  Grayline
  Rapid Signal Fading (QSB) – just before going out
    (MUF) Maximum Usable Frequency is dropping
  Use Propagation Prediction Software - modeling

## Slide 15: Operating Practices
Contesting (Radio Sport) on the air events
  Making the maximum number of contacts within defined time limits and according to the rules.
  Competitive outlet
  Quickly achieve Awards (WAS, DXCC)
  Enhance operating efficiency (Honing Skills)
    Pull weak signals out
    Maintain log in the heat of battle
    Improve your own station and antenna system
    Improved score implies improved operating proficiency

## Slide 16: Operating a Contest
Good activity to learn about radio-frequency propagation and planning an operating strategy
Search & Pounce Method
  Tuning up and down a band for stations to contact
    Listen how to say the exchange
    Listen for the cadence of the calls and responses
  S&P is the easy way to get started Contesting

## Slide 17: Operating a Contest
Running a Frequency
  Maintaining control of a frequency
  Station calling CQ Contest or CQ Test
  Let others come to you
  Usually results in a larger total score
  Hard core contesters say “IF you aren’t running, you are loosing”

## Slide 18: Operating a Contest
Submitting a Contest Log
  Cabrillo Format is a standard for organizing information where the sponsor can check and score the QSOs.
  Each contest has a deadline for submitting a log file via email in a Cabrillo Format
  Contest participants are not require to submit a log
  Submitted contest logs to LoTW can earn awards

## Slide 19: Operating a Contest
  Using Spotting Networks:
  Contests entrants in the single operator category are usually required to do everything themselves
    Finding stations to contact including multipliers
    operating the radio
    logging
  The use of Spotting Networks during a contest to locate stations puts the operator in the “Assisted” entry classification. (i.e. Single Operator Assisted)
  Spotting Networks can not be use for self spotting

## Slide 20: Digital Mode Operating
Packet Radio
  Most often used on VHF/UHF FM using AFSK modulation at 1200 baud on 2-Meters
  Data is exchanged in frames using the AX.25 protocol standard
  HF Packet uses 300 baud with FSK of a SSB signal
  Hardware: Transceiver, TNC, Computer with terminal software

## Slide 21: Digital Mode Operating
Packet Cluster – DX spotting network uses a special type of bulleting board software
  System allows many station to be connected to the PacketCluster Host and communicate with each other to share “DX Spots”
  Information is retransmitted to all stations connected on the cluster

## Slide 22: Digital Mode Operation
PACSAT
  (LEO) Low Earth Orbit Satellites that are in a “sun synchronous” orbit
  Satellites function as a packet bulletin board store-and-forward system
  A station can upload a message to the satellite and another station can download the message when it’s in view

## Slide 23: Digital Mode Operating
APRS – Automatic Packet Reporting System
  Developed by Bob Bruninga, WB4APR
  Uses a common frequency nationally (144.390 MHz)
  Uses Standard Packet radio equipment plus a GPS
  Uses Packet radio beacon function transmitting station call sign and GPS position information
  Uses non-connected packet AX.25 to transmit short messages between stations. (Mostly on 2-Mtrs)
  Uses an Internet backbone that allows long distance communications (www.findu.com) using Igates

## Slide 24: Amateur Satellites
Satellites provide Amateurs a greatly increased communication range by using the repeaters, transponders, or store-and-forward equipment onboard Satellites orbiting the Earth
Most of the satellites can be accessed or used to relay signals with very modest equipment
More information at www.amsat.org

## Slide 25: Amateur Satellites
Understanding Satellite Orbits
  2 factors affect a body in orbit around the Earth
    Forward Motion – inertia keeps the body moving in a straight line direction
    Gravity tends to pull the body toward the Earth
    When inertia and gravity are balanced, the object’s path is a stable orbit around the Earth
    One Orbit is one complete revolution around the Earth

## Slide 26: Amateur Satellites
Understanding Satellite Orbits
  Johannes Kepler mathematically described the orbits of planets (3 Laws)
    Keplerian elements allow you to calculate the position of the satellite at any time
    Geostationary satellites stay in the same position over the earth. They are geosynchronous with the Earth’s orbit

## Slide 27: Amateur Satellites
Orbital Mechanics - Vocabulary
  Inclination is the angle of the satellite orbit with respect to the Earth (Fig. 2-6)
  Node is where the satellite’s orbit crosses the equator
  Assending Node is where it crosses the equator from south to north (assending pass)
  Descending node is the point where the orbit crosses the equator traveling from north to south (descending pass)
  Apogee is the greatest height
  Perigee is the point of least height

## Slide 28: Amateur Satellites
Faraday Rotation
  Satellite’s signal changes polarization as it passes through the ionosphere
  Best way to deal with Faraday rotation is to use a circular polarized antennas for both TX and RX
Spin Modulation
  Satellites are often stabilized by being spun about an axis like a gyroscope
  Spin Modulation is the Fairly rapid , pulsed signal fading happening when the spin axis is not pointing directly at your ground station

## Slide 29: Satellite Operation
Repeaters
  Satellite Repeater are like terrestrial repeaters
    Cross-band to avoid heavy cavity duplexers
Transponder is the name given to any linear translator that is installed in a satellite
  Transponder receive signals from an entire segment of a band are shifted to a new frequency range and retransmitted on a different band
  Multi Mode (SSB or CW) FM discouraged
  Limit ERP to allow as many signals to access the transponder
  Transponder are usually identified by “mode” (U/V, V/U, L/U, V/H, etc. Table 2.2)
Satellite Operating Frequencies (uplink/downlink) Fig. 2-9 and Table 2-2)

## Slide 30: Homework
Read Chapters through Chapter 3
Do the practice questions as called out in the textbook
Use the Practice Test CD to insure you are familiar with the test material.