## Slide 1: Chapter 3 Rules & Regulations

## Slide 2: Operating Standards
As an Extra class licensee, your growing experiences will expose you to a wider variety of operating situations and circumstances.
Most obvious new experiences will be with your new and exclusive HF operating privileges

## Slide 3: Operating Standards
Frequency and Emission Privileges
  Extra’s have all the amateur frequency privileges on all amateur bands (Table 3-1 & 3-2 for HF)
  Each different ITU Region has different amateur frequency privileges
  The USA is in Region 2, where Region 2 frequency rules apply

## Slide 4: Operating Standards
Special Restrictions:
  30-meter band is a secondary basis, limited to 200 watts, CW or Data only (USA)
  60-meter band is restricted to 5 channels on a secondary basis
    5 channel specified as center frequencies
    1.5 kHz SSB display offset
    2.8 kHz bandwidth
    USB only for phone
    100 watts ERP
    RTTY & Data, no automatic control
Figure 3-1
Pg. 3-5

## Slide 5: Operating Standards
Automatic Message Forwarding
  Amateurs are held accountable for any message transmitted from their station
  3rd party messages relayed are easy to follow
  Automatic forwarding does not allow control operators to screen every message
    FCC Rules were modified making the originating station primarily responsible
    1st relay station bears some responsibility, 2nd on none
    Discontinue forwarding the message if it violate FCC Rules

## Slide 6: Operating Standards
Races Operation
  An amateur radio service of amateur stations for civil defense communications during periods of local, regional or national civil emergencies
  RACES is a formal FCC service
    Amateurs are required to register with their local Civil Defense organization
    All amateur frequencies are available to stations participating in RACES operations
    RACES stations communicate with other RACES stations and other stations authorized by the civil defense official

## Slide 7: Station Restrictions
Operating Restrictions:
  Under certain conditions, the FCC may modify the terms of your license
    Interference between properly operating amateur stations and users of other license services (US Govt)
    General interference may result in “Quiet Hours”
    Amateur station must operate within the rules and without “spurious emissions” (frequencies outside of the necessary bandwidth of a transmission, 43 dB below the mean power of the fundamental signal)

## Slide 8: Operating Restrictions
Station Location and Antenna Structures
  Location: If the land has environmental importance or it is significant in American history, architecture or culture, you may be required follow special rules
    Designated wilderness area, wildlife preserve or listed in the National Register of Historical Places, you must submit and Environmental Assessment to the FCC
    If your station is located within 1 mile of an FCC monitoring facility, you must protect that facility from harmful interference (Table 3-4 on pg. 3-9)
  Antenna Structures: over 200 ft. or near a public use airport (FAA) has limitations

## Slide 9: Station Control
With the Internet connected directly to the radio and all manner of “Smart Devices” that will allow the equipment to work in concert, the possibilities are endless.
The control operator doesn’t have to be the station owner and doesn’t even have to be physically present at the transmitter
  Someone must be responsible for all amateur transmissions whether the equipment is directly supervised or not

## Slide 10: Station Control
Local Control
  The FCC defines local control as “the use of a control operator who directly manipulates the operating adjustments in the station to achieve compliance with the FCC Rules.”
    Rules don’t say by hand, or via computer, or even a voice-activated speech system
    If you are present at the station, that’s local control
    Turning a VFO knob or pushing the PTT is local control

## Slide 11: Amateur-Satellite Service
Definitions:
  Amateur-satellite service: Radio communications service using stations on Earth satellites for the same purpose as the amateur service.
  Earth Stations: Stations operating at or within 50 km of the Earth’s surface
  Space Station: Amateur station located above 50 km from the Earth’s surface
  Telecommand: One-way transmission to initiate, modify or terminate functions of a device at a distance
  Telecommand Station: An amateur station that transmits telecommand control functions
  Telemetry: One way transmission of measurements from measuring instruments

## Slide 12: Amateur-Satellite Service
Telecommand & Telemetry: provides a way to remotely control various function of the satellite
  FCC allows telecommand transmissions to use special codes to intentionally obscure the meaning of the message. (secure encryption)
  Satellite telemetry might indicate the state of battery charge, transmitter temperature or other spacecraft conditions

## Slide 13: Amateur-Satellite Service
Satellite Licensing & Frequency Privileges
  Any licensed Amateur Radio operator may be the control operator of a space station
  Any Amateur Radio station can also be a space station (assuming you can get it there)
  One special telecommand function required by the FCC – must be able to turn the station OFF!
  Frequencies:
    HF – 17, 15, 12, 10 & portions of the 40 & 20 meters
    VHF/UHF – segments of 2-meters, 70cm, 23cm & 13cm

## Slide 14: Volunteer Examiner Program
The Volunteer Examiner Coordinator
  VEC Accredits licensed Amateur Radio Operators
  VEC does not grade exams
  VEC is responsible for recruiting and training Volunteer Examiners
  The VEs determine where and when to hold license exam sessions

## Slide 15: Volunteer Examiner Program
Accreditation
  VEC accredits a VE certifying they meet the qualifications to perform all the duties required
    18 yrs old or older
    General class license or higher
      (General test Techs, Advanced & Extra test Generals, only Extras can test Extras)
    Never had license suspended or revoked
Exam Preparation
  VEC Coordinates the preparation and administration of exams
    ARRL VEC provides the test material & forms including exam software to their VEs
    VEC collects the completed exam documents and reviews them to ensure accuracy
      Forwards the documents to the FCC for a new license to be issued
VEC cooperates in the development and maintenance of the question pool used on the exams (QPC).

## Slide 16: Volunteer Examiner Program
Exam Session Administration
  Every exam session must be coordinated by a VEC
    Exam VEs must be accredited by the coordinating VEC
    It takes 3 VEs to administer an exam session
    You don’t have to be a member of the ARRL to be an ARRL accredited VE (membership is not required)
    VEs can not test family members

## Slide 17: Volunteer Examiner Program
Exam Session Administration
  VE Duties During the Exam Session
    Supervise the exam session (ensure proper conduct)
    Must be present during the entire exam session
    Ensure candidates follow the VE instructions
      Failure to comply with instructions terminates the exam
    VE collect and grade exams (74% is passing)
      VE notify candidates whether they passed or failed the exam
      VEs issue a CSCE to those who pass to certify their qualifications

## Slide 18: Volunteer Examiner Program
After the Exam
  The VE team must submit the application forms and test papers for all the candidates who passed to the coordinating VEC (Within 10 Days)
Re-administration of Exams
  The FCC has the authority to re-administer exam elements to any licensee
    Testing irregularities
    FCC determines a fraudulently administered or certified exam
  The FCC may designate a specific VEC to re-examine elements
  If you fail to appear for re-examination, the FCC will cancel your license

## Slide 19: Miscellaneous Rules
Auxiliary Stations
  Are amateur station, other than in messaging forwarding system, that transmit communications point-to-point within a system of cooperating amateur stations
    Links to remotely controlled stations
    Cross-band repeat stations

## Slide 20: Miscellaneous Rules
External Power Amplifiers
  RF power amplifiers capable of operating on frequencies below 144 MHz may require FCC certification
    Certification
      Satisfy the spurious emission standard
      Must not be capable of amplifying the input signal by more than 15dB
      Must not amplify between 26 and 28 MHz (CB)
    Amateurs my build their own amplifier or modify amplifiers for use in an Amateur Radio station without concern for the certification rules
    Dealers may sell non-certified amplifiers if they were purchased in used condition and resold to another amateur

## Slide 21: Miscellaneous Rules
Line A & National Quiet Zones (Fig. 3-4, pg. 3-20)
  The 420-430 MHz band segments
    Canada has allocated this segment to fixed and mobile service
    USA (remember treaties) amateurs are not permitted to transmit on these frequencies north of the boundary line along the boarder with Canada (see fig. 3-4)
    Quiet Zones: 50 mile radius centered on Buffalo, NY, Detroit, MI, Cleveland, OH
    Quiet Zones: Area surrounding the National Radio Astronomy Observatory Maryland, West Virginia and Virginia (National Radio Quiet Zone)
    Quiet Zones: Area surrounding Naval Research Laboratory at Sugar Grove, West Virginia

## Slide 22: Miscellaneous Rules
Business & Payment
  No transmissions are permitted in which you or your employer have a pecuniary (monetary) interest
  Your personal activities don’t count as business
    Talking to your spouse about shopping
    Order a pizza over a phone patch
    Radio swap nets on the air (usually close deal on phone) Don’t do it regularly or can become a business
  No compensation for communications directly or indirectly (Not for Hire or Trade)

## Slide 23: Miscellaneous Rules
Spread Spectrum Operation
  SS communications is a signal-transmission technique in which the transmitted carrier is spread out over a wide bandwidth (Bandwidth Expansion Modulation)
    Spread a little power over a wide bandwidth to minimize interference rather than concentrating a lot of power in a narrow bandwidth
    SS transmission are permitted as long as they don’t cause interference
    SS transmissions must not be used to obscure the meaning on any communications
    FCC limits maximum transmitter power for spread spectrum to 10 watts
    Operation of spread spectrum is restricted to frequencies above 222 MHz

## Slide 24: Miscellaneous Rules
Non-US Operating Agreements
  (CEPT) European Conference of Postal and Telecommunications Administrations radio license
    Allows US amateurs to travel and operate from most of European countries
    Amateurs from CEPT countries can operate in the USA
  (IARP) International Amateur Radio Permit
    Allows for operations in certain countries in Central and South America without seeking a special license or permit to enter and operate from that country
  (ITU) Reciprocal Permit is an agreement between the US and a country that does not participate in either CEPT or IARP agreements

## Slide 25: Miscellaneous Rules
Special Temporary Authority
  Occasionally, a new mode is developed that is not covered under existing FCC rules
    (STA) – Special Temporary Authority can be granted for experimental amateur communications
      Spread Spectrum was an example
      500 kHz communications
    STAs are temporary, lasting long enough for experiments to be performed and information accumulated
    STAs don’t give amateurs exclusive use of a frequency nor does it wave all the rules
    STAs may result in changes to the FCC rules but is not a wavier of any rule