## Slide 1: Chapter 4 Electrical Principles

## Slide 2: Radio Mathematics
Volts, Amps, Resistance / Impedance
Can’t see
Use equations to describe
Graphs are pictures of equations
Two types of graphs that show the same data in two different ways

## Slide 3: Rectangular Coordinates
Graph is composed of two axis, horizontal (x) and vertical (y)
The point (0,0) is called the origin
Data point is identified as a (x,y) data pair

## Slide 4: Polar Coordinates
Graph is composed of a fixed point called a pole (analogous to origin)
Data point (called a ray) is identified by a distance from the pole and an angle from the horizontal axis (counter clock wise is positive)
Angles are measured in degrees and radians
  One cycle / circle = 360 degrees = 2 π radians (1 radian ≈ 57.3°)

## Slide 5: Convert from Rectangular to Polar
Hyp =
θ = tan -1 (Opp / Adj)

## Slide 6: Convert from Polar to Rectangular
Radius (r) = Hyp
Adj = r * cos θ
Opp = r * sin θ

## Slide 7: Complex numbers / coordinates
Imaginary numbers
  = ?
  = 6
  = * = 2 * 3 = 6
  = ?
  = * = 5 *
  is defined as “imaginary number“
  Mathematicians use i, Electrical Engineers use j because “i" is used to indicate instantaneous current

## Slide 8: Complex Coordinates
Combine real & imaginary numbers (real + j imaginary)

## Slide 9: Convert Rectangular ˂˃ Polar
Rectangular to Polar
Hyp =
5 =
θ = tan -1 (Opp / Adj)
53.1⁰ = tan -1 (4 / 3)
Polar to Rectangular
Adj = r * cos θ
3 = 4.2 * cos(-45⁰)
Opp = r * sin θ
-3 = 4.2 * sin (-45⁰)

## Slide 10: Complex numbers Math
Add/Subtract - Use Rectangular form
(a + j b) + (c + j d) = (a + c) +j (b + d)
(2 + j3) + (4 + j1) = (6 + j4)
Multiply/Divide - Use Polar form
a θ1 * b θ2 = (a * b) (θ1 + θ2 )
a θ1 / b θ2 = (a / b) (θ1 - θ2 )
6 45⁰ / 2 30⁰ = (6 / 2) (45 - 30 ) = 3 15⁰

## Slide 11: Electrical Principals
Electric and Magnetic fields
  Introduced to E & M fields associated with antennas

## Slide 12: RC and RL Time Constants
Electrical energy
  Can be detected as voltage differences between two points
  Capacitors store and release electrical energy
  Capacitors will resist a change in voltage
Magnetic energy
  Is detected by moving electrical charges (current)
  Inductors store and release magnetic energy
  Inductors will resist a change in current movement

## Slide 13: Current / Magnetic field direction
Electronics (Elect Engr) use “whole” or “conventional” current
  Current flows positive (+) → negative (-)
  Use “Right Hand rule” to determine North
Physics use “electron” current
  Current flows negative (-)→ positive(+)
  Use “Left Hand rule” to determine North

## Slide 14: Time Constant
RC circuit - The time it takes to charge (or discharge) a capacitor (VC) depends on the size of the resistor
RL circuit - The time it takes for current to increase (or decrease) through an inductor (iL) also depends on the size of the resistor.

## Slide 15: RC Circuit
When charging a capacitor, VC (t) where τ = RC
When discharging a capacitor, VC (t)
= 2.71828 (base for natural logarithms)
It takes approximately 5 time constants to charge to 99.3% (or discharge to 0.7%)

## Slide 16: RL Circuit
Building current through an inductor, IL (t) where τ = L/R
When disrupting current through an inductor, IL (t)
It takes approximately 5 time constants to charge to 99.3% (or discharge to 0.7%)

## Slide 17: Phase Angle
Phase Angle refers to time
  1 cycle of frequency x = 1/x seconds
  1 cycle = 360⁰
  Phase angle is measured between similar points on each waveform
Resistors dissipate energy
  voltage & current are “in phase”

## Slide 18: Phase Angle
Capacitors and Inductors store / release energy
  Unlike in Resistors, voltage & current waveforms do NOT rise and fall together
ELI the ICE man
  Inductors – voltage (E) leads current (I)
  Capacitors – current (I) leads voltage (E)

## Slide 19: Voltage/Current Relationship in Capacitors
Capacitors resist changes in voltage
DC voltage / current
  Physical example, filling a tank with air

## Slide 20: AC Voltage/Current phase relationship in Capacitors
ICE - current LEADS voltage (VC)
  voltage (VC) LAGS current
  (current is reference) phase angle is -90⁰
(I)
(VC)

## Slide 21: Electric (field strength) energy is stored and released twice each cycle
Max current at 0 volts
0 current at Maximum volts
Current leads voltage (ICE)
(I)
(VC)

## Slide 22: Voltage/Current Relationship in Inductors
Inductors resist changes in current
  Physical example, flywheel
Relationship between AC voltage and current (in an inductor) complements that in a capacitor
  Stored Magnetic (field) energy is in phase with current

## Slide 23: Back EMF (induced voltage) in Inductors
is greatest when the magnetic field is changing the fastest
is generated with a polarity that opposes the change in current

## Slide 24: AC Voltage/Current phase relationship in Inductors
ELI - current LAGS voltage (VL)
  voltage(VL) LEADS current
  (current is reference) phase angle is +90⁰

## Slide 25: Resistance versus Reactance
Resistance is the opposition to the passage of (DC or AC) current (ohm Ω)
Reactance is the opposition to the AC current flow through an inductor or capacitance
  Inductive reactance
  Capacitive reactance

## Slide 26: Inductive Capacitive Reactance Reactance
Increases with increasing frequency
XL = 2π f L
  where
  XL =reactance in ohms
  f = frequency in hertz
  L = inductance in henries
Increases with decreasing frequency
XC = 1/2π f C
  where
  XC =reactance in ohms
  f = frequency in hertz
  C = capacitance in farads

## Slide 27: Complex Impedance
Impedance (Z) is composed of two components, resistance and reactance
Reactance can be either inductive or capacitive
Resistance and Reactance may be connected either in series or parallel

## Slide 28: Series Parallel Circuit Circuit
Current (I) is the same through both elements (R & X)
  I = IR = IX
Voltages (across the elements) are different (VR & VX)
  Vac = VR + VX
Voltage (Vac) is the same across both elements (R & X)
  Vac = VR = VX
Currents (through each element) are different (IR & IX)
  I = IR + IX

## Slide 29: Complex Impedance
The phase relationship between the current (I) and voltage (for the whole circuit, Vac) can be between 0⁰ and ±90⁰
The phase angle depends on the relative amounts of resistance and reactance
The sign of the angle depends on the type of the reactive element
  Inductive reactance produces a positive angle
  Capacitive reactance produces a negative angle

## Slide 30: Reduce multiple elements to one equivalent element
Multiple resistors to one resistor
Multiple reactive elements (capacitors / inductors) to one reactive element
  Capacitors (-90⁰) and inductors (+90⁰) have opposite phase angles
  Combining capacitors and inductors will result in a smaller TOTAL reactance (adding the negative and positive angles will cancel each other)
  If the capacitors and inductors have EQUIVALENT reactive values, they will cancel each other (angle=0⁰ thus X=0), resulting in only a resistive element (R)

## Slide 31: Calculate Impedance
Calculate Reactance of 20 mH inductor at 10 kHz
XL = 2π f L
XL = 2 x 3.14 x (10 x 103) x (20 x 10-3)
XL = 1256Ω

## Slide 32: Calculate Impedance
Since we aren’t given a VT , we assume I=1
VR = 1000v (voltage in phase with current)
VL = 1256v (voltage leads current by 90⁰, “ELI”)
= 1605
VT = 1605 51.5⁰

## Slide 33: Calculate Impedance
What if we would have had a 20,000 mF capacitor?
XC = 1/(2π f C)
XC = 1/[2 x 3.14 x (10 x 103) x (20,000 x 10-6)]
XC = 1/1256Ω = 1256 -90⁰
OR current leads voltage by 90⁰, “ICE”

## Slide 34: Calculating Impedances and Phase Angles - BASIC Rules
Impedances in series add together
Admittance is the reciprocal of impedance
  Y =
Admittances in parallel add together
Inductive and capacitive reactance in series cancel

## Slide 35: Refresher
Conductivity (G) is the reciprocal of Resistance (R)
  G = units of siemens (S)
Susceptance (B) is the reciprocal of Reactance (Y)
  B = units of siemens (S)
Taking the reciprocal of an angle, changes its sign
  37⁰ = and -73⁰ =

## Slide 36: Refresher (cont)
Voltage determines the reference for phase angle
  Current is the reference
  If voltage LEADS current (ELI) -> Positive phase angle
  If voltage LAGS current (ICE) -> Negative phase angle
    Voltage LAGS current = current leads voltage

## Slide 37: Reactive Power and Power Factor
Power = Voltage x Current (DC circuit)
Reactive Power = VoltageRMS x CurrentRMS
  AC circuit, when voltage & current are in phase
Apparent Power
  Does not take into consideration phase angle
  Expressed in units of volt-amperes (VA)
  AKA reactive, nonproductive or wattless power (VAR)

## Slide 38: Power Factor
Apparent power = 250 V x 2 A = 500 VA
Real power = I2 R = (2 A)2 x 75 Ω = 300 W
PF = = = 0.6
Power Factor is calculated using phase angle (θ) between the current and voltage [PF= Cos (θ)]
  PF = 1 when θ = 0⁰ (all apparent power is real power)
  PF = 0 when θ = 90⁰ (all apparent power is reactive power)

## Slide 39: Resonant Circuits
Circuits with different inductive and capacitive reactances
  Series – different voltages
  Parallel – different currents
Circuit is said to be resonant when XL = XC
  Series – VC will cancel VI , leaving only VR
  Parallel - IC will cancel II , leaving only IR
Calculation of Resonant frequency
  XL = XC
  2π f L = 1/2π f C
  Resonant frequency (fr)

## Slide 40: Impedance of Resonant Series Circuits
At resonant
  VL = VC
  Equal amounts of energy are stored in each component
  The energy being supplied will cause voltages across the inductor and capacitor to build to multiple times the source voltage
  XL cancels XC, resulting in maximum current
  Voltage and current are in phase
Series Circuits
Same current
VL is 180⁰ out of phase with VC

## Slide 41: Impedance of Resonant Parallel Circuits
At resonant
  IL = IC
  I = (IL + IC) = 0, so the parallel combination will appear like an open circuit
  The energy being exchanged between the inductor and capacitor will result in large circulating current
  Total current from the generator is small
  Voltage (across the tank) is at maximum
  Voltage and current are in phase
Parallel Circuits
Same voltage
IC is 180⁰ out of phase with IL

## Slide 42: Q and Bandwidth of Resonant Circuits
Practical components
  Can be represented as ideal components (inductor or capacitor) in series with a resistor
  That resistance dissipates some of the stored energy
Quality factor ( Q )
  Represents how close to an ideal component is the practical component
  Ratio of how much energy is stored to how much energy is dissipated
  Energy losses of a capacitor is usually much less than that for an inductor
  Thus the Q of the inductor is usually the limiting factor of the Q of a resonant circuit
  The only way to raise the Q of an inductor or capacitor is by using components with less internal resistance

## Slide 43: Q and Bandwidth of Resonant Circuits (cont)
Resonant Circuit Bandwidth
  Bandwidth of the frequency range where the voltage (or current) is no more than 3 dB (i.e. .707) below the peak
  Also called the half-power (or -3 dB) bandwidth
    the half power bandwidth
    resonant frequency of the circuit
  Higher Q, the narrower the bandwidth (sharper)

## Slide 44: Q and Bandwidth of Resonant Circuits (cont)
Skin Effect and Q
  As frequency increases
    more of the current travels closer to the surface of the wire
    the “effective” resistance of the wire increases
  HF – outer few thousandths of an inch
  VHF & UHF – outer few ten-thousandths

## Slide 45: Magnetic Cores
Inductors store magnetic energy, creating reactance
Wire can be wound around various material
  Air is relatively inefficient way to store magnetic energy
  Magnetic material increases the storage of energy (and the inductance)
Inductance is a function of
  Number of turns of wire on the core
  Core materials permeability (air = 1)

## Slide 46: Magnetic Cores (cont)
Select the core material carefully
  Perform over a desired frequency range
  Temperature stability
Core shape
  Affects magnetic field (shape around the inductor)
  Magnetic field of one inductor can interact with nearby components (coupling)
  Toroid cores reduce unwanted coupling by keeping the magnetic field contained in the “donut”

## Slide 47: Magnetic Cores (cont)
Calculating Inductance
  Or number of turns
  Each time the wire passes through the core, it counts as a turn
Ferrite bead
  Small core, slipped over component leads, often used as suppressors for VHF & UHF oscillations

## Slide 48: Questions