## Slide 1: Electronic Circuits
Chapter - 6

## Slide 2: Amplifiers
RF, IF, Audio
High Power Low Power
Gain
  Ratio of output to input Voltage, Current, or Power
Input & output impedance
Main Component
  Transistors, Tubes, or ICs

## Slide 3: Common-Emitter Circuit
Most often used
Input to base Output from collector
R1 & R2 form a voltage divider for fixed bias
R3 is used for self bias to prevent thermal runaway
Provides the highest gain

## Slide 4: Common Base Circuit
Input on Emitter output on collector
Low impedance input
High impedance output
Primarily used as an impedance converter

## Slide 5: Common Collector
Also, Emitter Follower
High input and low output impedance
Output coupling capacitor C2
R is the Emitter load resistor
Often used as buffer amplifiers

## Slide 6: Op Amp Amplifiers
Amplifies DC as well as AC signals
Direct coupled, with High input and low output impedance
Have two inputs
  Inverting (-)
  Non-inverting (+)
Amplifies the difference between the two inputs

## Slide 7: OP Amp Characteristics
Ideal Op Amp
Infinite input impedance
Zero output impedance
Infinite voltage gain
Flat frequency response
Zero output when the input is zero
Practical Op Amp
Very high input impedance
Very low output impedance
As high as 120 DB (open loop) gain
Gain decreases with frequency in an open loop circuit
Small output with zero input

## Slide 8: Op Amp Basic Circuit
Gain and frequency response determined by feedback components
Voltage gain is determined by the values of R1 and RF
  |AV|=RF / R1
As this example circuit is using the inverting input the result will be negative

## Slide 9: Vacuum Tubes
Compared to Transistors
  Grid - Base
  Cathode - Emitter
  Plate – Collector
Circuits
  Common Cathode
    High input impedance, Power Gain
  Grounded Grid
    Low input impedance, matches well to 50 ohms

## Slide 10: Amplifier Classes
Class A
  Bias is set at about halfway on the Load Line
Class B
  Bias is set at cutoff level
Class AB
  Operates between the 180ͦ and 360ͦ points of the signal cycle
Class C
  Bias is set well into the cutoff region
Class D
  Uses switching technology to achieve high efficiency
  Requires low pass filter on output to remove harmonics

## Slide 11: Distortion and Intermodulation
Distortion
  Nonlinearity produces distortion
  Distortion results in harmonics
  You can have low distortion or high efficiency, but not both
Intermodulation
  2 or more signals mixed to produce other signals
  Even order products result in spurious signals
  Third order products are close to the desired frequency

## Slide 12: Selecting Operating Class
For Audio, AM & SSB Linear amp is required
For CW or FM a nonlinear amp will work
Using a Class C amp for AM or SSB will result in distortion and excessive bandwidth
Class B amplifiers can be used for audio by connecting two of them in push-pull to eliminate even order harmonics

## Slide 13: Instability and Parasitic Oscillation
Excessive gain or positive feedback may case amplifier instability
Oscillation can be prevented by neutralizing the stage or parasitic suppression
One way to neutralize an RF power amplifier is by feeding a 180 degree out of phase portion of the output back to the input
Parasitics are oscillations that are not related to the operating frequency of an amplifier

## Slide 14: VHF, UHF & Microwave Amplifiers
Klystrons
  Uses Velocity Modulation
Parametric Amplifiers
  Uses a varactor diode and separate oscillator
  Uses varying reactance for amplification
  Low noise on the output
Microwave Semiconductor Amplifiers
  Geometry of junction transistors limits upper frequency limit to a few GHz
  Gallium-Arsenide FET’s can operate up to 20-30 GHz

## Slide 15: Oscillator Circuits and Characteristics
Amplifier with positive feedback
  AV = Amplifier gain
  β = Feedback ratio
  Loop Gain = AV x β
  If positive loop gain > 1 and in phase, circuit will oscillate

## Slide 16: RF Oscillators
Colpitts
  Tapped capacitance
  “C” for capacitance & Colpitts
Hartley
  Tapped Inductance
  “H” for henry and Hartley
Pierce
  Colpitts with a crystal
  Most stable of three

## Slide 17: Crystals
Usually a small wafer of quartz with precise dimensions
Piezoelectric effect
  Crystal deforms physicaly when voltage applied
  Voltage generated when crystal deformed
High Q
  Very stable and precise
Use parallel external capacitance to insure the proper frequency

## Slide 18: Variable Frequency Oscillator (VFO)
Used to allow an oscillator to tune over a frequency range
  Like in the tuning circuit on a radio
Either the capacitance or inductance must be variable
  Variable capacitance is the most common
Not as stable as a crystal oscillator

## Slide 19: Microwave Oscillators
Magnetron
  A diode vacuum tube with a specially shaped anode surrounded by a magnet
  Used for UHF and Microwave frequencies
  Used in microwave ovens
Gunn Diode
  Use a resonant cavity to control frequency
  Uses negative resistive properties of properly doped semiconductors
  Used in traffic radar guns

## Slide 20: Digital Signal Processing (DSP)
Sequential Sampling
    Commonly used to convert analog signals to digital signals
Data Converters
  ADC – converts analog signals to digital
  DAC – converts digital signals to analog
Software Defined Radios (SDR)
  A radio whose functionality can be altered by software
  Replaces traditional analog circuits with DSP

## Slide 21: Mixers
Are used to change the frequency of a signal
In a receiver converts to the IF frequency
Can also be used to change frequencies in a transmitter
Excessive signals can cause spurious signals to be generated from a mixer
Mixer output contains Input Signal, Oscillator Signal, the sum of the two and the difference of the two
Use a filter to select the proper frequency

## Slide 22: Modulators
Process of adding information to an RF carrier
  The frequency components (voice or data) in the modulating signal make up the baseband
Amplitude Modulation
  Contains a carrier and two sidebands
  Amplitude of the signal depends on the amplitude audio signal

## Slide 23: Single Sideband (SSB)
Starts with an AM signal
Filter method
  Use balance modulator to remove carrier
  Use a bandpass filter to remove one of the sidebands
The Quadrature method
  Uses 90 ͦ phase shift to cancel the carrier and one sideband
    Hard to do with analog circuit
    Can do with DSP circuit – Hilbert transformer
    Preferred method in radios using DSP

## Slide 24: Frequency Modulation (FM)
Direct FM
  Can be produced with a reactance modulator on the oscillator
  Gives true F3E emission
Indirect FM (Phase Modulator)
  PM signals can be produced by electrically variable capacitance or inductance
  Uses a reactance modulator to vary tuning on an RF amplifier tank circuit

## Slide 25: Pre-emphasis & De-emphasis
Pre-emphasis is used on FM transmitters
  Boosts the higher audio frequency
  Not needed in Phase Modulated transmitters
De-emphasis is used on FM receivers
  The opposite of De-emphasis
  Used to restore the audio back to its original form
This process is used to reduce high frequency noise

## Slide 26: Detectors & Demodulators
Used to recover information from modulated signal
Diode Detector
  Works by rectifying and filtering modulated signal
Product Detectors
  Uses locally generated carrier (BFO)
  Used for SSB, CW, & RTTY
Direct Conversion
  Incoming RF signal is mixed to baseband for ADC conversion
Detecting FM signals
  A common way is to use a Frequency-discriminator

## Slide 27: Phased-Locked Loops
An electronic servo loop
  Reference Oscillator, Phase Detector, Low-Pass Filter, and Voltage Controlled Oscillator
This allows a radios VFO to have the stability of a crystal oscillator
The capture range is the frequency range over which the circuit can lock

## Slide 28: Phase-Locked Loops
Unwanted variations Any short term variation in the phase of the output signal will Phase Noise
  Major spectral impurity component of PLL synthesizer
Phase-Locked Loops can also be used for FM Modulation and Demodulation

## Slide 29: Direct Digital Synthesizers (DDS)
Phase Accumulator
  Reads data from the adder
Lookup Table
  Contains amplitude values to create sine wave
Digital to Analog Converter
Low-pass alias filter
  Smooth's sine wave output
No phase noise, but spurs at discrete frequencies

## Slide 30: Passive Filters
Passive Filters
  Constructed using passive components
    Capacitors, Inductors, Resisters
  Crystal
  Mechanical (Collins)
  Cavity (Used for Repeater Duplexers)
  Always have insertion loss
Active Filters
  Include an amplifying device
    No insertion loss, may have gain

## Slide 31: Filter Classification
Low-pass
  Passes frequencies below the cut off frequency
High-pass
  Passes frequencies above the cutoff frequency
Band-pass
  Passes signal between upper and lower cutoff frequency
Band Stop or Notch
  Rejects signals between upper and lower cutoff frequency
    Used to attenuate interfering signals
Cutoff frequencies are at 3db below the maximum

## Slide 32: Filter Design Definitions
Phase Response
  Shift of signal phase vs, frequency between input and output
  Linear response indicates smooth no ripple as frequency changes
  Non-linear response can result in distortion of complex digital signals
Ringing
  Oscillations continue after signal is removed

## Slide 33: Filter Types
Butterworth
  Passband and stopband are flat
Chebyshev
  Ripple in the passband
  Sharper cutoff transition
Elliptical
  Notches in passband and stopband
  Sharpest cutoff

## Slide 34: Crystal Filters
Used in receiver IF stages to obtain narrow bandwidth to filter out adjacent signals
  Normally a Crystal Lattice filter is made from quartz crystals and has narrow bandwidth and steep response curves
  The bandwidth and response curve are determined by the crystal frequencies
  A Jones filter is a special type of Crystal Lattice filter with a variable bandwidth
Crystal Lattice filter are used in SSB transmitters to filter out unwanted sideband

## Slide 35: Active Filters
Can be built without inductors
No insertion loss & can have gain
Normally built with Op-amps
  Gain and frequency determined by external capacitance and resistance values
  Use polystyrene capacitors to improve stability
Best suited for audio filtering in receivers
Easily available low cost parts
May have ringing and audio instability
  Restrict gain and Q to reduce this problem

## Slide 36: Digital Signal Processing (DSP)
Adaptive processing
  Software can recognize and adopt to different signals and conditions
  No tuning required
  Can be used to remove unwanted noise from a received SSB signal
Can build filters that are impossible with hardware
  “Brick Wall” filters approach shape factor of 1.0

## Slide 37: Impedance Matching
If load and source impedances are not equal, an impedance matching network is needed
Assuming a source impedance of 50Ω, the matching network must:
  Cancel the reactive portion of the load impedance
  Transform the resistive component to 50Ω

## Slide 38: Impedance Matching Networks
L-Networks
  Can match virtually any 2 impedances
  Q is fixed
  Usually can only operate on one frequency band
T-Networks
  Commonly used in antenna coupling equipment
  Can match wide range of impedances
  It also acts as a band-pass filter

## Slide 39: Pi Impedance Matching
Pi and Pi-L Networks
  An inductor is between the input and output with capacitors on each side going to ground
  Equivalent to two L-networks connected back-to-back
  The Q can be varied compared to a fixed Q for L-networks
  A Pi-L network has an additional series inductor on the output and greater harmonic suppression
  On a power amplifier the tuning capacitor is adusted for minimum plate current and the load capacitor is adjusted for maximum permissible plate current

## Slide 40: Linear Voltage Regulators
The conduction is of a control element is varied to maintain a constant output voltage
Shunt Regulators
  Maximum current flows all of the time
  Has a constant load on the unregulated power source
Series Regulator
  Good efficiency compared to shunt regulator
  Only the current required by the load flows

## Slide 41: Linear Regulator Circuit
Q1 increases the current handling capability
C1 is a filter capacitor
C2 bypasses hum around D1
C3 prevents self oscillation
R1 supplies current to D1
R2 provides a constant minimum load to Q1
D1 is a Zener diode which provides a voltage reference
  Zener diodes provide a stable reference voltage

## Slide 42: Other Power Supplies
Switching Regulators
  The control device’s duty cycle is controlled to produce a constant average voltage
  By using a high frequency inverter design the transformers and filter components are smaller and lighter
High Voltage supply capacitors
  Connecting series to increase voltage handling
    To equalize the voltage drop across each capacitor
    To provide a safety bleeder
    To provide a minimum load current
  Step-start Circuit
    Allows filter capacitors to charge gradually
A bleeder resistor is used improve output regulation on Unregulated power supplies