## Slide 1: Chapter 7 Radio Signals and Measurements

## Slide 2: Types of AC Waveforms – Sine
Most fundamental waveform
Also describes rotating motion
A = sin(θ)
2 π radians = 360 degrees
  T = time to complete 360 degrees
  f = frequency

## Slide 3: Types of AC Waveforms - Complex
Complex Waveforms
Signals composed of more than one sine wave
Telephone keypads – dual-tone multi-frequency (DTMF)
regular waveforms
  made up of a sine wave and its harmonics
  resulting waveform has single overall frequency
  Lowest frequency sine wave is called the fundamental
Irregular waveform
  Made up of sine waves NOT harmonically related
  Human speech

## Slide 4: Complex Waveforms
Sawtooth Waves
Sine wave at its fundamental frequency
plus all of its harmonics
Ramp waveform is reverse
Square Waves
Sine wave at its fundamental frequency
plus all of its odd harmonics

## Slide 5: Pulse Waveforms
Consist of narrow bursts of energy, followed by periods of no signal
Used to transmit information by varying amplitude, rate, width or position

## Slide 6: AC Measurements
For symmetrical waveforms,
the dc voltage that would cause an identical amount of heating to the ac peak voltage )

## Slide 7: AC Measurements for Sine and Square Waves
 | Sine Wave | Square Wave
Peak-to-Peak | 2 x Peak | 2 x Peak
Peak | 0.5 x Peak-to-Peak | 0.5 x Peak-to-Peak
RMS | 0.707 X Peak | Peak
Peak | 1.414 x RMS | RMS
Average | 0 (full cycle) | 0 (full cycle)
 | 0.637 x Peak (half cycle) | 0.5 x Peak (half cycle)
AC Power

## Slide 8: AC Power
Peak envelope voltage (PEV) is used to determine power of a complex waveform

## Slide 9: Electromagnetic Waves
Composed of Electric and Magnetic fields that move through space independently of any component or conductor
The fields cannot be separated
The energy in the wave can be detected as either electric or magnetic force
The fields are created as a single entity (electromagnetic wave) by the motion of electrons in the transmitting antenna

## Slide 10: Polarization
Orientation of the electric field determines polarization of the wave
Transmitting antenna’s orientation determines wave’s polarization
Vertical – electric field is perpendicular to the Earth
Horizontal – electric field parallel to surface of the Earth
Circular

## Slide 11: Test Equipment
Multimeters, Volt-Ohm-Milliammeter (VOM), Voltmeter
  Accuracy defined as ± X% of full scale
  Meter sensitivity specified in ohms-per-volt (
Dip Meters
  Used to measure circuit frequency, resonant frequency, inject freq into circuit
  Coupling should be as loose as possible to prevent loading/reducing accuracy
Impedance Bridges
  Works by balancing the two voltage dividers
  Used to measure SWR

## Slide 12: Test Equipment
Frequency Counters
  Counts number of cycles per second of a signal
  Accuracy is determined by the quality of its reference crystal and expressed in parts per million (ppm)
Oscilloscope
  Used to observe/measure high-speed and complex waveforms
  Specified in terms of (vertical amplifier) bandwidth
  Screen grid; Vertical ( & Horizontal (
  Keep ground connection short as possible
  Adjust probe compensation with reference square wave (per scope user manual)

## Slide 13: Test Equipment
Oscilloscopes operate in the Time domain
  Display signal’s amplitude versus time
  Horizontal (x) axis represents time (
  Vertical axis calibrated in volts per division
Spectrum Analyzer operate in the Frequency domain
  Display signal’s amplitude versus frequency
  Horizontal (x) axis represents frequency (
  Vertical axis normally calibrated in dB per division

## Slide 14: Uses for Spectrum Analyzers
Use where the frequency content of a complex signal is of primary importance (i.e. amplifiers, oscillators, detectors, mixers, filters, etc.)
Check the output from a transmitter or amplifier for signal quality
  Remember to attenuate the signal level to the analyzer to typically 10 mW or less
Check SSB for two-tone intermodulation distortion (IMD)
Measure isolation between input and output ports of a 2 meter duplexer

## Slide 15: Modulation Systems
Adding and later recovering information from radio frequency signals.
Amplitude Modulation
Frequency Modulation
Phase Modulation
Pulse Width Modulation

## Slide 16: FCC Emission Designations
International Telecommunication Union (ITU) identifiers
May be up to 5 characters but 3 is common
Common in Amateur Radio:
N0N – Unmodulated carrier | F3E – FM telephony
A1A – CW | G3E – Phase modulated telephony
A3E – AM, DSB, Full carrier telephony | F1B – FSK RTTY
J3E – AM, SSB, suppressed-carrier telephony | F2B – AFSK RTTY
J3F – AM, SSB, suppressed-carrier television | F1D – FM data

## Slide 17: FM/PM Modulation
Signal frequency varies at the rate of the modulating-signal frequency
Amount of frequency change is proportional to modulating signal amplitude = deviation
Deviation Ratio = ratio of max deviation to highest modulating frequency
  Constant for a given transmitter/modulator

## Slide 18: Modulation Index
Ratio of maximum signal frequency to instantaneous modulating frequency
Frequency modulator – MIndex inversely proportional to modulating frequency
Phase modulator – MIndex constant regardless of modulating frequency
FCC Limits MIndex to maximum of 1.0

## Slide 19: Pulse Modulation
Transmitting analog information as a series of pulses; on/off pulses = 1/0 digital signal so considered digital data
Pulse-width modulation
Pulse-position modulation
Pulse-amplitude modulation
Used for R/C control and switching power supplies

## Slide 20: Multiplexing
Combining more than one stream of information into one modulated signal
Frequency division (FDM) multiple subcarriers
Time division (TDM) interleaving two or more signals into discrete time slots
Not to be confused with multi-carrier digital modes which interleave a single signal across multiple carriers to increase transmission speed

## Slide 21: Interference and Noise
Interference/QRM – signals that have characteristics of transmitted signals
  Usually “manmade”, arc welder, CFLs, electric motors
Noise/QRN – random natural sources or unintentional generation by non-transmitting equipment
  Usually “natural” i.e. static crashes from lightning

## Slide 22: Intermodulation
Intermodulation (IMD) – multiple frequencies mixed in a non-linear manner
  Transmitter IMD, nearby transmitted signals mixed in the PA of a transmitter and thus retransmitted
    Commercial sites may use circulators to eliminate
  Receiver IMD, strong received signal causes front end to go non-linear and may mix other undesired signals producing spurious received signal
    Good receiver dynamic range is important to mitigate

## Slide 23: Static & Noise
Static from lightning is especially common on HF bands and can sometimes be heard much higher
With good propagation it is possible to hear static from lightning on the other side of the world on medium HF frequencies
Precipitation picking up a charge as it falls can cause rain or snow static

## Slide 24: AC Line Noise
Unfortunately one of the more common forms of QRM (manmade)
  Caused by arching between electrical conductors or electrical leakage across an insulator that is breaking down
  Caused by small motors with brushes
  Light Dimmers, motor speed controls

## Slide 25: Locating QRN & QRM Sources
Process of elimination
  Run your receiver off battery and shut off main breaker to your house
    Noise went away; it’s in your house; shut off all circuit breakers, main back on, turn on circuit by circuit till noise comes back, then start turning off/unplugging devices on that circuit
    Noise stayed; it’s not in your house; more work required, portable AM receiver can be used to track down in some cases

## Slide 26: Automotive Noise
Ignition Noise – make sure the ignition components are in good condition and making secure connection
Charging system – radio powered direct from battery may help, make sure battery is in good condition, radio and antenna properly grounded
Instruments – bypass capacitor on sender/motor

## Slide 27: Electronic Noise Reduction
Do NOT use with Digital Modes!
Noise Blanker – shuts off signal for short duration “blanking” noise; good for impulse noise

## Slide 28: Electronic Noise Reduction (cont.)
DSP – electronic filter that adapts to noise pattern and eliminates it; especially good for notch filters

## Slide 29: Questions