## Slide 1: Chapter 8 Radio Modes and Equipment
<number>

## Slide 2: Digital Protocols and Modes
Bits vs. Baud (plural of Baud is Baud NOT Bauds)
Bits = over the air data rate, bits/sec
Baud = symbol rate, symbols/sec, transitions/sec, signaling event
Bit rate = Baud rate when there are only 2 states 1 or 0, on or off, 2295 or 2125 HZ

## Slide 3: Digital Protocols and Modes (cont.)
Data rate (bits) > Baud rate when there are more than 2 states per transition (baud)
Baud | States | Bits/sec
300 | 2 | 300
300 | 4 | 600
300 | 8 | 1200
300 | 32 | 4800

## Slide 4: Digital Signal Bandwidth
“No free lunch” applies to bandwidth of digital signals; faster baud rate = more bandwidth
BW = B X K where BW is the bandwidth needed, B is the Baud rate and K is a constant related to the shape of the keying envelope

## Slide 5: Protocols and Codes
Protocol = rules for encoding, packaging, exchanging & decoding digital data
Code = method of conversion to/from digital data
  Varicode (mores & PSK) variable length
  Baudot – 5 bits, requires shift for numbers/letters
  ASCII 7 bits allow numbers and letters without shift character

## Slide 6: Codes (cont.)
  Start bits, Stop bits, Parity bits
    Transmissions are Asynchronous (transmitting and receiving clocks are not synchronized) so need bits to signify start and stop of data frames; i.e. start and stop bits
    A Parity bit can be added to detect single bit errors
      Even parity = even number of 1’s in data frame
      Odd parity = odd number of 1’s in data frame
      No parity = most common
    Stop bit; 1.5 for Baudot, 1 for ASCII (2 was used for mechanical teleprinters) always 1 for electronic devices

## Slide 7: Digital Modes
Digital Mode = protocol + method of modulation
FCC assigns different emission designator for each specific use (3rd symbol of designator)
  E = voice (J3E)
  B = text (telegraphy for automatic reception) (F2B)
  D = data (F1D)
  F = television/image (C3F)
Advantage is ability to transmit and copy multiple times without error

## Slide 8: CW
Simplest form is turning an AM transmitter on and off (A1A)
Bandwidth determined by speed and keying envelope
Standard “word” is PARIS
BW = WPM x 1.2 x K where K is 3 to 5 reflecting abruptness of keying waveform, more abrupt is larger
13 WPM BW = 13x1.2x4 = 62.4 Hz

## Slide 9: FSK/AFSK
Most amateur data transmissions (all on HF) use Frequency Shift Keying (FSK)
RTTY/ASCII use two states/tones (Mark & Space)
Shift is the difference between Mark & Space tones
Direct FSK is F1B generated by directly shifting oscillator freq
AFSK is J2B or J2D generated by injecting audio tones into mic circuit

## Slide 10: FSK/AFSK Bandwidth
BW = (K x shift) + B where K is 1.2 and B is baud
170 Hz 300 baud ASCII J2D transmission bandwidth = (1.2x170)+300=504Hz
VHF Packet example (1.2x1000)+1200=2400Hz

## Slide 11: PSK
Phase Shift Keying (PSK) PSK31 very popular keyboard to keyboard mode on HF
J2B emission, full 128 char ASCII 256 char ANSI
Uses variable length characters (Varicode)
00 is the intercharacter gap
BW minimized by using sinusoidal shaping
PSK31 BW=31.25x1.2=37.5 Hz narrowest HF digital mode
Many variations now; PSK125C12 (BW 2100 Hz), PSK1000C2 (BW 2400 Hz), PSK250R6 (BW 2000 Hz)(bits/sec # carriers R includes error correction)

## Slide 12: HF Packet
Uses AX.25 protocol same as VHF packet but limited to 300 baud by FCC; designated J2D
AX.25 includes error detection so if receiving station does not ACKnowledge good reception transmission is repeated up to max retry limit, typically 5

## Slide 13: Pactor I/II/III
Performs well under weak signal and high noise conditions
Supports binary data transfers
Automatic Repeat reQuset (ARQ) error correction
Pactor II/III require SCS Pactor modem
Automatic evaluation of conditions between transmitter/receiver to adjust speed to highest for current conditions
Pactor III can exceed 5000 bits/sec

## Slide 14: MFSK/MT63
Soundcard modes
Use multiple tones to increase data rate
MFSK16 uses 16 tones BW 316 Hz 63 bps
MFSK can use 4,8,11,16,22,31,32,64 or 128 tones
MT63 uses 64 tones BW 1000 Hz 70 bps
MT63 can use 500, 1000 or 2000 Hz bandwidth

## Slide 15: www.W1HKJ.com Sights and Sounds of Digital Signals

## Slide 16: WSJT
Developed for weak-signal VHF/UHF such as EME
5 modes
  FSK441 meteor scatter
  JT65 EME
  JT6M 6 meter meteor scatter
  EME Echo for measuring your own signal bounced from the moon
  CW 15 WPM QSOs
JT65 can decode signals well below noise level

## Slide 17: Where to get WSJT/JT65
Google WSJT or JT65
WSJT Home Page http://www.physics.princeton.edu/pulsar/K1JT/
JT65
http://sourceforge.net/projects/jt65-hf/
JT65 frequencies 14.076, 10.139, 7.039, 7.076

## Slide 18: JT65 Signal

## Slide 19: Transmitting Digital Modes
DO NOT OVERDRIVE THE TRANSMITTER
Keep drive level low enough that no ALC is indicated
Do not use any speech processing
Check your signal by transmitting into a dummy load and receiving on a second receiver with computer/soundcard with demodulation program for that mode

## Slide 20: Spread Spectrum (SS)
Spreading a signal over a very wide bandwidth by rapidly varying carrier frequency in a predefined sequence (spreading-code)
Dilution of the signal across many frequencies makes it sound like noise to conventional receiver; may appear to be below noise floor
Ignores strong non-spread signals because they do not follow the spreading-code

## Slide 21: SS (cont.)
FM, SSB,CW signals as well as other SS with a different spreading-code are ignored
Many SS systems can share frequencies by using different spreading-code; Code-Division Multiple Access (CDMA)
CDMA is used by may Cellular service carriers

## Slide 22: Error Detection & Correction
What good is data if it’s corrupted!
RTTY & PSK31 have no error detection or correction
Adding a Parity bit can detect single-bit errors
Cyclic-Redundancy-Check (CRC) can detect multi-bit errors
Automatic Repeat reQuest (ARQ)
  ACKnowledged (ACK) or Not AcKnowledged (NAK)

## Slide 23: Error Correction (cont.)
But can’t we include some additional data up-front to correct errors!
Forward Error Correction (FEC) does just that
FEC adds correction data ahead of the “information” data, may be spread over several data packets
Many types of FEC codes, Reed-Solomon, Hamming, BCH, Golay

## Slide 24: Error Correction (cont.)
Garbage once error rate exceeds correction threshold
Viterbi encoding restricts the number of symbols sent over the air to a subset of the original data, the Viterbi decoder algorithm then presents the most likely data to been sent to the encoder

## Slide 25: Amateur Television (fast Scan)
Analog TV standards are used, not current HDTV (digital) standards

## Slide 26: Signal Definitions
B/W NTSC
Line rate | 15,750 Hz
Field rate | 60 Hz
Frame rate | 30 Hz
Horizontal Lines | 262.5/field 525/frame
Sound subcarrier | 4.5 MHz
Channel bandwidth | 6 MHz

## Slide 27: RS-170 B/W Signal

## Slide 28: IRE Levels
Zero carrier | 120 IRE
White | 100 IRE
Black | 7.5 IRE
Blanking | 0 IRE
Sync tip | -40 IRE
%Peak Envelope Voltage (%PEV) is obsolete, use IRE

## Slide 29: Color Video
NTSC Analog Color not Digital
Line rate | 15,734 Hz
Field rate | 59.94 Hz
Frame rate | 29.97 Hz
Horizontal Lines | 262.5/field 525/frame
Color subcarrier | 3.579545 MHz
Sound subcarrier | 4.5 MHz
Channel bandwidth | 6 MHz

## Slide 31: Transmitting ATV
Need to have a stable picture even with very weak analog signals
RS-170 video is inverted for transmission
Peak signal is thus the tip of the sync pulses
Of the 525 lines only 483 are used for picture, the rest are sync only
UHF or above only
FM ATV 1.2, 2.4, 10.25 GHz, 17-21 MHz BW
AM carrier of video can be FM’d with audio

## Slide 32: Slow-Scan Television
Isn’t there some way of transmitting pictures on HF or VHF?
On HF & VHF we can use facsimile (pretty much obsolete) or Slow-scan television
Slow-scan using soundcard based software is popular using SSB on HF or FM on VHF
No interlace, one frame per picture
NASA used a form of SSTV for the Apollo program

## Slide 33: SSTV Station

## Slide 34: Analog SSTV
B/W Standards
Frame time | 8 sec
Lines per frame | 120
Time to send 1 line | 67 ms
Duration Hsync pulse | 5 ms
Duration Vsync pulse | 30 ms
Hsync & Vsync freq | 1200 Hz
Black freq | 1500 Hz
White freq | 2300 Hz
Bandwidth | 2000 Hz

## Slide 35: Color Analog SSTV
Format | Name | Time (sec) | Lines
Wraase SC-1 | 24 | 24 | 128
 | 48 | 48 | 256
 | 96 | 96 | 256
Martin | M1 | 114 | 256
 | M2 | 58 | 256
 | M3 | 57 | 128
 | M4 | 29 | 129
Scottie | S1 | 110 | 256
 | S2 | 71 | 256
 | S3 | 55 | 128
 | S4 | 36 | 128

## Slide 36: Digital SSTV
Based on the Digital Radio Mondale (DRM) protocol
Bandwidth limited to 3 KHz
No additional hardware required beyond a receiver required to decode DRM on a PC
EasyPAL is most common software
http://www.kc1cs.com/
14.233 MHz is where most activity is found

## Slide 37: Operating SSTV
100% duty cycle, reduce power
As with other digital modes, no ALC or speech processing
No noise blanker or DSP on receive
Phone segment of all bands except 30 Meters
Analog 14.230 & 7.171 MHz most popular
Picture ID is ok, voice recommended in case listener is unable to copy picture

## Slide 38: Receiver Performance
<number>
It is important to be able to measure and evaluate receiver quality.
  Successful communications depends on quality reception of signals.
    Free of noise and distortion
    Ignore unwanted signals
    Sensitive to the weakest signals

## Slide 39: Receiver Performance Sensitivity and Noise
<number>
One basic receiver specification is sensitivity or Minimum Discernible Signal (MDS).
  MDS of a receiver is the strength of the smallest discernible input signal.
  Depends on noise figure and bandwidth.
  MDS also called the receiver’s noise floor.
    Signal that produces same audio level as the receivers noise.
  The lower the MDS the more sensitive the receiver.

## Slide 40: Receiver Performance Sensitivity and Noise
<number>
  MDS often expressed in dBm
    Decibels with respect to one milliwatt
      0 dBm is the same as 1 mw, +10 dBm 10 mw, etc.
  MDS also expressed as μV.
    An MDS of 0.5 μV equals and MDS of -113 dBm.
      Practical MDS on the HF bands.
      The theoretical noise at the input of an ideal receiver, with an input filer bandwidth of 1 Hz, is -174 dBm/Hz at room temperature.
  Atmospheric noise is the primary source of noise in and HF receiver and therefore the limiting factor for sensitivity of receivers on the HF bands.

## Slide 41: Receiver Performance Sensitivity and Noise
<number>
A receiver bandwidth of 1 HZ is impractical but is used as a reference.
  For the filter width the receiver uses you can calculate the theoretical MDS.
    MDS for a receiver with a -174 dBm/Hz noise floor if a 400 Hz filter band-width is used.
      10 log (400 Hz) = 26 db
      -174 dBm + 26 db = -148 dBm

## Slide 42: Receiver Performance Sensitivity and Noise
<number>
Noise Floor and Signal-to-Noise ratio
  Noise figure is a “figure of merit” for the receiver.
    Ratio in dB of the noise generated by the receiver itself to the theoretical MDS.
    The higher the noise figure the more noise generated within the receiver.
    Higher noise floor.
    Lower noise figures are more desirable
      Low-noise UHF preamp might have a noise figure of 2dB.

## Slide 43: Receiver Performance Sensitivity and Noise
<number>
  Receiver’s internal noise degrades the noise floor, or raises the power that actual signals must have to be heard.
  You can calculate the actual noise floor.
    Actual Noise Floor = Theoretical MDS + noise figure
  Noise figure of a receiver is related to signal-to-noise ratio (SNR) or the input and output signals.
  Lowering a receiver’s noise figure lowers it noise floor and improves weak signal sensitivity.
  Another type of signal to noise ratio is signal-to-noise-and-distortion (SINAD).

## Slide 44: Receiver Performance Selectivity
<number>
The perfect receiver can tune any frequency and reject every signal except the one you want to receive.
Selectivity
  The ability to select a specific signal.
  Selectivity determined by bandwidth the receiver’s entire filter chain from front end to audio output.
  Superheterodyne receivers have several filters in the signal path.

## Slide 45: Receiver Performance Selectivity
<number>
Band-pass front end filters
  Provide front end selectivity
  Reject strong near out of band signals
Preselector
  Tunable input filter that passes the desired frequency.
  Increases rejection of out of band signals.
Band pass filters and preselectors both are effective in eliminating image signal interference.
IF amplifier filters.
  LC, quartz crystal, ceramic resonator.
  Reject unwanted mixing products and prevent spurious signals from slipping into the signal path.

## Slide 46: Receiver Performance Selectivity
<number>
Increasing a superheterodyne receiver’s IF frequency improves selectivity. As the IF is increased the frequency at which image responses occur becomes farther from the desired signal and easier to filter out.
Example:
  IF of 455Khz. Signal on 14.300 MHz
  BFO tuned to 14.3 + .455 = 14.755 MHz
  Image on 15.210 received because 15.210 – 14.755 MHz = 0.455 MHz.
  If we raise the IF to 9 MHz, BFO is 14.3 + 9 = 23.3 MHz and the image frequency would be 23.3 + 9 MHz. Farther away from the desired signal and easier to filter.

## Slide 47: Receiver Performance Selectivity
<number>
At the input to each IF stage a roofing filter is often used.
  Usually crystal filters.
  Bandwidth wider than the widest signal to be received.
  Attenuates strong signals near the receive frequency.

## Slide 48: Receiver Performance Selectivity
<number>
In the final IF, narrow filters used to select on signal from the many that may be present.
  Crystal (most common)
  Mechanical
  Filter must be appropriate for the desired signal.
    Examples: RTTY 300 Hz, SSB, 2.4 KHz
  Narrower filters improve selectivity but limit fidelity and the ability to detect nearby signals.
  Wider filters are more comfortable to listen to but allow undesired signals on nearby frequencies to be heard as well.

## Slide 49: Receiver Performance Dynamic Range and Intermodulation
<number>
Dynamic Range
  The ability of a receiver to tolerate strong signals outside of the normal passband.
  The ratio between the MDS and the largest input signal that does not cause audible distortion products.
  Dynamic range measurements are in dB.
Blocking Dynamic Range (BDR)
  A strong input signal can cause the receiver to no longer respond linearly and gain to drop.
  Causes weaker signals to appear to fade
  Gain compression or blocking.

## Slide 50: Receiver Performance Dynamic Range and Intermodulation
<number>
  Blocking may be observed as desensitization or desense…the reduction in apparent strength of a desired signal caused by a nearby strong interfering signal.
  Blocking Dynamic Range (BDR) is the difference in dB between the noise floor and the level of an incoming signal which will cause 1 dB of gain compression.
  It may be possible to reduce the desensitization by using IF filters to reduce the receiver’s RF bandwidth and reject the strong signals.

## Slide 51: Receiver Performance Dynamic Range and Intermodulation
<number>
Intermodulation (IMD)
  A perfectly linear receiver will produce an output signal with a strength that changes exactly the same as the input signal. This is called first order response.
  As the signal strength increases the receiver’s response becomes nonlinear and IMD products are created.

## Slide 52: Receiver Performance Dynamic Range and Intermodulation
<number>
  IMD products are created at frequencies which are the sum and differences of the input signals and their harmonics.
  The frequencies of second-order IMD products caused by signals that are close together are far from the frequency of either input signal and are generally not a problem if caused by signals within an amateur band.

## Slide 53: Receiver Performance Dynamic Range and Intermodulation
<number>
  If the signals causing the IMD products are close together, such as in the same amateur band as the desired signal, the subtractive IMD products could be very close to the desired signal.
    Third Order IMD Product Frequencies
    fIMD1 = 2f1 + f2
    fIMD2 = 2f1 - f2
    fIMD3 = 2f2 + f1
    fIMD4 = 2f2 - f1
  Third-Order IMD performance of a receiver is an important specification.

## Slide 54: Receiver Performance Dynamic Range and Intermodulation
<number>
  Example
    What are the likely frequencies for a second strong signal that could combine with the one on 146.52 MHz to produce the IMD product you hear on 147.70 MHz ?
    fIMD2 = 2f1 - f2
    f2 = 2f1 - fIMD2
    f2 = 2 x 146.52 – 147.70
    f2 = 146.34 MHz
    fIMD4 = 2f2 - f1
    f1 = (fIMD2 + f2) / 2
    f1 = (146.70 + 146.52) / 2
    f1 = 146.61 MHz

## Slide 55: Receiver Performance Dynamic Range and Intermodulation
<number>
  It may not be practical to filter out strong input signals because they are in-band signals.
    Possible remedies
      Use a receiver with higher dynamic range.
      Use an attenuator at the signal input.
      Reduce RF gain
      Use a roofing filter.

## Slide 56: Receiver Performance Dynamic Range and Intermodulation
<number>
  Intercept Point
    The input signal power at which the level of the distortion products equals the output level for the desired signal is the receiver’s intercept point.
      Example
        A 40 dBm third-order intercept point means the a pair of 40 dBm signals would produce and IMD product of same 40 dBm level.

## Slide 57: Receiver Performance Dynamic Range and Intermodulation
<number>
Intermodulation distortion dynamic range measures the ability of the receiver to avoid generating IMD products. When input signal levels exceed the IMD dynamic range, IMD products will begin to appear along with the desired signal.
If a receiver has poor dynamic range, cross modulation or IMD products will be generated and desensitization (blocking) from strong adjacent signals will occur.

## Slide 58: Receiver Performance Phase Noise
<number>
Phase noise has become more apparent as receiver improvements have reduced the noise floor and increased dynamic range.
Caused by PLL or DDS synthesizers continually adjusting their frequency as compared to a reference.
Excessive phase noise in a receiver local oscillator allows strong signals on nearby frequencies to interfere with the reception of a weak desired signal.

## Slide 59: Receiver Performance Capture Effect
<number>
FM receivers exhibit an effect know as capture effect. The loudest signal received even if it is only a few dB stronger than the other signals on the same frequency will be the only signal demodulated, blocking all weaker signals.
  Can be an advantage if you are trying to receive a strong station and there are weaker stations on the same frequency.