## Slide 1: Chapter 10 Topics in Radio Propagation
Rick, WØPC

## Slide 2: HF Propagation
HF signals make their journey between stations by either traveling along the Earth’s surface (ground-wave) or by returning to Earth after encountering the layers in the upper ionosphere (sky-wave or skip)

## Slide 3: Ground-Wave Propagation
The direction of radio wave can be changed by both diffraction and refraction.
Diffraction – is created by the construction and reinforcement of wavefronts after the radio wave encounters a reflection surface’s corners or edges
Refraction is a gradual bending of the wave because of changes in the velocity of propagation in the medium through which the waves travels.

## Slide 4: Ground-Wave Propagation
Diffraction with Vertical HF Antennas
  The lower part of the radio wave losing energy because of currents induced in the ground
  This slows the lower portion of the wave causing the wave to tilt forward slightly, following the curvature of the Earth
  Tilting results in Ground-Wave propagation allowing low-frequency signals to be heard well beyond line of sight (160 & 80 meter band)
  Ground-wave propagation is lossy because the vertically polarized portion of the wave’s electric field that extends into the ground is mostly absorbed
  Loss increases with frequency (28 MHz = only a few miles)
  Ground-wave is most useful during the daytime

## Slide 5: Sky-Wave Propagation
Signals that travel into the ionosphere can be refracted (bent) by ionized gas in the ionosphere’s E & F region, returning to Earth some distance away.
Refraction occurs because the region of ionized gases causes the radio wave to slow down which bends the wave.
Refraction or Sky-wave is the primary HF mode of propagation
  One hop skip distance for the F-layer is 2500 miles
  One hop skip distance for the E-layer is 1500 miles

## Slide 6: Sky-wave
Absorption: D-layer (35-60 miles above Earth) is a relatively dense region where ionized atoms are closer together and recombine quickly
A great deal of the radio wave energy is dissipated as heat called Ionospheric absorption in the 1.8 to 3.5 MHz bands during the daytime

## Slide 7: Sky-Wave
Long-Path & Gray-Line Propagation
  The circumference if the Earth is 25,000 miles, short path would be less than 12,500
  Long-path distance would be 25,000 minus the short path distance
    Tokyo to Pittsburg is 6619 miles at 328 degrees, long-path would be 18,381 miles bearing 148 degrees
If you notice an echo on the signal, turn you beam 180 degrees for long-path

## Slide 8: Sky-Wave
20-meters is the most common band to experience Long-path propagation
For paths of 6,000 miles or less, the short path usually is best
Long-path is usually observed either along the gray-line (the terminator between light and darkness) or over the nighttime side of the Earth
Gray-line propagation can be quite effective because the D-layer disappears rapidly at night (160-30 meters)

## Slide 9: VHF/UHF/Microwave Propagation
For space wave signals that travel essentially in a straight line between the transmitter and the receiver, antennas that are low-angle radiators (concentrate signals toward the horizon) are the best
Radiation angle decreases as horizontally polarized Yagi antennas are raised above the ground
Transmitting and Receiving antennas should be in the same polarization (20dB loss cross-polarized)

## Slide 10: VHF/UHF/Microwave Propagation
Radio Horizon – VHF radio waves are bent or scattered in several ways, making communications possible with station beyond the visual or geometric horizon. (plus 15%)
The farthest point to which radio waves will travel directly, via space-wave propagation, is called the radio horizon

## Slide 11: VHF/UHF/Microwave Propagation
Multipath: Several components of the same transmitted signal may arrive at the receiving antenna from different directions.
  Phase relationship between multiple signals may cause them to cancel or reinforce each other.
  “Picket Fencing” is a a common example

## Slide 12: Tropospheric Propagation
VHF Big Gun station with high power and big antenna arrays are usually limited to 500 miles
Weather conditions that create a sharp transition between air layers (ducts) in the troposphere can allow VHF radio waves to follow the curvature of the Earth for hundreds or thousands of miles like a wave guide.
  Tropospheric Ducting Forecast “Hepburn Report”
  (http://www.dxinfocentre.com/tropo_eur.html)

## Slide 13: Transequatorial Propagation (TE)
TE is a form of F-layer ionospheric propagation
TE occurs between mid-latitude station approximately the same distance north and south of the Earth’s magnetic equator (2,500 north and south of the equator)
TE occurs on 50, 144 MHz and to some extent 432 MHz
The high-density-ionization regions from approximately between 10 and 15 degrees on either side of the Earth’s magnetic equator
Best time to look for them is March 21 & Sept 21

## Slide 14: Auroral Propagation
Auroral borealis is caused by the collision of solar-wind particles with oxygen and nitrogen molecules in the upper atmosphere.
  These collisions partially ionize the molecules by knocking loose some of their outer electrons
VHF radio waves are reflected from the ionization created by an auroral curtain
VHF/UHF propagation up to 1,400 miles
Generally, auroral propagation is available only to stations in the northern states

## Slide 15: Meteor Scatter Communications
Radio waves can be reflected by the ionized trail of a meteor (level of the E-layer, 50-75 miles)
The ability of a meteor trail to reflect radio signals depends on the electron density
The best frequency range is between 28 and 148 MHz
Meteor-scatter communication is best between midnight and noon
Meteor Showers – are predictable (Perseids in August, Geminids in December)
FSK441 part of the WSJT software suite, HSCW 800 to 2,000 WPM.

## Slide 16: Earth-Moon-Earth Communications
Stations that can simultaneously see the Moon communicate by reflecting VHF or UHF signals off the lunar surface (Mutual Lunar Window)
Stations maybe separated by nearly 12,000 miles
Low-noise receiving setup is essential for successful EME work since most of the signal is close to or in the noise