## Slide 1: Chapter 11 Safety
Gordon, AH6DA

## Slide 2: Safety
Three Hazardous materials:
  PCBs (polychlorinated biphenyls) insulating oil used in electronic gear. (Transformers, High voltage capacitors, dummy loads, old equipment like amplifiers, etc)
  Beryllium & Beryllium Oxide – used in copper alloys to stiffen it, Spring Contacts, duplexer fingers
  Lead & Soldering – Solder is a mixture of lead and tin that is only dangerous when ingested or absorbed in the body
  Carbon Monoxide – from generators or heating equipment during portable emergency operations

## Slide 3: RF Exposure
Low level RF exposure in harmless
RF exposure is dangerous when levels are high enough to affect body temperature
RF radiation is non-ionizing, it does not have sufficient energy to break apart atoms and molecules

## Slide 4: RF Exposure
Power Density – Is the intensity of the RF energy expressed in milliwatts per square centimeter
  Increasing power levels increases power density
  Increasing distance from an antenna lowers power density

## Slide 5: RF Exposure
Absorption & Limits
  The rate which energy is absorbed from the power to which the body is exposed is called the (SAR) Specific Absorption Rate.
  SAR depends on the frequency, power density, average amount of exposure and the duty cycle of the transmission
  Safe levels of SAR have been established by the FCC for amateurs in the form of “Maximum Permissible Exposure” (MPE)

## Slide 6: RF Exposure
Averaging & Duty Cycle
  Exposure to RF energy is averaged over fixed time intervals because the response of the body to heating is different for short duration and long duration exposures.
  People in a Controlled environment are considered aware of their exposure and take precautions (power density limits are higher, averaging period is 6 minutes)
  People in Uncontrolled environments are unaware of their exposure (the averaging period is longer, 30 minutes)

## Slide 7
The lower the transmission duty cycle (the less the transmitter is transmitting), the lower the average exposure.
Check Table 11-2 on page 11-5 for more details
Duty Cycle

## Slide 8
You can perform the evaluation by actually measuring the RF field strength with calibrated field strength meters and calibrated antennas.
You can also use computer modeling to determine the exposure levels.
http://hintlink.com/power_density.htm
Estimating Exposure and Station Evaluation

## Slide 10: The End, Almost
Time to review using practice tests online and from the CD included with the course.
If you are consistently passing with an 85% or better on multiple practice tests, you are ready for the real thing.
Next week is the VE Test Session
  Bring your original license and a copy to leave
  Bring photo ID and $15.00 CASH